Solutions to the Exercises

of

Hydrology

An Introduction

(Wilfried Brutsaert)

CAMBRIDGE

UNIVERSITY PRESS

Caution:  These solutions have been obtained in one pass, and have not been double-checked.

Chapter 1

1.1   When all precipitation enters into the soil surface, the flux through the soil storage system is 0.8 m y-1. Soil storage amounts to 0.05 m.   Hence the residence time is 0.05/0.8 = 0.0625 y = 23 days. When the flux is only 0.4 m y-1, the residence time is 46 days.

1.2   An energy flux in equivalent mm y-1 of evaporation is (3600*24*365*10-6/2.5) = 12.6 times that flux expressed in W m-2.  Hence for net radiation this is 1,312 mm/y, for evaporation 1,009 mm/y, and for sensible (turbulent) heat flux 240 mm/y.

Chapter 2

2.1     b, d

2.2       c, d, e

  - Because , the answer is m.

Similarly, , so that m.

2.4   Because , one obtains  m.

Similarly, , so that  m.

2.5   Using the same approach as in the previous problem one obtains  m and  m.

2.6

2.7           0.00145 cm

2.8    (a)

(b)    1.26 10-3

(c)

2.9

2.10   Several combinations of  are possible.  Two possibilities are as follows.  If , then

If  , then

, in which .

2.11

(a)  For the average air temperature, and an assumed pressure of 101325 Pa, the density of the air is 1.16 kg/m3.  The calculations of  are carried out with (2.50) and (2.51) [or (2.54) and (2.55)], in which the -functions are given by (2.63) and (2.64), as follows. An initial calculation of  for assumed neutral conditions, i.e. with , yields  0.2265 m/s; with this value and with , one obtains an initial estimate of the heat flux H = 64.01 W/m2.  This produces the first estimate of the Obukhov length by means of (2.46), namely L = -16.44 m.  This value of L can now be used to obtain new estimates of , from which an improved value of L is obtained, and so on. The process converges rapidly.  After 9 iterations the results stabilize at  0.2434 m/s, H = 121.8 W/m2, and L = -10.73 m.

(b)  392 – 122 = 270 W/m2.  Hence 288 mm/mo (of liquid water).

2.12   (a)   1.1374 m/s;  m/s and  m/s.

(b)   if the pressure is assumed to be 1013 hPa at 2 m above the surface, the density of the air is  1.225 kg/ m3, and the specific humidity is ; hence at 800 m above the surface it is calculated to be .

2.13

2.14   (a)   From (2.77) for  one has always and everywhere  or .

(b)   At sunrise and sunset ; when the day length is 12 h or , one also has . This is the case when , i.e. on the equator (always), and when , i.e. at the time of the equinoxes (everywhere).

2.15

from which (2.78) follows immediately.

2.16   On June 21 the declination is  and .  Thus (2.78) with  yields the result  or 977 cal cm-2d-1 = 473 W m-2; this is roughly the same as shown in Figure 2.23.

2.17   For a vibrant short vegetation assume an albedo , and a surface emissivity .  The incoming short-wave radiation is = 226.79 W/m2, and the net short-wave radiation is  W/m2.  The air temperature is  K, and with (2.14) the vapor pressure in the air is hPa; hence with (2.81) the atmospheric emissivity is , and with (2.80) this gives a downward long-wave radiation W/m2.  With the surface temperature assumed to be the same as the air temperature, (2.79) yields an upward long-wave radiation  W/m2.  The net radiation is obtained with (2.73), namely  W/m2.

2.18   For a vibrant short vegetation assume an albedo , and a surface emissivity .  The incoming short-wave radiation is = 231.15 W/m2, and the net short-wave radiation is  W/m2.  The air temperature is  K, and with (2.14) the vapor pressure in the air is  hPa; hence with (2.81) the atmospheric emissivity is , and with (2.80) this gives a downward long-wave radiation W/m2.  With the surface temperature assumed to be the same as the air temperature, (2.79) yields an upward long-wave radiation  W/m2.  The net radiation is obtained with (2.73), namely  W/m2.

2.19   For a deep water body assume an albedo , and a surface emissivity .  Consider first the month of December.  Figure 2.23 indicates that the daily extraterrestrial radiation is roughly  W/m2.  With (2.74) this yields a daily short-wave radiation at ground level of  W/m2 and a value of net short-wave radiation of  W/m2.  The air temperature is  K, and with (2.14) the vapor pressure in the air is  hPa; hence with (2.81) the atmospheric emissivity is , and with (2.80) this gives a downward long-wave radiation W/m2.  The surface temperature is  K; thus (2.79) yields an upward long-wave radiation  W/m2.  The daily net radiation is obtained with (2.73), in which  is used instead of ; the result is  W/m2.

For the month of July the corresponding values are as follows.  W/m2;   W/m2 ;  W/m2.   K;   hPa; ;  W/m2.   K;  W/m2.  Finally,  W/m2.

2.20   Because the temperature of the air equals that of the snow cover, the lower atmosphere is neutral, so that .  Thus the maximal rate of evaporation would occur when all the incoming radiation is converted to evaporation and to outgoing radiation (and does not contribute to warming the snow).  Accordingly, under steady conditions at night, (2.72) with (2.73) can be written for a snow surface as  or , in which  is the latent heat of sublimation; this yields  W/m2, or  mm/d.

2.21   The literature review behind (2.87) indicates that typical values of  are around 0.37 and 0.5, respectively.  For cropland Table 2.9 gives a mean value of the leaf area index , with which (2.87) yields .  For grassland the table shows a mean value ; this produces with (2.87) the result .

2.22    The earth, as “seen” by the sun, is a circle with area , in which R is the earth’s radius.  On the other hand the earth as a sphere, has a total area equal to .  Hence the area intercepting the solar radiation is one quarter the total area of the earth.

-

Chapter 3

3.1

3.2   Recall that n is the number of stations and m is the number of subareas.  When b=0, one has

where  is the arithmetic mean of P.  Hence, (3.2) becomes

3.3   The rainfall at station m (the one with a malfunctioning gage or without a gage), which is surrounded by (n-1) functioning gage, can be estimated by means of

3.4   Typical values are ; for  one can assume .  With  in (3.3) one obtains .

3.5

.

3.6  Several estimates can be made.  Table 3.2 suggests a value between 401 and 440 mm; but these are just two isolated maxima.  If all other observed maxima are considered, which suggest a power-type function, Figure 3.17 indicates PD = 500 mm, approximately.  Similarly, from Equation (3.5) one obtains   506 mm.

3.7   Assume that the deficiency in Fig. 3.21 is the same as the percent difference in Fig. 3.22 divided by 100.  Inspection of the two figures indicates that typical rainfall intensities of curve 1 in Fig. 3.21 must have been in the range of roughly 1 to 1.5 mm/h.

-

Chapter 4

4.1   According to (4.3) one has .  Substitution of  from (2.41) and  from (2.44) yields immediately (4.4).

4.2   With a surface roughness of 0.01 m and a wind speed of 5 m/s at 2 m above the ground surface, (2.41) produces a friction velocity equal to  m/s.  This in turn produces with (2.41) a wind speed at 10 m equal to .

The rate of evaporation is given as E = 4 kg m-2 d-1 = 4/(3600*24) kg m-2 s-1.  Assuming an atmospheric pressure of about 1000 hPa, one obtains from Table 2.4, with (4.6) and a relative humidity of 60 % and a temperature of 20oC, the value of the specific humidity at 2 m, namely .  At T = 293.16 K and p = 105 Pa, the density of air is close to 1.188 kg/m3.  Substitution of these values of  into (2.43) yields the specific humidity at 10 m, namely .

4.3   Assume equality of the scalar roughness lengths , and of the stability correction functions ; also, assume that the actual and potential temperature differences are equal, i.e. .  Under neutral conditions the derivation is simple: eliminating the term  between (2.44) and its analog for temperature, one obtains the desired result.  In SI units a mass flux is normally given in kg/(m2s).  Because here the rate of evaporation E is given in mm/d and the density of liquid water is around 1000 kg/m3, the final result is

in units of W m-2.    Under non-neutral conditions, eliminate the term  between (2.55) and (2.56)] to obtain the same expression.

4.4   The specific humidity which is defined in (2.2) can be expressed as the ratio of (2.5) and (2.4); this produces .  The vapor pressure is normally several orders of magnitude smaller than the pressure of the air, and it can therefore usually be neglected in the denominator.

4.5   First equate (4.3) and (4.7); this produces .  Substitution of (4.4) for Ce, of (4.6) for q, and finally of (2.7) (with neglect of q, which is much smaller than one) for , yields the desired result (4.28).

4.6   b, c, d.

4.7   a, b, c, d, e.

4.8   Consider (4.28) with (4.25) to obtain the scalar roughness length explicitly as follows

Note that the factor  is needed to convert the units of (4.25) from  to .  This expression can be solved for , , , and , to yield 1.118 10-6 m.  If the constant of Doorenbos and Pruitt is used, i.e. 0.86 instead of 0.54, one obtains 0.863 10-4 m.

4.9   At 25oC the latent heat of evaporation is 2.442 106 J kg-1.  Thus an energy supply rate of 1 J m-2s-1 is capable of evaporating (2.442 106)-1kg m-2s-1; this is equivalent with             (3600*24*30*10-6/2.442) =  1.06 kg m-2month-1.  Because the density of liquid water is around 1000 kg m-3, this is 1.06 mm/month.

4.10   (a)   The evaporation rate was  E = 5*10-8 m/s =  5*10-5 mm/s = 5*10-5 kg/(m2 s).  Assume that on average the latent heat of evaporation is .  This gives a latent heat flux .  Thus according to (4.13) with the assumption that , one can write H = 200-40-122.5 = 37.7 W/m2.

(b)   The Bowen ratio was

(c)   The atmosphere was unstable because , which means that the sensible heat flux was upward, and .

(d)   The ground was warming because , that is the heat flux into the ground was positive.

4.11   (a)   According to (4.13) with the assumption that , one can write .  If it can be further assumed that on average the latent heat of evaporation is , one obtains an evaporation rate .  Because the density of liquid water is around , units of kg/m2 are equivalent with units of mm.

Therefore the rate of evaporation can also be expressed as .

(b)   The Bowen ratio was

(c)   The atmosphere was unstable because , which means that the sensible heat flux was upward, and .

(d)   The ground was warming because , that is the heat flux into the ground was positive.

4.12   According to the calculations for Problem 2.17, for that summer day the air temperature was  K, and with (2.14) the saturation vapor pressure in the air was  hPa, and the actual vapor pressure in the air was hPa.

The average net radiation was calculated as  W/m2.  This is equivalent with 3.586 mm/d.

At this air temperature Figure 4.2 indicates that roughly .  In the absence of a more detailed table, the values listed in Table 4.1 can be interpolated by means of standard formula’s such as, for example, Stirling’s or Bessel’s; with Bessel’s formula retaining second differences for  one obtains a value .

The wind speed is given as 10.4 km/h at 10 m above the ground.  Equation (4.25) requires the mean wind speed in m/s at 2 m above the surface.  To a first approximation in the present application, one can use (4.26), so that the required wind speed is  m/s.

(a) With these values Penman’s (4.23) with (4.24) and (4.25) yields an evaporation rate  3.749 mm/d.

(b)  Equation (4.31) of Priestley & Taylor produces  3.020 mm/d.

(c)   Equilibrium evaporation (4.30) yields  2.378 mm/d.

(d)   Equation (4.48) of Brutsaert & Stricker’s advection aridity approach produces 2.292 mm/d.

4.13   According to the calculations for Problem 2.18, for that summer day the air temperature was  K, and with (2.14) the saturation vapor pressure in the air was  hPa, and the actual vapor pressure in the air was hPa.

The average net radiation was calculated as  W/m2.  This is equivalent with 3.808 mm/d.

At this air temperature Figure 4.2 indicates that roughly .  The values listed in Table 4.1 can be interpolated by means of Bessel’s formula; retaining second differences for  one obtains a value .

The wind speed is given as 8.96 km/h at 10 m above the ground.  Equation (4.25) requires the mean wind speed in m/s at 2 m above the surface.  To a first approximation in the present application, one can use (4.26), so that the required wind speed is  m/s.

(a) With these values Penman’s (4.23) with (4.24) and (4.25) yields an evaporation rate  4.067 mm/d.

(b)  Equation (4.31) of Priestley & Taylor produces  3.349 mm/d.

(c)   Equilibrium evaporation (4.30) yields  2.637 mm/d.

(d)   Equation (4.48) of Brutsaert & Stricker’s advection aridity approach produces 2.631 mm/d.

4.14   The equilibrium evaporation as defined in (4.30) implies a Bowen ratio .  As shown in Table 4.1, at a temperature of 25oC its magnitude is 0.3505

4.15   a, c, d, e

4.16   Consider first the month of December.

(a)   The air temperature is  and the water surface temperature is .  Assume  and .  The saturation vapor pressure at the water surface temperature is .  Hence, the Bowen ratio is =1.020.  The available energy flux is  = 4.313 mm/d.  Thus with (4.16) this yields a rate of evaporation , or = 2.135 mm/d.

(b) To determine , the values listed in Table 4.1 can be interpolated by means of Bessel’s formula;  for  one obtains a value .

The wind speed is given as 15.3 km/h at 10 m above the ground.  Equation (4.25) requires the mean wind speed in m/s at 2 m above the surface.  To a first approximation in the present application, one can use (4.26), so that the required wind speed is  m/s.

With the given values, Penman’s (4.23) with (4.24) and (4.25) yields an evaporation rate  2.14 mm/d; Priestley and Taylor’s (4.31) with =1.27 yields  2.01 mm/d.

For the month of July the corresponding values are as follows.

(a)   The temperatures are  and .  Assume  and ; from (2.14) one obtains ;

=-0.1327;  =

-0.446 mm/d; with (4.16) , or = -0.514 mm/d.

(b) To determine , the values listed in Table 4.1 can be interpolated by means of Bessel’s formula;  for  one obtains a value .

The wind speed is 10.1 km/h at 10 m, so that  m/s.

Hence from (4.23)  1.22 mm/d, according to Penman, and -0.393 mm/d according to Priestley and Taylor.

4.17   Equation (4.3) can be applied directly with the available data.

(a)  Consider first the month of December.

The air temperature is  and the relative humidity is 0.76; with (2.14) the vapor pressure in the air is  hPa.  The water surface temperature is , and the corresponding saturation vapor pressure at this temperature is   Assuming in (4.6), one obtains the respective specific humidities  and .  At the given air temperature and an assumed pressure of 105 Pa, (2.4) shows the air density to be close to  kg/m3.  At 10 m the wind speed is = 15.3 km/h = 4.25 m/s.  Thus (4.3) produces =1.991 mm/d.

For the month of July the air temperature is  K and the vapor pressure is  hPa;  so that .  With , one obtains  and .  At the given air temperature and an assumed pressure of 105 Pa, (2.4) shows the air density to be close to  kg/m3.  At 10 m the wind speed is = 10.1 km/h = 2.81 m/s.  Thus (4.3) produces =1.449 mm/d.

(b)  For the month of December the atmosphere was unstable; therefore a larger value of Ce should be used.  In July the air was stable; therefore a smaller value of Ce should be used.  This is illustrated by comparing the results of this exercise with the energy budget results of exercise 4.16.

4.18   Equation (4.3) can be used to estimate potential evaporation, that is evaporation from a moist surface, as follows

in which  is the saturation specific humidity at the temperature of the moist surface.  The actual evaporation from a non-moist surface, formulated in terms of the resistance parameter, is given by (4.38), that is

Hence, , as defined in (4.33), becomes

4.19   A longitude of 96o31’ is equivalent with a time difference of (96+31/60)*24/360 = 6.434 h. Therefore, local (solar) time at that location is 6.434 h behind UTC, or 1.434 h = 1 h and 26 min behind CDT.  This means that solar noon occurs at 1:26 pm or 1326 CDT.

4.20   The three required equations are

and (2.50) and (2.51); in the latter two  and the functions  are given by (2.63) and (2.64), respectively.  The system can be solved by iteration; the initial estimates of  are obtained by assuming the initial values of  to be zero.

Chapter 5

5.1   In this case [(unlike (1.13)], the z-axis is not vertical but normal to the bed, which has a slope angle  with the horizontal.  Thus the x-component (parallel with the bed) of (1.12) can be written as

(1)

If there is also a local source flow , this is accelerated instantaneously from 0 to the velocity u of the ambient fluid; this represents a rate of change in momentum (per unit mass) in the x-direction equal to , which must be included in the equation.

The flow is turbulent and therefore the dependent variables are conveniently decomposed into a mean and a turbulent fluctuation as follows: , [in which  and ], , and .

Equation (1) becomes in terms of the decomposed variables

(2)

Apply now the time-averaging operation, represented by the overbar symbol, i.e.  to each of the terms in (2).  Recalling that the mean of a mean remains the mean, and that the mean of a turbulent fluctuation is zero, and also noting that the averaging operation is independent of the partial derivative operations (in the case of the time derivative the reason is that the time scales of both operations are totally different), one finally obtains

(3)

The equation of continuity (1.9) is equally applicable to the mean and to the turbulent velocity fluctuations.  After multiplying the equation of continuity for the velocity fluctuations by , and subsequently applying the averaging operation to this product, one obtains the following zero magnitude quantity

(4)

Because it is zero, it can be simply subtracted from the right hand side of (3) without affecting it.  Thus one finally obtains

(5)

For two-dimensional flow, one can omit the mean flow in the y-direction and also gradients of mean quantities in the y-direction,  i.e.  , and , so that (5) becomes

which is the desired result (5.14)

5.2    With (5.30), i.e. , one can rewrite (2.41) [or (5.34)] as

(1)

The logarithmic velocity distribution is applicable between , where , and between , where .  Substituting (1) with these limits in (5.8), one obtains the average velocity

or

This becomes finally,

which reduces to (5.35) when .

5.3   Note again that the logarithmic velocity distribution is applicable between , where , and between , where .  Assume, as is done in (5.36), for simplicity that .  With (5.34) and (5.36) and substitution of (5.30), i.e. , the Boussinesq correction (5.19) can then be written as

Upon integration this is

or

This can be simplified to

which is the desired result.  It shows that the correction factor  approaches unity as the depth  increases.   For instance for , one has ; for  it decreases to .

5.4   In contrast to the logarithmic velocity distribution, the power-type velocity distribution function (5.37) is applicable between , where , and between , where .  With (5.37) and (5.38) and substitution of (5.30), i.e. , the Boussinesq correction (5.19) can then be written as

This correction factor approaches unity when m becomes smaller, that is when the turbulent mixing becomes more intense, so that the velocity profile becomes more uniform.  For instance as 1/6, this result yields 1.021, and for 1/10, one has 1.0083.

5.5   For a triangular cross section:

For a rectangular cross section:

5.6   From inspection of (5.38), it can be seen that the values of the powers in (5.43) would be  and .

5.7   For the given geometry of the channel, the water surface width is .  The cross sectional area of the channel is  .  The hydraulic radius is .  According to (5.41) the velocity is V = 2.4994 m/s, and the rate of flow .  For an assumed water temperature of 10oC the viscosity is  , and the resulting Reynolds number is Re = 2.46 106.

5.8   The channel has the same characteristics as in the previous problem.  Thus the values of  are kept constant and the side banks have a slope of 1 vertical and 2 horizontal.  Adopt a trial value of h and proceed to calculate a first value of Q as in the previous problem.  Adjust the value of h and calculate a new value of Q.  Continue this process until Q = 60 m3/s is obtained.  The calculations can be easily carried out on spreadsheet, or by using standard interpolation procedures.  The solution is .

5.9   Equating (5.34) [in terms of the roughness  as in (2.41)] with (5.36), one can write , or .  From this it follows that the average velocity occurs at the depth where ; this is close to the ratio 0.40, which is commonly used in stream gauging practice.

5.10   Equating (5.37) with (5.38), one can write  ; thus the ratio depends on m.  For example, for m = 1/6, one has z/h = 0.397 , for m = 1/7, one has z/h = 0.393; this illustrates that the ratio decreases with decreasing m.  It is of interest to note that, by putting , one can also write the ratio as , which in the limit, as , approaches  exp(-1) = 0.368; this is the same value as that obtained in the previous exercise with the logarithmic profile.  Again, all these values are close to the ratio 0.4, which is commonly used in stream gauging practice.

5.11   When the velocity profile is logarithmic, the true mean velocity is given by (5.36), that is

This is approximated by the average of the measurements at the 2 depths, or using (5.34) [in the form of (2.41)],

Thus the error is

The error depends on the relative roughness of the river bed , and it decreases with decreasing roughness.  For example, for , the respective errors are .  Evidently, this practice is quite accurate, at least when compared to all the other errors incurred in stream flow measurements, such as due to uncertainty in the bed geometry or current meter functioning and calibration.

5.12   For conciseness of notation put  and , so that (5.51) can be rewritten as .  Then, by successive differentiations it follows that

and

(1)

In a similar way one has

and

(2)

Substitution of (1) and (2) into (5.49) shows that (5.51) satisfies this differential equation, and is therefore a solution.

5.13   From the definition of  in (5.83) one has

Therefore, the second term on the left of (5.87) can be transformed as follows

But from (5.93) and (5.43) [i.e. (5.39) for a wide channel, with an effective width ] it is also known that ; since the width of the channel  is a constant, the advectivity becomes

or, upon retaining only the uniform steady part, .  This is the same as , if one uses the uniform steady flow rate  and the cross sectional area for the wide channel is given by .

5.14   The second term on the left of this diffusion equation is known as the advectivity and it represents , the speed of propagation (or celerity) of the bulk of the flood wave [cf. (5.91) and (5.94)].

(a)  According to the Kleitz-Seddon principle (5.108) with (5.43), the mean velocity is   . In the case of the GM equation this yields  m/s, and in the case of the Chezy equation m/s.

(b)   From (5.91) and (5.94) (dropping the zero subscripts) or from (5.112) one has to a good approximation   and

From (5.43) one has , and since  and , this yields .

(c)  The magnitude of the coefficient 2.17 indicates that the flood wave is traveling at that celerity (in this case in m/s); it indicates the rate of translation of the centroid of the wave in the downstream direction.  The magnitude of the coefficient 1365, which is a diffusivity, is related to the rate of spreading (or flattening) of the flood wave with time (and traveled distance downstream); the larger it is, the faster the wave diffuses out and attenuates.

5.15  (a) Equation (5.39) produces the following rate of flow in the case of a narrow channel .  Because the wetted perimeter  depends on the same geometric parameters as , one obtains with (5.112) .  An infinitesimal increase in cross sectional area can be expressed as .  Hence the celerity becomes , which is in the form of (5.114).

(b) In the case of a triangular cross section, (with a bottom angle  and a maximum depth h as the vertex of the triangle), one has the following relationships:

; ;  ; .  After their substitution in the second term of (5.114), the celerity is ; with the GM equation this is .

5.16    b, d.

-

Chapter 6

6.2   At any distance x on a plane, as shown in Figure 6.1, under steady state conditions the rate of flow (per unit width of plane), resulting from a constant rainfall rate P, is given by .  Since it can be assumed that laminar flow is occurring when the  Reynolds number < 500, the required relationship for the location of the transition is  .

6.3   First establish whether the flow is laminar or turbulent.  At the downstream end of the plane, where the flow rate reaches its maximum, the Reynolds number is

.  For a typical temperature of 10oC, the viscosity is ;  the rainfall rate is .  Thus with , one obtains , which indicates laminar flow conditions.

Laminar flow with rainfall impacting on the surface can be described by (5.33).  The kinematic wave assumption allows .  Under steady conditions the rate of flow is equal to the rainfall on the upstream plane, so that .  Therefore (5.33) transforms to

in which one can use , provided P inside the round brackets is expressed in cm/h, that is 3.7 cm/h; note that the other P  should be expressed in units that are consistent with those of the other variables, in this case .  The result is mm.

6.4   Because the flow is steady but still spatially varied, the only terms that can be omitted are  in (6.1) and  in (6.2).  Thus these equations can be simplified to

and

For flow in a wide channel, according to (5.43) the friction slope is

in which the values of the parameters  are listed in Table 5.2.

6.5   According to (6.10), after the rain ceases so that , to an observer who travels with a celerity  it appears that the water depth remains constant, that is .  Conversely, a point on the water surface with a given (i.e. constant) depth (say ) travels downstream at a celerity .  Hence in the present case, the point in question moves at a celerity

.

6.6   The volume of rain water, which does not run off the plane during the rising of the outflow hydrograph, is held in storage on the plane.  This volume is the input minus the output, and according to (6.21) this volume (per unit width of plane) can be calculated as follows

After substitution of (6.20), that is  in terms of , one obtains

This water, which is stored on the plane, results in the outflow after the rainfall has ceased.  Thus if now  refers to the time when the rainfall stops, this volume is equal to , or which is the same , in which the upper limit is the value of  at the beginning of the recession, when .  According to (6.27) this can be written as

which can readily be integrated to obtain ; this is

the same as the volume obtained during the rising of the hydrograph, as required.

6.7   (a) For a typical temperature of 10oC, the viscosity is ; the rainfall rate is .  Thus with , one obtains at the downstream end of the plane , which indicates laminar flow conditions, and the applicability of (5.33).

(b) The parameter  in the kinematic relationship (6.8) can be obtained from (5.33) as  (with P expressed in cm/h); this yields 3747 without the rain effect, and 1771 with the rain effect.  The time to equilibrium can be obtained with (6.20) and it produces without the rain effect 604.9 s = 0.168 h, and with the rain effect 776.6 s = 0.216 h; at those times the equilibrium flows are reached, namely .  The rising hydrograph  is calculated with (6.21).  In SI units this outflow rate is normally in m2/s, but for convenience it can also be expressed in mm/h by multiplying it by  in which L = 40 m.  For t = 0.05, 0.1, 0.15, 0.168 h, the calculations without rain effect in (5.33) yield respectively  mm/h; for t = 0.05, 0.1, 0.15, 0.2, 0.216 h with the rainfall impact effect respectively  mm/h.

6.8   (a) For a typical temperature of 10oC, the viscosity is ; the rainfall rate is .  Thus with , one obtains at the downstream end of the plane , which indicates turbulent flow conditions, and the applicability of (5.41) with , and .

(b) The parameter  in the kinematic relationship (6.8) can be obtained from (5.41).  Assuming a roughness coefficient , one obtains = 7.071.

The time to equilibrium, obtained with (6.20), is 215.3 s = 0.0598 h; the equilibrium flow is .  The rising hydrograph  is calculated with (6.21).  In SI units this outflow rate is normally in m2/s, but for convenience it can also be expressed in mm/h by multiplying it by  in which L = 45 m.  For t = 0.01, 0.02, 0.03, 0.04, 0.05, 0.0598 h, the calculations yield respectively  mm/h.

6.9   (a) For a typical temperature of 10oC, the viscosity is ; the rainfall rate is .  Thus with , one obtains at the downstream end of the plane , which indicates laminar flow conditions, and the applicability of (5.33), or rather (5.32), because the effect of the rain drop impact need not be considered.

(b) The parameter  in the kinematic relationship (6.8) can be obtained from (5.32) as ; with  this yields 12490.  The recession hydrograph can be calculated with (6.27) as , and yields for  mm/h the following values of the time  h.

(c) By trial and error or interpolation, one finds that after 15 min (= 900 s) the rate of flow is 1.72 mm/h (= 1.24 10-5 m2/s).

6.10   From (6.37) the relative increase equals the ratio .  Equations (6.8) and (5.33) show that this can be calculated as ; with  this indicates that as the rainfall ceases suddenly, the flow rate becomes 2.2 times the equilibrium flow rate .  With  the answer is nearly the same, namely 2.14 times the equilibrium flow rate.

6.11   The average depth can be defined as .  Under steady state conditions, at any point x the rate of flow is ; in the kinematic wave approach q is also related to the flow depth as shown in (6.8), so that , or in differential form .  This allows the determination of the average depth as

in which use is made of the fact that  at .

6.12   c, d, e.

Chapter 7

7.1   As was done in the example, assume that the channel is wide so that .

If it takes 57 minutes to cover 23 km, the required celerity is  m/s.

(a)  With a GM roughness , (5.41) produces m/s.  Trial and error (or interpolation) with (7.7) yields a required depth  m to obtain m/s (that is a travel time of 57 min).

(b) In the same way for , (5.41) produces m/s.  This requires a depth m in (7.7) to obtain the same celerity.

7.2   With a GM roughness , (5.41) produces m/s.  With m2 and m2, (7.8) produces m/s.

7.3   Equation (7.37) can be applied directly.  With  the coefficients are ,  and .  The results appear in the right hand side column.  To get started, the first value of  is assumed to be the same as that of .

| time (h) | Qi | Qe |
| --- | --- | --- |
| (h) | (m3/s) |  |
| 0 | 139 | 139 |
| 1 | 124 | 140 |
| 2 | 220 | 127 |
| 3 | 342 | 170 |
| 4 | 542 | 250 |
| 5 | 805 | 391 |
| 6 | 1271 | 586 |
| 7 | 1684 | 927 |
| 8 | 1973 | 1312 |
| 9 | 2169 | 1651 |
| 10 | 2090 | 1929 |
| 11 | 1895 | 2024 |
| 12 | 1622 | 1970 |
| 13 | 1333 | 1801 |

etc.

7.4   (a) The values of the coefficients, obtained with (7.44), are as follows, , , and .

(b) With (7.45) these yield the Muskingum parameters , and .

(c)  The results can be presented in the same manner as in Figure 7.10.  The calculated values for days 1, 2, 3, etc. are 0, 59, 135, 224, 343, 461, 530, 664, 971, 1288, etc., m3/s.

7.5   (a) By plotting  in the manner shown in Figure 7.9 for different trial values of X, a “satisfactory” overall single-valued relationship can be obtained with .  (The procedure is subjective, but to the eye it seems to be better than with other choices of X, at least in the range of high flows).  The corresponding slope of the regression through the points is .

(b)  The results can be presented in the same manner as in Figure 7.10.  The calculated values for days 1, 2, 3, etc. are 0, 68, 151, 243, 372, 501, 556, 677, 1027, 1389, etc., m3/s.

7.6   (a) In the linear case the design outflow peak is .

(b) In light of (5.41) for a wide channel, (7.57) can be written as .  On account of (5.41) one also has , so that (7.57) becomes .  With the data given in the table of Exercise 7.4, this yields a design value .

For the same reason, (7.58) can be written as , which yields a design value .

7.7   It takes the flood wave  to travel a distance of  35 km.  Hence its celerity is 0.2025 m/s, which is also equal to .  For a peak flow of  at Brooklyn, one finds .

7.8  The coefficient 2.17 in the diffusion equation of Exercise 5.14 represents the celerity of the flood wave in the channel.  Since K represents the time of travel of the wave, for a channel reach of 2.5 km, its value is

7.9   (a) With  and , the Muskingum storage function (7.15) is simply  (in m3h/s).  Substitution in the storage equation (7.35), in which , yields .  This allows the calculations stepping back in time as follows:

, , , etc., all in m3/s.

(b) .

(c) The celerity of the flood wave is to a good approximation given by the kinematic approach (Kleitz-Seddon formula), so that .  The travel time of the wave through the reach is ; hence, the length of the reach is

7.10   (a) The values of the coefficients can be obtained with (7.44), and are as follows, , , and .

(b) With (7.45) these yield the Muskingum parameters , and .

(c) The results can be presented in the same manner as in Figure 7.10.  The calculated values for days 1, 2, 3, etc. are 0, 681, 1936, 4560, 7144, 7328, 5666, etc., m3/s.

7.11   (a) The flow velocity at that point is m/s.  With the Kleitz-Seddon relationship this gives  m/s = 10.3 km/h.

(b) With  and , the Muskingum storage function (7.15) is simply  (in m3h/s).  Substitution in the storage equation (7.35), in which , yields .  By routing the given inflow hydrograph with this equation, on finds a peak outflow rate of 56.8 m3/s.

7.12   For convenience rewrite (7.47)

From (7.38) it follows that

and (7.47) can be rewritten as

After substitution of (7.49), namely

this transforms further into

which directly leads to (7.50).

7.13   In (5.63) the Froude number is defined as .   Thus (7.56) can be rewritten as  .  This expression should be applicable to any flow rate with concurrent variables , that can be used as reference in the linearization.  Let the subscript  refer to values of variables and parameters obtained from the record, and the subscript  refer to those to be used in the design calculations; then, in the example where values of the variables for the peak inflows are used as reference, the ratio of both expressions is

which is essentially (7.59).

7.14     a.

7.15     a, b, e

7.16     c, d

7.17      c, e, f, i

7.18      b, d

-

Chapter 8

8.1   In the case of parallel plates (8.3) requires .  At 18oC the surface tension is approximately .  Since , (8.3) yields the capillary rise , when both  are in m, or  when the variables are in cm.

8.2   (a)

(b)   If the water table were stationary and the profile in equilibrium, the water content would be .  In reality, it is , which is higher than equilibrium.  This means that the water content has not had the time yet to adjust, and the water table is falling.  An alternative explanation is that a water content of , requires a suction of about ; thus the suction (or negative pressure) is smaller than 100 cm, i.e. the pressure is larger than hydrostatic at that height, which implies downward flow.

8.3

8.4

8.5

8.6   (a) In general, the slope angle with the x-axis is .  This yields in the present case .

(b) In general, .  In the present case this is , from which the slope angle with the x-axis is .

(c) .

.

Hence the vector is .

(d) Because both  are negative, .

8.7   (b)  The gradient is orthogonal to the equipotentials, so that .  The direction of the flow makes an angle  with the x-axis.  Hence from (8.30) the result is .

8.8   With (8.15) first obtain the derivative  , and with (8.36) into (8.32), the result (8.14) follows.

8.9   When the variables are in cm, (8.5) is simply .

Then with (8.14) the density function is

With (8.15) the density is

8.10

8.11   From (8.14) one has ; thus with Burdine’s assumption (8.44) becomes .

8.12   From (8.14) one has .  Therefore the integral appearing in (8.48) can be written as , which upon integration becomes .  Substitution in (8.48) yields (8.49).

8.13   At 20oC the surface tension is approximately , the viscosity is , and the density .

(a) Equation (8.49) produces the permeability .

(b) With (8.23) the hydraulic conductivity is .

8.14   Use the last two equations of (8.67) to express  in terms of the other variables in those same two equations; then, substitute the resulting expressions for  into the first three equations of (8.67).

8.15   The first equation of (8.76) is obtained by first operating on (8.74) as indicated in the text, and then replacing the first term on the left by (8.61). Rewrite the first of (8.76) for convenience

(8.76)

The left hand side can be developed as

or, after making use of the continuity equation for the solid (8.63) in the second term,

The first term is kept as it is. The order of spatial and temporal partial derivatives can be inverted; therefore, in the second term use can be made of (8.58), replacing the divergence of the solid displacement by the strain.  The third term cancels the fifth.  The compressibility is usually defined as ; therefore if the finite differences are replaced by partial time derivatives to define , this is no longer the compressibility in the strict sense, but it can still be considered and treated as a parameter related to the fluid compressibility.  Thus assume that the fourth term can be written as .  If the sixth term is neglected, on the grounds that it is the product of small quantities (i.e. derivatives), with all these changes (8.76) converts into

(8.80)

On account of (8.79) the second term can be expressed in terms of the pressure fluctuations in the water and in the air.  This produces immediately the first of (8.82), which is the desired result.

8.16    a, e

8.17    a, e

8.18    d, e

8.19    a, b, d, e

8.20    c

8.21    b, f

-

Chapter 9

9.1   (a) The cumulative infiltration volume can be calculated from (9.63) with , as follows

or, upon integration .  The units are cm.

(b) The rate of infiltration is , or in the present case, with the result in (a),

. The units are cm/min.

(c) The wetting front can be found where , or

.

9.2   (a) Proceed as in 9.2.  Thus,

cm.

(b)   cm/min.

(c)

9.3   Straightforward

9.4   The two functions are related as .  Thus, conversely with (8.76) one has

, or upon integration .

9.5   As shown in the previous Exercise, Horton’s (9.76) produces a cumulative infiltration .  This equation can only give the same result as (9.69) for large values of time, provided .  Hence with this constraint the parameters  must satisfy .

9.6   The two functions are related as , so that the cumulative infiltration capacity is .

9.7  A steady downward flux eventually establishes a uniform soil water content and uniform soil water pressure throughout the profile, with a hydraulic gradient equal to minus one, i.e.  (if  is pointing down).  In this case the rainfall rate equals the capillary conductivity, that is .  Hence with (8.37) the soil water suction is , which yields with the given values of the parameters  of equivalent water column.  The manometer (at 0.5 m above the ground surface) of the tensiometer with its sensing element at 0.5 m below the surface reads a negative pressure of 160.32 cm; the tensiometer with its sensing element at 1.0 m below the surface reads a negative pressure of 210.32 cm.

9.8   (a) From (9.87), rewritten here for convenience , one obtains a time to ponding of .

(b) Equation (9.91), namely , can be implemented with the expression for  from Problem 9.6 to yield .  This equation can be readily solved for the compression reference time ; but the same problem has already been considered in Example 9.3, so that the solution (9.97) can be used here with  and .  This produces with  and  from part (a) the result .

(c)  Because , (9.92) can be written as

(d) With the result of part (a) one obtains .

9.9   a, b, c, e, f

9.10   a

9.11   a, c, d

9.12   (a) Proceed in the same way as shown in (9.12) in the text to obtain

(b)  Symmetry is required.  This means that at , the dependent variable  should have the same value as at ; similarly at ,  should assume the same value as at .

9.13   The answer, obtained with (9.24), is

9.14   While reliable methods are available for numerical differentiation and integration, for the purpose of this exercise a simple trapezoidal approach should be adequate.  Thus finite difference approximation of (9.25) produces for the following values of the water content  the respective values of the diffusivity .  By linear interpolation one obtains for the requested values of the water content , the values , respectively.

9.15   While reliable methods are available for numerical differentiation and integration, for the purpose of this exercise a simple trapezoidal approach should be adequate.  Thus finite difference approximation of (9.25) produces for the following values of the water content  the respective values of the diffusivity .  By linear interpolation one obtains for the requested values of the water content , the respective values .

9.16   Since for sorption the water content is a function of the Boltzmann variable, i.e. , where , after  the tabulated values of the water content will be found at distances .  Thus the water contents of the table of Exercise 9.15 , namely  will be found at cm.

9.17   From the definition of  in (9.17) and  in (9.8), the sorptivity can be written as

, or with (9.27)

Upon integration this immediately leads to (9.28)

9.18   From the definition of  in (9.17) and  in (9.8), the sorptivity can be written as

.  Hence with (9.38) this becomes

(1)

The double integral in the numerator of (1) can be worked out by parts, namely as , with  and .  Hence , and with Leibniz (see Appendix) it is found that .  The double integral becomes

.  The first term in this expression is zero at both ; substitution of the second term for the double integral in (1) produces the desired result (9.39).

9.19   With  (9.38) and (9.39) produce, respectively,

and

Elimination of time between these two expressions leads to the following relationship between the infiltrated volume and the distance to the wetting front

If the diffusivity is given by (8.39) this becomes

For , this yields  and , respectively.  The values of these constants are not very different from the more accurate ones given behind (9.48) namely 0.626 and 0.862, respectively; as expected, the agreement improves as  increases.

9.20   The maximal flux, , occurs when the soil water suction at the ground surface becomes very lary large, that is  at .  Equation (9.103) becomes for this situation, after substitution of  by (8.37),

Put now

This changes (9.103) further into

The definite integral is known to be equal to , and the desired result (9.104) follows immediately.

9.21   The depth, for which the soil definitely controls the flux, is given by (9.104); if it is smaller than that, the atmosphere also plays a role.  Thus with the given values of the parameters the result is  with (9.104) and  with (9.105).

9.22    The parameters in (8.37) for Diablo loam can be obtained by inspection of Figure 8.29.  Close to saturation, when  is small, the figure shows that  cm/d, approximately.  Hence .  The slope of the straight lower end of the curve is roughly –2; thus .  Finally by trial and error a good fit can be obtained with the curve shown in the figure for .

With these values of the parameters (9.105) produces the following results.

For depths of the water table at  below the soil surface, the maximal rates of evaporation are, respectively, .

9.23   a, e

9.24   b, d

-

Chapter 10

10.1   If a recession hydrograph can be described by an exponential decay function, such as (10.153), the flow at any time  is ; similarly the flow at a time , which is a constant time interval  later, so that , is given by . Therefore their ratio, namely  is a constant and independent of , so that  describes a straight line through the origin.

10.2   Integration of (10.157) with the stated boundary condition can be written as , and this yields , or .

10.3   (a) The derivative of (10.153), namely  indicates that  when  in (10.157); actually, this result is also given in (10.171).  In the present case this produces .

(b) The constant in (10.154) can be expressed in terms of the result of (a) as , which yields a daily depletion ratio, i.e. for   in the present case .

10.4   (a) The derivative of (10.153), namely  indicates that  when  in (10.157); actually, this result is also given in (10.171).  In the present case this produces .

(b) The constant in (10.154) can be expressed in terms of the result of (a) as , which yields a daily depletion ratio, i.e. for   in the present case .

10.5   (a) Straightforward.

(b) Equation (10.160) can also be written as

(1)

The derivative of (10.160) is

, or after substitution of (1) for the time variable, .  This is in the form of (10.157) with the parameters as given in (10.161).

10.6   (a) Straightforward

(b) Equation (10.162) can also be written as

(1)

The derivative of (10.162) is

, or after substitution of (1),

.  This is in the form of (10.157) with the parameters as given in (10.163).

10.7    (a) Straightforward

(b) The derivative of (10.164) is obtained directly as

, which is in the form of (10.157) with the parameters as given in (10.165).

10.8   According to (10.169) with (1.68) and

,

or since   and in light of(10.161)

.

Equation (10.170) yields the same result for .

10.9   Multiplication of (10.161) by (10.165) with the default value  produces

.

Equation (10.165) with the above result for D yields

.

10.10   According to (10.174) the effective values at the basin scale are

and .

10.11   Division of (10.163) by (10.161) produces

.

Equation (10.163) with the above result for  yields

.

10.13    a, d, e, f, g

10.14    c, d

10.15    d, f

10.16    d, f

10.17    a, b, d, e

10.18   The governing equation is (10.5).  A solution can be attempted by separation of variables in the form of a product solution like (10.51), namely

Substitution into Laplace’s (10.5) produces in this case

(1)

where  must be a constant;   are totally independent of each other, so that the  dependent parts of this expression can only be equal if both are constant.  The constant is squared to ensure that each component of (1) is positive.  As will be seen below, each component of (1) must be positive for the solution to satisfy the boundary conditions along .  The solution of the ordinary differential equation for  is

(2)

and the solution of the ODE for  is

(3)

in which  are additional constants.  All these constants can be determined from the boundary conditions (10.6).

The fourth of (10.6) requires  at ; this yields with (3) .

The third of (10.6) requires at ; this yields with (2) , or .  This changes (2) into

.

With the two constants  determined, the solution can be written for the time being

(4)

in which

Consider next the fifth of boundary conditions (10.6).  It will prove convenient to shift the reference level of h by an amount D.  (This will not jeopardize the validity of (4) as a solution of (10.5), but will allow the formulation of the fifth of (10.6) in a more amenable form, namely

This is realized by an infinite number of values of , namely for

For any given value of n the solution can now be written as

(5)

where  is the constant for the particular value of n.  Only the first and the second of boundary conditions 10.6 remain to be satisfied.  It is clear from inspection that for  no single selected value of n will yield a solution in the form of (5) that will satisfy those conditions and that a Fourier series is required to do this.  Because (10.5) is linear, the sum of the solutions is also a solution.  This can be written as

(6)

Imposition of the first of (10.6) on (6) yields

(7)

and imposition of the second of (10.6) yields

(8)

The values of the constants  can now be obtained with the method of Fourier.  This consists of multiplying both sides of (7) and (8) by  (in which m is any one of ), and then integrating over the flow domain, which in this case covers the range  .  This results in the following equation

This produces finally

Insertion of this expression into (6) yields the desired result (10.7).

10.19    Both expressions in (10.8) involve similar operations.  The first requires first the partial derivative of (10.7) with respect to x, and then its integration over z.  The second expression in (10.8) requires first the partial derivative of (10.7) with respect to z, and then subsequently its integration over x.  For the present illustration consider the second option.

At  the sin term becomes , so that

Integration of the dependent part of this expression over the required interval gives

so that

from which (10.9) follows directly.

10.20   The time-dependent part of (10.70) can be written as

.  Integration yields (10.71), i.e. .  Insertion in (10.69) produces (10.72), i.e. , in which for convenience of notation  and .

10.21   The ratio of the second and the first term of (10.112) is

.  This ratio is smaller than 1 %, when .  This is roughly the value of  where the 2 curves join in Figure 10.23.

10.22   This problem is the inverse of the one treated in section 10.3.4, in that instead of draining of the aquifer, it describes its filling.

(a) Two essential boundary conditions are

A third boundary condition can be either

(b) The application of Boltzmann’s transform (10.54)

(c)  If  is known, by virtue of the applicability Boltzmann’s transform, we know that this solution is not a function of  separately, but of the combined variable . Therefore the solution must be of the form , or conversely

.  With a known solution , if is specified, say , then  is also specified.  Hence the relationship is .

10.23   Rewrite the unit response (10.117) for convenient reference

The outflow rate from the aquifer in response to an input  as given by (10.118) is

Thus if the input is given by (10.127) as described in Example 10.3, the response of the aquifer, as outflow rate at  at time , is

Upon integration this becomes the desired result

10.24   The linearized Boussinesq equation (10.88) is

This partial differential equation can be transformed into an ordinary differential equation by means of the Boltzmann transform (10.54), i.e. .  The operations on each term are as follows

These transform the Boussinesq equation into

10.25    b, e, g, h, i

Chapter 12

12.1

|  | 1-hour | Combined |  | 1-hour | Combined |
| --- | --- | --- | --- | --- | --- |
| Time | Unit | Storm |  | Time | Unit | Storm |
| (h) | Hydrogrph | Outflow |  | (h) | Hydrogrph | Outflow |
|  | (cm/h) | (cm/h) |  |  | (cm/h) | (cm/h) |
| 0 | 0 | 0.0000 |  | 8 | 0.0138 | 0.3443 |
| 0.5 | 0.016 | 0.0240 |  | 8.5 | 0.0094 | 0.2467 |
| 1 | 0.0828 | 0.1242 |  | 9 | 0.0098 | 0.1841 |
| 1.5 | 0.1766 | 0.3049 |  | 9.5 | 0.0068 | 0.1289 |
| 2 | 0.2392 | 0.5658 |  | 10 | 0.0012 | 0.0801 |
| 2.5 | 0.2624 | 0.8975 |  | 10.5 | 0.0006 | 0.0546 |
| 3 | 0.255 | 1.3034 |  | 11 | 0.0038 | 0.0469 |
| 3.5 | 0.2242 | 1.6810 |  | 11.5 | 0.0028 | 0.0322 |
| 4 | 0.183 | 1.8449 |  | 12 | -0.0016 | 0.0118 |
| 4.5 | 0.146 | 1.8029 |  | 12.5 | -0.0012 | 0.0075 |
| 5 | 0.1158 | 1.6257 |  | 13 | 0.0016 | 0.0132 |
| 5.5 | 0.0868 | 1.3696 |  | 13.5 | 0.0012 | 0.0097 |
| 6 | 0.0608 | 1.0944 |  | 14 | -0.0016 | -0.0046 |
| 6.5 | 0.044 | 0.8524 |  | 14.5 | -0.0012 | -0.0035 |
| 7 | 0.0346 | 0.6555 |  | 15 | 0.0016 | 0.0046 |
| 7.5 | 0.0244 | 0.4851 |  |  |  |  |

12.2   a.   The unscaled S hydrograph obtained by means of the procedure illustrated in Figure 12.4 is tabulated in the first column of the table below.  The data given for this exercise are taken from one single storm runoff hydrograph, so they really cannot be expected to represent a “perfect” unit hydrograph.  It is no surprise therefore that this S hydrograph exhibits severe oscillations with a 4-hour period.  Although several schemes are possible, for the purpose of this exercise the S hydrograph can simply be smoothed by taking a running average after 3 h, namely by calculating the S value as follows , where  is the smoothed value of the S hydrograph.  The smoothed hydrograph is shown in the second column and indicates that the equilibrium flow, resulting from a rainfall continuing indefinitely at the same rate, is .  Since the drainage area is 29.5 km2, this corresponds to a rainfall input rate of 0.80439 cm/h.

|  | unscaled | smoothed | 2-hour |  | unscaled | smoothed | 2-hour |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Time | S | S | unit | Time | S | S | unit |
|  | hydrograph | hydrograph | hydrograph |  | hydrograph | hydrograph | hydrograph |
| (h) | (m3/s) | (m3/s) | (m3/s) | (h) | (m3/s) | (m3/s) | (m3/s) |
| 0 | 0.00 | 0.00 | 0.00 | 8 | 65.10 | 61.29 | 4.25 |
| 1 | 4.01 | 4.01 | 2.49 | 9 | 60.25 | 63.37 | 3.10 |
| 2 | 15.26 | 15.26 | 9.49 | 10 | 58.87 | 64.69 | 2.11 |
| 3 | 36.55 | 35.43 | 19.53 | 11 | 69.25 | 65.53 | 1.34 |
| 4 | 45.40 | 43.42 | 17.51 | 12 | 70.40 | 65.92 | 0.76 |
| 5 | 44.49 | 49.52 | 8.76 | 13 | 63.58 | 65.92 | 0.24 |
| 6 | 47.25 | 54.45 | 6.85 | 14 | 60.43 | 65.92 | 0.00 |
| 7 | 60.95 | 58.39 | 5.51 | 15 | 69.25 | 65.92 | 0.00 |

b.   The 2-hour unit hydrograph is obtainable by the shift-subtract procedure of the S hydrograph, as illustrated in Figure 12.5.  If the unit volume is taken as 1 cm, the 2-hour unit hydrograph is the result of a rainfall intensity of 0.5 cm/h lasting for 2 hours.  Thus, to ensure a volume of 1 cm, the shift-subtract result must be multiplied by 0.5 and divided by 0.804.  The final result is shown in the third column of the table above.

c.   The peak flow, resulting from the three rainfall bursts, calculated as illustrated in Figure 12.2, is 42.21 m3/s.

12.3   a.  The S hydrograph can be derived using the procedure illustrated in Figure 12.4.  The steady equilibrium shows some oscillations, but they are relatively mild so that the S hydrograph can be used as it is (i.e. without smoothing) to calculate the unit hydrograph for part (b).  The averaged equilibrium flow of this S hydrograph is 243.06 m3/s.  Hence, as the drainage area is 875 km2, the rainfall intensity that produced the 6-hour unit hydrograph, was 1.00 mm/h.  This also means that the “unit” volume of this unit hydrograph is 6 mm.

b.   The 4-hour unit hydrograph, needed to calculate the runoff resulting from the three successive 4-hour periods of rain, can be obtained by the shift-subtract procedure with the S hydrograph, as illustrated in Figure 12.5.  A steady rainfall input of 1 mm/h, lasting for 4 hours produces a volume of 4 mm; therefore the result obtained from the shift-subtract procedure of the original S hydrograph must be multiplied by ¼ in order to obtain a unit hydrograph with a unit volume of 1 mm.  The resulting 4-hour unit hydrograph is shown in the table below.  The peak flow resulting from the three successive 4-hour periods of rain is 903 m3/s.

| Time | 4-h UH | Time | 4-h UH | Time | 4-h UH |
| --- | --- | --- | --- | --- | --- |
| (h) | m3/s | (h) | m3/s | (h) | m3/s |
| 0 | 0 | 28 | 1.820 | 54 | 0.156 |
| 2 | 0.033 | 30 | 1.250 | 56 | 0.128 |
| 4 | 0.100 | 32 | 2.765 | 58 | 0.106 |
| 6 | 0.418 | 34 | 0.320 | 60 | 0.094 |
| 8 | 1.768 | 36 | 0.085 | 62 | 0.083 |
| 10 | 3.985 | 38 | 2.248 | 64 | 0.073 |
| 12 | 5.918 | 40 | 0.035 | 66 | 0.061 |
| 14 | 8.603 | 42 | -0.365 | 68 | 0.050 |
| 16 | 13.323 | 44 | 1.898 | 70 | 0.039 |
| 18 | 20.755 | 46 | -0.282 | 72 | 0.028 |
| 20 | 20.273 | 48 | -0.532 | 74 | 0.017 |
| 22 | 15.325 | 50 | 0.916 | 76 | 0.006 |
| 24 | 12.753 | 52 | 0.183 | 78 | 0.000 |
| 26 | 7.100 |  |  |  |  |

12.4   The calculations can be carried out by forward substitution, as shown in (12.14).

Thus  and ;

;

, and in the same way .  Graphically, these values of  represent a triangle.

12.5     a, d, f, k, m.

12.6   (a)  The S hydrograph is given in m3/h.  To obtain the instantaneous unit hydrograph one has to take the derivative of ; this yields , but it must still be scaled to ensure that it yields a unit volume of 1 cm.  If the S hydrograph were expressed in cm/h, it should produce a steady outflow rate of 1 cm/h after a long time; in actual fact, the given expression yields .  Therefore the instantaneous unit hydrograph must be scaled with 9000 to produce results in cm/h.  Finally, the desired result is  , which represents an outflow in cm/h per cm of instantaneous input volume.

(b)  The rain stops after 2 hours; therefore with h, application of the convolution integral (12.2) yields

12.7   (a)

Its units are cm/h.

(b)  The rain stops after 3 hours; therefore application of the convolution integral with

produces

(c)  In this case the rain continues beyond ; thus

12.8     e, f, g

12.9   The four equations (12.17) and their analogs for  can be written in the following form .  The values of the coefficients of each of these equations can be written in matrix form as follows

| a | b | c | d | e |
| --- | --- | --- | --- | --- |
| 21 | 12 | 2 | 0 | -11.49 |
| 12 | 21 | 12 | 2 | -14.72 |
| 2 | 12 | 21 | 12 | -10.82 |
| 0 | 2 | 12 | 21 | -5.28 |

The four simultaneous linear equations can be readily solved by a variety of methods.

Gauss’s method produces for , the respective values 0.2919, 0.4146, 01921, and 0.1021; not surprisingly, these values resemble those used in Example 12.3, namely 0.3, 0.4, 0.2, and 0.1.

12.10      b, c, d, e

12.11     c

12.12     b, d, f, g, i

12.13    The right triangle shown as a dashed line in Figure 12.15 represents a triangular time-area function (or width function), which can be formulated as follows

where  is the time of concentration.  The unit response is calculated by applying (12.29) with this function.  Thus, one has for

which upon integration results in

or finally

Similarly for , one can write

which yields

Again, it can be readily checked that the two expressions yield the same value for  at , as they should.

12.14   The inflow into the third tank is the outflow from the second tank (12.36) plus an instantaneous rainfall input ; the response of the third tank is given by (12.28).  Therefore, the required convolution operation can be written as

or, upon integration

which is (12.37).

12.15   The inflow into the fourth tank is the outflow from the third tank (12.37) plus an instantaneous rainfall input ; the response of the third tank is given by (12.28).  Therefore, the required convolution operation can be written as

or, upon integration

12.16   The first moment of the unit response about the origin is by definition (13.9), that is .  In the case of (12.41) this becomes

The integral on the right is the complete gamma function , which in turn satisfies the recurrence relationship  Hence, one obtains

, which is (12.42).

12.17   The second moment of the unit response about the origin is by definition (13.9), that is .  In the case of (12.41) this becomes

The integral on the right is the complete gamma function , which in turn satisfies the recurrence relationship  Hence, this second moment about the origin becomes .  According to (13.12) the second moment about the mean is related to the first two moments about the origin by .  Since  [see (12.42) and Exercise 12.16], one obtains immediately , which is (12.43), as required.

12.18   In the case of a channel with a triangular cross section, both the cross sectional area  and the wetted perimeter  are functions of the water depth .  For the purpose of the present exercise these can be written as  and , in which  are constants which can be readily determined for any triangular geometry; it follows that the hydraulic radius is .  The storage in a channel reach of length  is .  For steady uniform conditions (5.39) produces then the outflow rate from the reach as ; the channel storage is in terms of the outflow from the reach

Hence the exponent of  is  which yields  in the case of the GM equation and  in the case of the Chezy equation.

12.19   Because , (10.85) can be written as a positive flow rate in the channel

With  one obtains the outflow rate per unit area of catchment

from which one obtains

and

This can be inserted in the integral (12.54) to yield

in which z is the dummy variable of integration.  The values of the constants are , so that the integral yields finally (12. 55), that is

12.20   Because , (10.85) can be written as a positive flow rate in the channel

With  one obtains the outflow rate per unit area of catchment

This can be inserted directly into (12.54) as follows

Upon integration this becomes

which  is (12.56), that is .

12.21   The straight line can be described by , in which  are constants.  The desired functional relationship can be obtained simply by taking the differentials of both sides, namely  from which the derivative results as

.

12.22     d, e

Chapter 13

13.1

Because the mean, , is a constant, the second moment about the mean can be developed as

Similarly, with the same reasoning the third moment about the mean can be developed as

13.2    By virtue of the first equation of (13.12), the second moment about the mean can be obtained form the first two moments about the origin by ; for the exponential distribution these two moments are

Hence .  [See also exercises 12.16 and 12.17]

13.3   The fourth septile, denoted by, say , is the solution of

This yields

or finally

In a similar way one obtains for the fifth octile

15.4   The density function is given by  with a lower bound at .  Hence the mean is

The second moment about the origin is

With (13.12), that is , the second moment about the mean, that is the variance, becomes

13.5    The 95th percentile, say , is the solution of

This yields

or finally

13.6   A one hundred year event has a probability of non-exceedance .

The probability that this event will be exceeded after exactly 100 years is given by the geometric distribution; thus

.

The probability that this event will be exceeded some time in the coming 100 years, that is, that it will be exceeded before the 100 years have passed, is given by (13.30)??????; thus

.

13.7    b, c

13.8    d

13.9    a, d

13.10   Designate a week without rain as a success; thus the probability of success is , and the probability of failure .   The probability of 6 weeks out of 12 without rain is

13.11    c, e

13.12   (a) The median flood of this sample is 309 m3/s.

(b) Its mean is 323.8 m3/s.

(c) With the Weibull formula the estimate of the empirical non-exceedance probability of the m-th smallest event is , and its return period .  Inversion of this equation yields ; in the case of  and , this gives .  This means that the estimate of the 7-year flood is the

12-th smallest event of this record; this has a flow rate of 427 m3/s.

(d) 331 m3/s is the 8-th smallest event of this sample and with the Weibull formula its empirical non-exceedance probability is 8/14; similarly 393 m3/s is the 10-th smallest event and its probability is 10/14.  Hence the probability that in any given year the maximum flow rate will lie between these two flow rates is .

(e) The exponential distribution has only one parameter; therefore only one moment is needed, namely the first, i.e. the mean.  This can readily be shown to be given by (see also Exercises 12.16 and 13.2) ; hence for this record .

13.13    The mean of the first asymptote for largest values is given by .  Thus the exceedance probability of the mean is .

13.14    The non-exceedance probability in any one year is .  Therefore the non-exceedance probability in a decade, that is in10 consecutive years, is

13.15   (a) Fuller’s formula can be inverted to yield the return period as a function of the annual maximum, as follows

Since by definition , one has finally

(b)  ;  the probability that this flood will be exceeded every single year in four consecutive years is

(c) The probability that this flood of 700 m3/s will be exceeded only once, namely in the last year of a four-year period is .

13.18     b, c

-

# Text boxes

Potential Temperature,

z

A

B

C

D

4

3

2

1

%

H  (cm)

1

4

3

2

4

3

2

1

H  (cm)

%