## Slide 1: Physical Hydrology & Hydroclimatology (Multiscale Hydrology)
A science dealing with the properties, distribution and circulation of water.
R. Balaji
balajir@colorado.edu
CVEN5333 http://civil.colorado.edu/~balajir/CVEN5333
Includes Slides from Prof. Mike Gooseff

## Slide 2: Lecture – Week 1
Context for learning hydrology
  Water Resources Management
  Space-time variability of moisture delivery and abstraction
Global water cycle
Mass Balance Equation
  Global, continental, regional and watershed
Residence time of water in the system

## Slide 3: Syllabus
PREREQUISITES:
Undergraduate physics (understanding of forces, laws of motion and thermal properties of matter), mathematics (calculus and algebra),
basic computer literacy (e.g. analyze and plot data, spreadsheets)

## Slide 4: Class Goals
Provide you with a firm background in process-oriented hydrology
Large scale climate drivers and signatures to regional hydrology
Foster your ability to think critically the interconnections
Help you develop a strong understanding of physical science in preparation for engineering, research, and water management needs

## Slide 5: Evaluation
Homework (35%)
  Mix of problems from book and others
  Due ~every two weeks
  Must be organized and presented neatly
    Include diagrams and a box around your final answer
  Your name should be on each page
  The entire assignment should be stapled together

## Slide 6: Evaluation
Mid-term (20%) and Final Exam (30%)
  Mid-term: Closed book, open notes, in class
  Final: Comprehensive take-home exam
Hydroclimate Project (15%)
  Climate connection and diagnostics of hydrologic variability
  Predictability

## Slide 7: Course Materials
I will use the class web site and Google Drive to
  Post lecture presentations
  Relevant research papers
  Post homework assignments
  Facilitate discussion or further exploration of class topics
Weekly e-mails with reading assignment/resources, to prepare for the following week
Hydrology and Water Resources Seminar
  Wednesdays, ECCR1B41 11:15

## Slide 8: Motivation (from a recent drought)

## Slide 9
August 21, 2021
August 13, 2021
August 16, 2021
August 21, 2021
Lake Mead will fall below 1075’ on January 1, 2022, triggering first-ever ‘Tier 1’ water shortage in Lower Basin…..

## Slide 10: Colorado River
= Major Diversion
7 States, 2 Nations, 30 Tribes
8% of area of the Lower 48
Annual Flow ~14.75 MAF
  = Hudson River
Worst drought in gaged record started 2000 ~12.4 MAF/yr
= ~19% decline annually
40 M People
All of the Major Cities in SW US
4.5m Irrigated Acres
Fully Allocated in 1922
Complex Use Agreements
Withdrawals equaled Supplies ~2000
New Projects still contemplated
No longer reaches the ocean
Colorado River Basin Overview

## Slide 12
Colorado River Demand - Supply
UC CRSS stream gauges
LC CRSS stream gauges
What is the Colorado River System-wide Water supply risk profile under climate change?
      Need to consider the entire syste (~60AF Storage)
      Need to generate streamflow scenarios consistent with climate projections and combining (Paleo?)
Is there flexibility within the existing management framework?
Can Management Mitigate the future risk?

## Slide 13
Tier 1 Levels

## Slide 14: Annual Precipitation Decreases 2000-2020
21-Year Period tied with driest in 20th C
  -22 mm reduction (-6%)
High Years (blue box) are low relative to 20C
  2005, 2011, 2019
Low Years (red box) are very low relative to 20C
  2000, 2002, 2012, 2018, 2020
  3 of last 4 years bottom 15 (10?) since 1895

## Slide 15: Scale Matters
Runoff Efficiency (How much Precip actually runs off) Varies Greatly from ~5% (Dirty Devil) to > 40% (Upper Mainstem)
You can’t model the basin at large scales and expect accurate results
  GCMs (e.g. Milly, Seager) and H&E 2006 may get the right answer, but miss important topographical effects
14.4%
16.1%
24.9%
14.1%
6.3%
9.9%
11.8%
2.4%
% of Total Runoff
Notes: 15

## Slide 17
From http://www.doi.gov/water2025/index.html

## Slide 18: Emerging Megadrought
2000—2018 2nd Driest 19-year period since 800 AD as measured by JJA Soil Moisture
Caused by Natural Variability aided by anthropogenic drying
About 50% due to humans
Without anthropogenic drying, would be a moderate drought
Science, April 2020

## Slide 19
Reconstruction of Colorado River at Lees Ferry streamflow, 762-2005, with 10-year running mean
Six 10-year periods before 1900 with reconstructed mean flow lower than 12 MaF (lowest: 1146-1155)
1905-1930 one of the three wettest ~25-year periods in 1200 years
Mid-1100s: 57-year period with mean flow of ~13 MaF
Century-scale non-stationarity: 100-year mean varies from 13.9 to 15.4 MaF
Paleo Perspective
* Slide courtesy of Jeff Lukas, NOAA/WWA
Notes: 19
paleo reconstructed streamflow indicates that periods of more severe, sustained drought have occurred in the past.
overall substantial variability and lower mean per 100 year period.

## Slide 20: Aridification – not a drought
Declining Snowpack and earlier runoff
Higher Temperatures: >1.25°C
Drying Soil
Thirsty Atmosphere (holds more moisture)
Moving storm tracks (less certain, but a worry)
Shorter Winter
Megadrought

## Slide 22: A Water Resources Management Perspective
Time
Horizon
Inter-decadal
Hours
Weather
Climate
Decision Analysis: Risk + Values
Data: Historical, Paleo, Scale, Models
Facility Planning
  Reservoir, Treatment Plant Size
Policy + Regulatory Framework
  Flood Frequency, Water Rights, 7Q10 flow
Operational Analysis
  Reservoir Operation, Flood/Drought Preparation
Emergency Management
  Flood Warning, Drought Response

## Slide 23: Climate Variability
Daily
Annual
Inter-annual to Inter-decadal
Centennial
Millenial
Diurnal cycle
Seasonal cycle
Ocean-atmosphere coupled modes (ENSO, NAO, PDO)
Thermohaline circulation
Milankovich cycle (earth’s orbital and precision)

## Slide 24
What Drives Year to Year
Variability in regional
Hydrology?
(Floods, Droughts etc.)
Hydroclimate Predictions – Scenario Generation
(Nonlinear Time Series Tools, Watershed Modeling)
Decision Support System
(Evaluate decision strategies
Under uncertainty)
(Research) Framework
Forecast
Diagnosis
Application

## Slide 25
Water and Climate Change
The United Nations World Water Development Report 2020

## Slide 26: Water and Climate change
The hydrological changes induced by climate change will add challenges to the sustainable management of water resources, which are already under severe pressure in many regions of the world, and amplifies water-related extremes such as flood and droughts

## Slide 27: Impacts on Water Resources
Source: AQUASTAT (2010).
Note: *Evaporation from artificial lakes.
Figure 14 Global water withdrawals throughout the previous century
Note: This figure depicts the relative change in annual discharge at 2°C temperature increase compared with present day, under RCP8.5.
Source: Schewe et al. (2014, fig. 1, p. 3246). The Attribution Share-Alike 3.0 IGO (CC BY-SA 3.0 IGO) licence does not apply to this figure.
Figure 8 Climate change scenario trends in water availability
Source: Polade et al. (2014, fig. 2).
Note: Stippling indicates areas where at least 70% of the models agree on the sign of the change. Graph to the right: zonal mean values.
Figure 6 CMIP5 multi-model ensemble average mean change in frequency of dry days (days/year) by 2060–2089, relative to the historical period 1960–1989, using the RCP8.5 forcing scenario
Note: The average of the model projections available for the 2081–2100 period under the RCP2.6 (left) and RCP8.5 (right) scenarios for (a) change in annual mean surface temperature and (b) change in annual mean precipitation, in percentages. Changes are shown relative to the 1986–2005 period. The number of CMIP5 models used to calculate the multi-model mean is indicated in the upper right corner of each panel. Stippling dots on indicates regions where the projected change is large compared to natural internal variability (i.e., greater than two standard deviations of internal variability in 20-year means) and where 90% of the models agree on the sign of change. Hatching (diagonal lines) on and shows regions where the projected change is less than one standard deviation of natural internal variability in 20-year means.
Source: Adapted from IPCC (2014a, fig. 2.2, p. 61).
Figure 5 Coupled Model Intercomparison Project Phase 5 (CMIP5) multi-model mean projections
Notes: Figure 14, Figure 8, Figure 6, and Figure 5

## Slide 28: Adaptation and Mitigation
Adaptation encompasses a combination of natural, engineered and technological options, as well as social and institutional measures to moderate harm or exploit beneficial opportunities from climate change.
Mitigation comprises human interventions to reduce the sources or enhance the sinks of greenhouse gases (GHGs).

## Slide 29: Water resources management, infrastructure and ecosystems

## Slide 30: Disaster Risk Reduction
Source: MunichRe, NatCatSERVICE (2019).
Note: Accounted events have caused at least one fatality and/or produced normalized losses ≥ US$100K, 300K, 1M, or 3M (depending on the assigned World Bank income group of the affected country).
Figure 15 World weather-related natural catastrophes by peril, 1980–2018
The current impacts and future anticipated risks associated with extreme events demand sustainable solutions for climate change adaptation and Disaster Risk Reduction (DDR).

## Slide 31: Global Water Stress balance of people (demand), water available (supply)
Water and Climate Change
UN Report 2020
Notes: REPLACE WITH NEW VERSION FROM NATURE PAPER IN 2018????

## Slide 32: Hydrologic Science in the hierarchy from basic sciences to water resources management
Basic Sciences
Mathematics
Statistics
Physics
Chemistry
Biology
Geosciences
Geology
Soil Science
Atmospheric Science
Ocean Science
Glaciology
Geochemistry
Fluid Mechanics
Hydraulic Engineering
Meteorology
Hydrologic Science
Economics
Law
Sociology
Political Science
Engineering Hydrology
Agriculture
Forestry
Water Resources Management
Modified From: National Research Council Committee on Opportunities in the Hydrologic Sciences (COHS), (1991), Opportunities in the Hydrologic Sciences, Editor, P. S. Eagleson, National Academy Press, Washington, D.C.

## Slide 33: The Hydrologic Cycle
From Ross Woods

## Slide 34: Hydrologic Cycle
Compartments (storage reservoirs):
  Ocean
  Atmosphere
  Continent
    Lakes & Streams
    Glaciers, snowpacks
    Groundwater
Mechanisms (interactions)
  Precipitation (rain, snow)
  Infiltration
  Evaporation, Transpiration --> Evapotranspiration
  Surface Runoff
Notes: Compartments (storage reservoirs):
  Ocean
  Atmosphere
  Continent
    Surface impoundments (lakes, streams)
    Glaciers, snowpacks
    Groundwater
Mechanisms (interactions)
  Precipitation (rain, snow)
  Infiltration
  Evaporation, Transpiration  Evapotranspiration
  Surface Runoff

## Slide 35: The Hydrologic Cycle
Conservative STORAGE = INPUT - OUTPUT
(over long periods)
Compartments are not equal in terms of storage or residence time
Notes: Key Features:
Conservative: Storage = Input – Output (over a long period)
Water compartments are not equal in terms of storage or residence time

## Slide 36
From Chow et al., 1988

## Slide 37: Continental Water Balance m/yr
From Chow et al., 1988
0.73
0.73
0.69
0.67
0.74
Europe
Asia
Africa
N America
Australia
Data from Brutsaert, 2005, Table 1.2
0.32
0.29
0.14
0.29
0.23
0.41
0.44
0.55
0.38
0.51

## Slide 38: Water Budgets Storage = Input – Output
Reservoir (box, compartment: M in mass units): An amount of material defined by certain physical, chemical, or biological characteristics that can be considered ~homogeneous
  Ex. water in the ocean (property, reservoir)
Input: A flux of material into a reservoir
Output: A flux of material out of a reservoir
Flux: The amount of material transferred from one reservoir to another, per unit time (M/T or M/TL2)
  Ex. The rate of evaporation of water from the surface ocean
Notes: Reservoir (box, compartment: M in mass units): An amount of material defined by certain physical, chemical, or biological characteristics that can be considered homogeneous
Ex. water in the ocean (property, reservoir)
Input: A flux of material into a reservoir
Output: A flux of material out of a reservoir
Flux: The amount of material transferred from one reservoir to another per unit time (M/T or M/TL2)
Ex. The rate of evaporation of water from the surface ocean

## Slide 39: Hydrologic Mass Balance; recall…
Hornberger et al., 1998
r is roughly constant over this
“natural” range
Notes: MAKE THE POINT THAT BECAUSE r IS ~CONSTANT, WE CAN DEAL WITH VOLUME BALANCES AND NOT WORRY ABOUT CHANGES IN r.

## Slide 40: Hydrologic Mass Balance
The HC is defined by mass balance called a water budget; applied to a watershed: inputs (I) – outputs (Q) = storage (S)
But of course, these fluxes all occur dynamically;
One way to describe this is with a transfer function (W):

## Slide 41: Hydrologic Mass Balance
If outputs are linearly related to storage, then: S = kQ where k has dimension of time
But, storage is difficult to measure directly, so we can eliminate it using the 2 above equations: if k is constant, this is a linear system. If k is a function of Q or I, then this is a non-linear system

## Slide 42: Water Budget of Earth Sounds easy… What’s the big deal?
We need to know the size of compartments (storage) and fluxes to compare the supply and demand of water in systems
To allocate resources, need to know the inputs (precip, etc.) and outputs (plant use, evap, etc.) so that the amount that can safely be extracted can be calculated
Notes: We need to know the size of compartments (storage) and fluxes to compare the supply and demand of water in systems
To allocate resources, need to know the inputs (precip, etc.) and outputs (plant use, evap, etc.) so that the amount that can safely be extracted can be calculated

## Slide 43: Water Budgets The big deal: Everything is dynamic!
Q(t)
Streamflow from Pemigewasset River, NH.
N.B. the y-axis is on a log-scale…

## Slide 44: Simplicity
Hydrologists like simplicity, so we often state volumetric units [L3] as depths [L] applied to an area.
Example: A precipitation gauge may record a 3 cm storm. Assuming that the rainfall was uniform across a 1 km2 catchment, 30,000 m3 of water entered the catchment as rain, but 3 cm is an easier quantity to deal with. Same with runoff…
Notes: Hydrologists like simplicity, so we often state volumetric units [L3] as depths [L] applied to an area.
Example: A precipitation gauge may record a 3 cm storm. Assuming that the rainfall was uniform across a 1 km2 catchment, 30,000 m3 of water entered the catchment as rain, but 3 cm is an easier quantity to deal with. Same with runoff…

## Slide 45: Global water balance fluxes and stores
Storage in km3. Fluxes in km3/yr
From Dingman, 2002
From Brutsaert, 2005

## Slide 46: World Water Balance
From Brutsaert, 2005

## Slide 47
Atmospheric Water
Soil Water
Surface Water
Groundwater
Water Balance
Change of Storage
= Inflow - Outflow

## Slide 48: Watershed Hydrologic Cycle
Inputs:
  Rain, Snow, Groundwater
Outputs (in red below):
  Evaporation, Transpiration, Streamflow, Groundwater
Hewlett, 1969

## Slide 49: Systems Perspective
Precipitation
Evaporation
S
S
Interception
Transpiration
Overland Flow
Surface Runoff
Infiltration
Subsurface Flow
Groundwater Flow
Atmospheric Water
Subsurface Water
Runoff to streams + ocean
Groundwater recharge
Surface Water
Notes: Fill in arrows from Figure 1.2.1 in Chow et al.

## Slide 50: Watershed delineated on a topographic map

## Slide 51: Watershed water balance
P
ET
Q
Gout
Gin
S

## Slide 52: Regional Water Balance Equation
∆S=P-Q-E
P
E
Q
∆S
P=Q+E
Q=P-E

## Slide 53: Discrete Time Continuity
We often need to break up a time-changing situation into small steps (dt) we can manage:
dS = I(t)dt – Q(t)dt
Sj – Sj-1 = Ij = Qj and Sj = Sj-1 + DSj
DSj
Notes: FILL IN EQ 2.3.1 and 2.3.2 and 2.3.3 and 2.3.4

## Slide 54: Discrete Time Continuity
Q(t) and I(t) are continuous in time. 2 ways to evaluate:
Sample Data Function (e.g., ):
streamflow
Qj = Q(tj) = Q(jDt)
Qj and Q(t) are both [L3/T] or [L/T]
Notes: “rainfall”, then, FILL IN EQ 2.3.5
“streamflow”, then FILL IN 2.3.6 and 2.3.7

## Slide 55: Discrete Time Continuity
Q(t) and I(t) are continuous in time. 2 ways to evaluate:
Pulse Data Function (e.g., ):
rainfall
Qj [L3] or [L]
Use Average Approach:
but, Q(t) [L3/T] or [L/T]
now, Qj and Q(t) are both [L3/T] or [L/T]
Notes: “rainfall”, then, FILL IN EQ 2.3.5
“streamflow”, then FILL IN 2.3.6 and 2.3.7

## Slide 56: Example
Given: Calculate the storage of water in a watershed (7.03 mi2) as a function of time given the data for incremental precipitation across the watershed & streamflow measured at its outlet. Assume S0 = 0.
PULSE
SAMPLE

## Slide 57: Example Solution
Let’s change the Q(t) to PULSE data:
1) Average Qj and Qj+1
2) multiply this average by Dt, and then
3) Normalize by watershed area
From j0 to j1:
Q(0) = 203 cfs, and Q(0.5) = 246 cfs
A= 7.03mi2 = 1.96x108 ft2 
So now, DS1 – I1 – Q1 = 0.15 in – 0.02 in
DS1 = 0.13 in

## Slide 58: Example Solution
Table 2.3.1

## Slide 59: Example Solution

## Slide 61: Hydrologic Data and Hydrologic Budget
USGS http://waterdata.usgs.gov
  Logan River Mean Annual Flow 236.8 cfs
Streamstats http://water.usgs.gov/osw/streamstats/
  Logan River Mean annual precipitation in inches 35.5
  Area 214 mi2

## Slide 64: Concept of Residence Time
Recall:
Definition – average length of time that an entity (i.e., water molecule) will remain in a reservoir
This is only really meaningful at steady-state, when I = Q 
Storage, S
[M or L3]
Output, Q
[M/T or L3/T]
Input, I
[M/T or L3/T]
Notes: Average length of time that an entity, in this case a water molecule, will remain in a reservoir
Only meaningful at steady-state where I = O
Residence time t = S/I = S/O

## Slide 65: Exercise
Example: What is the residence time of water in the atmosphere?
Accessible atm water (above 800m) = 4.4x106 km3
Continental precipitation = 110,303 km3/yr
Accessible fresh water above 800 m = 4.4 x 106 km3
Continental precipitation = 110,303 km3/yr
TR = S/I = 40 years
Notes: Residence time of fresh water.
Accessible fresh water above 800 m = 4.4 x 106 km3
Continental precipitation = 110,303 km3/yr
TR = S/I = 40 years

## Slide 66: Residence Times of Global Reservoirs
Location | Residence time
Oceans and seas | 3500 yrs
Groundwater | 2 weeks --> 10,000 yrs
Ice caps & glaciers | 10-10,000 yrs
Lakes & reservoirs | 1-100 yrs
Swamps | 1-10 yrs
Soil Moisture | 2 weeks --> 10 yrs
River Channels | ~2 weeks
Atmospheric Water | ~ 10 days
Biosphereic Water | ~1 week

## Slide 68: Ex.: Modeling Watershed Functioning
One way to model stream discharge (q) is to relate it to watershed storage dynamics (dS/dt):
q
Re-arranged to put q in terms of S:
Where, fW1 is a watershed storage function
Then, use chain rule to differentiate:
)

## Slide 69: Modeling Watershed Functioning
Kirchner, 2009 WRR
Now we can represent dq/dS as:
One can now approximate dq/dt as a power-law function of q:

## Slide 70: Modeling Watershed Functioning
Kirchner, 2009 WRR
This can then be integrated to solve for a simple function that predicts q:
Or, as a function of instantaneous p, et, and q: