## Slide 1: Physical Hydrology & Hydroclimatology (Multiscale Hydrology)
A science dealing with the properties, distribution and circulation of water.
R. Balaji
balajir@colorado.edu
CVEN5333 http://civil.colorado.edu/~balajir/CVEN5333
Includes slides from Prof. Mike Gooseff

## Slide 2: Evapotranspiration
Evapotranspiration
  Basics, Importance
Physics of Evaporation
  Turbulent Transfer of Heat, Momentum and Vapor
    Diffusion
Energy – Balance
Mass Transfer
Combination – Penman approach
Pan Evaporation, Evaporation from open water
Evaporation from bare soil
Transpiration
  Penman-Monteith
PET, Crop ET
  Physical Hydrology, Dingman (Chapter 6, Appendix D)
  Terrestrial Hydrometeorology, Shuttleworth, (Chapter 2,3)
  Hydrology, Bras (Chapter 5)
  Chow (Chapter 3)

## Slide 6: Evapotranspiration – Fundamentals
Flux of water from the land surface back to the atmosphere
About 61% of precipitated water is evapotranspired back to the atmosphere
Evaporation and Transpiration are both driven by energy from the sun
Notes: Flux of water from the land surface back to the atmosphere
About 61% of precipitated water is evapotranspired back to the atmosphere
Evaporation and Transpiration are both driven by energy from the sun

## Slide 8: Unsaturated Zone Characteristics – Components
Sanford & Selnick, JAWRA 2012

## Slide 10: Why do we care about ET?
E and T are happening all the time…
  In plants, T  Life
Globally, ~62% of precip goes through ET to get back to the atmosphere
  42% is T
  3% is open-water E
  Rest is interception E and bare soil E
They are invisible fluxes!
These fluxes have associated energy transfers
Human water use influences ET across irrigated lands, etc.
Notes: E and T are happening all the time…
  In plants, T  life
Globally, ~62% of precip goes through ET to get back to the atmosphere
  42% is T
  3% is open-water E
  Rest is interception E and bare soil E
They are invisible fluxes!
These fluxes have associated energy transfers… (recall lv)
Human water use influences ET across time and space
  Irrigated lands, etc.

## Slide 11: Recall global energy fluxes…
ET is 80 W/m2
Incoming Solar Radiation is 341 W/m2
ET is 23.5% of incoming solar!
Notes: ET is 80 W/m2
Incoming Solar Radiation is 341 W/m2
ET is 23.5% of incoming solar!

## Slide 15: Evaporation – Basics
Based on an energy balance, evaporation is the natural phase change of liquid water to water vapor
The energy balance is driven by the input of solar radiation
Energy balance basics:
  All objects contain sensible heat
  Substances use latent heat (l) during phase changes
Notes: Based on an energy balance, evaporation is the natural phase change of liquid water to water vapor
The energy balance is driven by the input of solar radiation
Energy balance basics:
  All objects contain sensible heat
  Substances use latent heat (l) during phase changes

## Slide 16: Evaporation – Potential Evaporation
Potential Evaporation Ep [L/T] is the quantity of water evaporated per unit area, per unit time from an idealized, extensive free-water surface under existing atmospheric conditions.
Assumptions
No limitation of water
ignore influence of evaporation on meteorological conditions
E < Ep
Notes: Potential Evaporation Eo [mm/d] is the quantity of water evaporated per unit area, per unit time from an idealized, extensive free water surface under existing atmospheric conditions.
Assumptions
No shortage of water
Ignore influence of evaporation on meteorological parameters
AND, E <= Ep

## Slide 17: Evaporation – Physics of Evaporation & Energy Exchange
Conservation of mass
Conservation of energy
Ideal gas law as it pertains to water vapor
Latent heat of phase change (vaporization)
Turbulent transfer near the ground

## Slide 18: Evaporation – Conceptual molecular model
Env. Hydrol., Figure 4.2

## Slide 22: Evaporation – Conceptual molecular model
Requirements –
Water availability: soil moisture or open water is available to be evaporated
Energy input: net radiation drives the evolution of surface temperature, which drives energy state of surface and difference from air (energy gradient).
Transport of vapor away from surface: aerodynamic resistance regulates transport of vapor (or energy) away from the surface via turbulent motions.
Notes: Requirements –
Water availability: soil moisture or open water is available to be evaporated
Energy input: net radiation drives the evolution of surface temperature, which drives energy state of surface and difference from air (energy gradient).
Transport of vapor away from surface: aerodynamic resistance regulates transport of vapor (or energy) away from the surface via turbulent motions.

## Slide 23: Evaporation – Energy Balance Method
According to the first law of thermodynamics, the net radiant energy received at the land surface must be conserved
All matter has internal energy due to the kinetic and potential energy associated with individual molecules.
Notes: According to the first law of thermodynamics, the net radiant energy received at the land surface must be conserved.
All matter has internal energy due to the kinetic and potential energy associated with individual molecules.

## Slide 24: Evaporation – Energy Balance Model
To ‘free’ the molecules, they must overcome the latent heat of vaporization which is the quantity of heat energy needed to break the hydrogen bonds between molecules
Notes: FILL IN EQNS
To ‘free’ the molecules, they must overcome the latent heat of vaporization, lv, which is the quantity of heat energy needed to break the hydrogen bonds between molecules.

## Slide 25: Evaporation - Latent Heat Exchange
Evaporation  transfer of heat out of the evaporating surface (i.e., the surface cools)
Condensation  transfer of heat into the air (i.e., the air warms)
Condensation on the surface of an object is always accompanied by a transfer of heat to the surface (i.e., the surface warms)
Notes: Evaporation  transfer of heat out of the evaporating surface (i.e., the surface cools)
Condensation  transfer of heat into the air (i.e., the air warms)
Condensation on the surface of an object is always accompanied by a transfer of heat to the surface (i.e., the surface warms)

## Slide 26: Evaporation – Latent Heat Exchange
The latent heat transfer rate is:
  Where, E is the rate of evaporation [LT-1]; rw is the density of water [ML-3]
But, lv (MJ/kg) changes as a function of the temperature of the evaporating surface (Ts, ºC):
lE = lv rw E
lv = 2501 – 0.000236Ts
Notes: Fill in EQ 3.17 in Dingman
Fill in EQ 3.18 in Dingman (note the units)

## Slide 34: Evaporation & Heat-Exchange Processes 5. Bowen Ratio, Evaporative Fraction…
Hornberger et al., 1998
Consider a simple energy balance:
Notes: FILL IN 2 EQNS

## Slide 35: Evaporation & Heat-Exchange Processes 5. Bowen Ratio, Evaporative Fraction…
Max E corresponds to max Rn
Also note that at start, soil was saturated, so during day 1, lE is big (lots of ET).
On day 2, lE decreases as the soil dries.
Hornberger et al., 1998
lE

## Slide 36: Evaporation & Heat-Exchange Processes 5. Bowen Ratio, Evaporative Fraction…
ET is approximately PET at saturated soil conditions
Why this relationship?
Hornberger et al., Figure 2.12

## Slide 37: Evaporation & Heat-Exchange Processes 5. Bowen Ratio, Evaporative Fraction…
Bowen ratio – ratio of sensible heat to latent heat
And, g is defined as the psychrometric constant:
It’s not actually constant, g = f (p, elevation, T)
Notes: Bowen ratio – ratio of sensible heat to latent heat
FILL IN EQ. 6.19, 6.20 from DINGMAN
And, g is defined as the psychrometric constant: FILL IN EQ. 6.21 from DINGMAN
It’s not actually constant, g = f(p, elevation, T)

## Slide 38: Evaporation & Heat-Exchange Processes 5. Bowen Ratio, Evaporative Fraction…
We can also define the evaporative fraction (EF), of ET as:
This is the ratio of latent heat flux to total turbulent heat flux
Notes: We can also define the evaporative fraction (EF), of ET as:
FILL IN EQ 6.22 from DINGMAN
This is the ratio of latent heat flux to total turbulent heat flux…

## Slide 39: Evaporation & Heat-Exchange Processes 6. Full Energy Balance
We can write a full energy balance (on average) for evaporation/condensation as:
evaporation
net shortwave radiation input
net longwave radiation input
ground heat flux
sensible heat flux
net input associated with inflows and outflows of water
change in the amount of heat stored per unit area over some time scale.
Notes: We can write a full energy balance (on average) for evaporation/condensation as:
Where, lE is evaporation
K – net shortwave radiation input
L – net longwave radiation input
G – net output via conduction downward from the surface
H – net output of sensible heat with the atmosphere
Aw - net input associated with inflows and outflows of water
DU/Dt = change in the amount of heat stored in the body per unit area over some time scale.
THUS, evaporation must be balanced by some combination of heat inputs from radiation or sensible yheat from the atm, ground, water, or loss of heat energy in the evaporating body…
We can write a full energy balance (on average) for evaporation/condensation as:
𝜆𝐸=𝐾+𝐿−𝐺−𝐻+𝐴_𝑤−Δ𝑈/Δ𝑡
Where, lE is evaporation
K – net shortwave radiation input
L – net longwave radiation input
G – net output via conduction downward from the surface
H – net output of sensible heat with the atmosphere
Aw - net input associated with inflows and outflows of water
DU/Dt = change in the amount of heat stored in the body per unit area over some time scale.
THUS, evaporation must be balanced by some combination of heat inputs from radiation or sensible yheat from the atm, ground, water, or loss of heat energy in the evaporating body…

## Slide 40: Classification of ET Processes
Type of surface – open water, bare soil, leaf or canopy, reference crop, land region
Availability of water – unlimited vs. limited by stomata openings (plants)
Stored-energy use – DU may change a lot or a little
Water-advected energy use – Aw may be big or small
Notes: Type of surface – open water, bare soil, leaf or canopy, reference crop, land region…
Availability of water – unlimited vs. limited by stomata openings (plants)
Stored-energy use – DU may change a lot or a little.
Water-advected energy use – Aw may be big or small...

## Slide 41: Classification of ET Processes
ET Type | Type of Surface | Availability of water to surface | Stored Energy Use | Water-Advected Energy Use
Free-Water E | Open water | unlimited | none | none
Lake E | Open water | unlimited | maybe | maybe
Bare-soil E | Bare soil | Limited to unlimited | negligible | none
Transpiration | Leaf or canopy | limited | negligible | none
Interception E | Leaf or canopy | unlimited | negligible | none
PET | Reference crop | Limited to air, unlim to plants | none | none
AET | Land area | Varies in time, space | negligible | none
Notes: FILL IN FROM TABLE 6.1, p. 257

## Slide 46: Free-Water & Lake Evaporation Pan Evaporation Measurement
Direct Measurement
  Evaporation pans
  Mass balances
Estimates from Met Data
U.S. Weather Bureau Class A Evaporation Pan is 1.2 m in diameter and 250 mm deep. When installed it is elevated 150 mm off the ground. The operating water level is a depth of 175 – 200 mm. The water level in the pan is therefore kept 50 – 75 mm from the rim. A stilling well located on the side of the Class A Pan has a level sensor and is used to record the water depth. The measurements can be taken automatically. - British Columbia Ministry of Ag., Food, & Fisheries
E = Dstage – Precip
S2 = S1 – E + Precip

## Slide 47: Evaporation from a Pan
National Weather Service Class A type
Installed on a wooden platform in a grassy location
Filled with water to within 2.5 inches of the top
Evaporation rate is measured by manual readings or with an analog output evaporation gauge
Mass balance equation
Pans measure more evaporation than natural water bodies because:
  1) less heat storage capacity (smaller volume)
  2) heat transfer
  3) wind effects

## Slide 48: Evaporation pans are not all equal
Env. Hydrol., Figure 4.9

## Slide 53: Evaporation & Heat-Exchange Processes 1. Vapor-Pressure Relations
The vapor pressure (e) of an evaporating surface is
  Where, e*(Ts) is approximated by (T = Ts):
Above this surface,
  Where, e*[T(z)] = e*(z) is the saturation vapor pressure at the air temperature
es = e*(Ts)
e*(T)
e(z) = RH(z) x e*[T(z)]
Notes: The vapor pressure (e) of an evaporating surface is
  FILL IN EQ 6.1 from DINGMAN
  Where, e*(Ts) is approximated by:
  FILL IN EQ 6.2 from DINGMAN
Above this surface,
  FILL IN EQ 6.3 from DINGMAN
  Where, e*[T(z)] = e*(z) is the saturation vapor pressure at the air temperature

## Slide 54: Evaporation & Heat-Exchange Processes 1. Vapor-Pressure Relations
One approach to estimating ET is to evaluate the derivative of the e* curve:
e*
Notes: One approach to estimating ET is to evaluate the derivative of the e* curve:
FILL IN EQ 6.4 from DINGMAN

## Slide 55: Vapor Transport
Td
ea
Ta
es(Ta)
The vapor pressure at the surface is es(Ts); the vapor pressure of the overlying air is relative humidity times es(Ta). The rate of evaporation is proportional to es – ea.

## Slide 57: Turbulent transfer near the ground
From Chow et al., 1988
=0.4 von Karman

## Slide 58: Evaporation & Heat-Exchange Processes 2. Evaporation as a Diffusive Process
Recall Fick’s Law:
  The diffusivity term (DS) characterizes vertical transport by turbulent eddies that result from: (1) friction acting on horizontal winds, and (2) buoyancy due to heating of the surface
  If buoyancy effects are minimal (i.e., neutral stability), we can use the Prandtl-von Karman velocity distribution to characterize u(z):
= 0.4
zd is zero-plane displacement height
z0 is roughness height
Notes:   The diffusivity term (DS) characterizes vertical transport by turbulent eddies that result from: (1) friction acting on horizontal winds, and (2) buoyancy due to heating of the surface
  If buoyancy effects are minimal (i.e., neutral stability), we can use the Prandtl-von Karman velocity distribution to characterize u(z):
  FILL IN EQ 6.6 from DINGMAN

## Slide 59: Evaporation & Heat-Exchange Processes 2. Evaporation as a Diffusive Process
Recall that we can estimate evaporation rate with a mass-transfer equation:
  Now, if we set u at surface to 0, and es as the vapor pressure of the evaporating surface, we get

## Slide 60: Evaporation & Heat-Exchange Processes 2. Evaporation as a Diffusive Process
And, with the several constants involved, we can simplify to this as a function of zm and saturated vapor pressure at the surface (es*):
We can also define a water-vapor transfer coefficient, KE to then show that:
  Thus, E ∝ e, u
Notes: And, with the several constants involved, we can simplify to this as a function of zm and saturated vapor pressure at the surface (es*):
We can also define a water-vapor transfer coefficient, KE to then show that:
  FILL IN EQ 6.12 from DINGMAN
  Thus, E ∝ e, u
And, with the several constants involved, we can simplify to this as a function of zm and saturated vapor pressure at the surface (es*):
𝐸=1.20𝑥〖10〗^(−6) (𝑢(𝑧_𝑚)∙[𝑒_𝑠^∗−𝑒(𝑧_𝑚 )])/[𝑙𝑛((𝑧_𝑚−𝑧_𝑑)/𝑧_0 )]^2
We can also define a water-vapor transfer coefficient, KE to then show that:
  FILL IN EQ 6.12 from DINGMAN
  Thus, E ∝ e, u

## Slide 61: Evaporation & Heat-Exchange Processes 3. Latent Heat Exchange
Recall:
Latent Heat of Vaporization
Latent Heat of Fusion (melting)
vapor
liquid
solid

## Slide 62: Evaporation & Heat-Exchange Processes 4. Sensible Heat Exchange
Also based on Fick’s law:
  We can further simplify, but ultimately, the sensible heat flux is proportional to the product of the near surface T and u:
H = KH ∙ u(zm) ∙ [Ts - T(zm)]
Notes: Also based on Ficks law:
  We can further simplify, but ultimately, the sensible heat flux is proportional to the product of the near surface T and u:
  FILL IN EQ 6.18 from DINGMAN
Also based on Ficks law:
𝐻=−𝜌_𝑎∙𝑐_𝑝 (𝜅^2 [𝑢(𝑧_2 )−𝑢(𝑧_1 )]∙[𝑇(𝑧_1 )−𝑇(𝑧_2 )])/[𝑙𝑛((𝑧_2−𝑧_𝑑)/(𝑧_1−𝑧_𝑑 ))]^2
  We can further simplify, but ultimately, the sensible heat flux is proportional to the product of the near surface T and u:
  FILL IN EQ 6.18 from DINGMAN

## Slide 63: Mass Transfer / Aerodynamic Method

## Slide 64: Bowen Ratio
- psychrometric constant
Using standard values for P and v the value is 0.066 [kPa/K]

## Slide 65: Bowen Ratio Energy Balance Method
A = Rn – G = LE + H = LE(1+)

## Slide 67: Free-Water & Lake Evaporation
Theoretical concept of free-water evaporation, aka Potential Evaporation (E0) - rate of evaporation that would occur from an extended open-water surface under current meteorologic conditions without heat-storage or water-advected energy effects
Lake evaporation – is E0 adjusted for advection and heat-storage effects in a given water body
Notes: Theoretical concept of free-water evaporation, aka Potential Evaporation (E0) - rate of evaporation that would occur from an extended open-water surface under current meteorologic conditions without heat-storage or water-advected energy effects
Lake evaporation – is E0 adjusted for advection and heat-storage effects in a given water body…

## Slide 68: Free-Water & Lake Evaporation Eddy Correlation
Theoretically, based on trying to quantify turbulent fluxes of moisture in the air:
Practically, it’s mathematically complex and tends to yield evaporation estimates that are ~80% of rates calculated by energy balance approaches
Notes: Theoretically, based on trying to quantify turbulent fluxes of moisture in the air:
FILL IN EQ. 6.24
Practically, it’s mathematically complex and tends to yield evaporation estimates that are ~80% of rates calculated by energy balance approaches

## Slide 69: Eddy Correlation Approach
is vertical wind velocity component fluctuation
is specific humidity fluctuation

## Slide 70: Free-Water & Lake Evaporation Mass Transfer
Theoretically, based on fundamental mass transfer (from a few slides ago):
Where, b0 accounts for free-convection and b1 depends on the height and location at which u and e are measured…
If buoyancy effects are negligible, b0 = 0 and b1 = KE
E0 = [b0 + b1 ∙ u(zm)] ∙ [es – e(zm)]
Notes: Theoretically, based on fundamental mass transfer (from a few slides ago):
FILL IN EQ 6.25
Where, b0 accounts for free-convection and b1 depends on the height and location at which u and e are measured…
If buoyancy effects are negligible, b0=0 and b1 = KE
Theoretically, based on fundamental mass transfer (from a few slides ago): 𝐸= 𝐾_𝐸∙𝑢(𝑧_𝑚 )∙[𝑒_𝑠−𝑒(𝑧_𝑚 )]
FILL IN EQ 6.25
Where, b0 accounts for free-convection and b1 depends on the height and location at which u and e are measured…
If buoyancy effects are negligible, b0=0 and b1 = KE

## Slide 71: Free-Water & Lake Evaporation Mass Transfer
We can further simplify by setting z0 for water surfaces to 5x10-4m, and zd = 0m, and zm = 2m
However, free convection plays a role… Example: if Twater > Tair then, water warms air, which rises, causing turbulent transport of water vapor + heat away from the surface
Notes: We can further simplify by setting z0 for water surfaces to 5x10-4m, and zd = 0m, and zm = 2m
However, free convection plays a role… Example: water temp > air temp leads to warm air and then warm air rises, causing turbulent transport of water vapor and heat away from the surface
We can further simplify by setting z0 for water surfaces to 5x10-4m, and zd = 0m, and zm = 2m
𝐸_0=1.78×〖10〗^(−8)∙𝑢(2𝑚)∙[𝑒_𝑠−𝑒(2𝑚)]
However, free convection plays a role… Example: water temp > air temp leads to warm air and then warm air rises, causing turbulent transport of water vapor and heat away from the surface

## Slide 72: Free-Water & Lake Evaporation Mass Transfer
Practically, the method is very sensitive to how you handle b0 and b1 (KE) and how you handle the lake heat content
The method is derived for instantaneous rate of E under given instantaneous values, but is often applied over some time period (i.e., not instantaneous)
Notes: Practically, the method is very sensitive to how you handle b0 and b1 (KE), and how you handle the lake heat content
The method is derived for instantaneous rate of E under given instantaneous values, but is often applied over some time period (i.e., not instantaneous)

## Slide 73: Free-Water & Lake Evaporation Energy Balance
Solving for a rate, E yeilds:
By definition then, E0 is calculated as
And sensible heat loss is replaced by:
H = BlE
Notes: We can further simplify by setting z0 for water surfaces to 5x10-4m, and zd = 0m, and zm = 2m
However, free convection plays a role… Example: water temp > air temp leads to warm air and then warm air rises, causing turbulent transport of water vapor and heat away from the surface
We can further simplify by setting z0 for water surfaces to 5x10-4m, and zd = 0m, and zm = 2m
𝐸_0=1.78×〖10〗^(−8)∙𝑢(2𝑚)∙[𝑒_𝑠−𝑒(2𝑚)]
However, free convection plays a role… Example: water temp > air temp leads to warm air and then warm air rises, causing turbulent transport of water vapor and heat away from the surface

## Slide 74: Free-Water & Lake Evaporation Penman model
What if we could combine the mass transfer and energy balance approaches?
N.B. – no reliance on water surface temp!

## Slide 75: Combination Method Concepts
Rn – G = LE + H
Ta
es(Ta)
Ts
es(Ts)

## Slide 76: Combination or Penman Method

## Slide 77: Priestley Taylor Method
This is also sometimes taken as an estimate of equilibrium potential evapotranspiration for well watered surface

## Slide 78
From Brutsaert, 2005

## Slide 79
From Brutsaert, 2005

## Slide 80: Method Information Requirements
RN
Mass Transfer
Bowen Ratio / Energy Balance
Combination

## Slide 81: Summary of ET Equations
Bowen Ratio
Mass Transfer
Combination
Priestly Taylor
What happens in these equations if the wind speed doubles?

## Slide 82: Evapotranspiration Feedbacks
Conditions adjust to varying inputs. Calculations can interpret adjustments, but should not be used to predict the effect of changing one variable without considering the adjustments of connected variables
Rn
G
+
+
+
-
-
-

## Slide 83: Free-Water & Lake Evaporation Penman model
How well does it work?
Compared to pan evaporation measurements, it works pretty well.
Notes: Rearrange the mass-transfer equation for sensible heat into:
Rearrange the SEB into: H = Rn + LE - G and substitute into above eqn

## Slide 85: Soil Water Evaporation
Stage 1. For soils saturated to the surface, the evaporation rate is similar to surface water evaporation.
Stage 2. As the surface dries out, evaporation slows to a rate dependent on the capillary conductivity of the soil.
Stage 3. Once pore spaces dry, water loss occurs in the form of vapor diffusion. Vapor diffusion requires more energy input than capillary conduction and is much, much, slower.
Note that for soils under a forest canopy, Rnet, vapor pressure deficit, and turbulent transport (wind) are lower than for exposed soils.

## Slide 87: Soil water loss with different cover
Forest Soil

## Slide 88: Rooting Depth Effects
Surface
2 months later

## Slide 89: Bare Soil Evaporation
Water near the surface is evaporated from the pores between soil grains

## Slide 90: Bare Soil Evaporation occurs in stages…
Stage 1 – evaporation from wet soil;
  controlled by surface energy balance and mass transfer conditions at the surface
  rate is ~ that of free-water evaporation
  water lost from soils is replaced by other subsurface water
Notes: Stage 1 – evaporation from wet soil;
  controlled by surface energy balance and mass transfer conditions;
  rate is ~ that of free-water evaporation
  water lost from soils is replaced by other subsurface water

## Slide 91: Bare Soil Evaporation occurs in stages…
Stage 2 – “soil controlled”, rate is lower than stage 1 (0.7 – 3.5 mm/d)
  controlled by water movement in soil pores (vapor diffusion and film flow)
Notes: Stage 2 – “soil controlled”, rate is lower than stage 1 (0.7 - 3.5 mm/d)
  controlled by water movement in soil pores (vapor diffusion and film-flow)

## Slide 92: Evaporation
Transfer of H2O from liquid to vapor phase
  Diffusive process driven by
    Saturation (vapor density) gradient ~ (rs – ra)
    Aerial resistance ~ f(wind speed, temperature)
    Energy to provide latent heat of vaporization (radiation)
Transpiration is plant mediated evaporation
  Same result (water movement to atmosphere)
Summative process = evapotranspiration (ET)
  Dominates the fate of rainfall
    ~ 95% in arid areas
    ~ 70% for all of North America

## Slide 93: Evapo-Transpiration
ET is the sum of
  Evaporation: physical process
  from free water
    Soil
    Plant intercepted water
    Lakes, wetlands, streams, oceans
  Transpiration: biophysical process modulated by plants (and animals)
    Controlled flow through leaf stomata
    Species, temperature and moisture dependent

## Slide 94
Four Requirements for ET
Vapor Pressure Gradient
Energy
Water
Wind
NP
TP

## Slide 95
Evapotranspiration has Multiple Components

## Slide 96: Transpiration (Dingman P 294)
Absorption of soil water by roots
Translocation through plant vascular system
Stomata open to take in CO2 for photosynthesis and water is lost by transpiration
Plants control stomata openings to regulate photosynthesis and transpiration
from http://www.trunity.net/envsciClone/articles/view/177351/?topic=81575

## Slide 97: Transpiration
Plant mediated diffusion of soil water to atmosphere
  Soil-Plant-Atmosphere Continuum (SPAC)
CO2
H2O
1 : 300
Transpiration and productivity are tightly coupled
Transpiration is the primary leaf cooling mechanism under high radiation
Provides a pathway for nutrient uptake and matrix for chemical reactions
Worldwide, water limitations are more important than any other limitation to plant productivity

## Slide 99: Total System ET – Ordered Process
Intercepted Water  Transpiration  Surface Water  Soil Water
Why?
Implications for:
  Cloud forests
  Understory vegetation in wetlands
  Deep rooted arid ecosystems

## Slide 100: Interception
Surface tension holds water falling on forest vegetation.
  Leaf Storage
    Fir 0.25”
    Pines 0.10”
    Hardwoods 0.05”
    Litter 0.20”
    SP Plantations 0.40”.
Interception Loss (% of rainfall)
Hardwoods 10-20% (less LAI)
Conifers 20-40%
Mixed slash and Cypress Florida Flatwoods 20%

## Slide 101
Transpiration Dominates the Evaporation Process
Large surface area
More turbulent air flow
Conduits to deeper moisture sources
Hardwood ~80%
White Pine~60%
Flatwoods ~75%
T/ET
Trees have:

## Slide 102
Cover | Evaporation | Interception | Transpiration
Forest | 10% | 30% | 60%
Meadow | 25% | 25% | 50%
Ag | 45% | 15% | 40%
Bare | 100% |  | 

## Slide 103
The driving force of transpiration is the difference in water vapor concentration, or vapor pressure difference, between the internal spaces in the leaf and the atmosphere around the leaf

## Slide 104: Transpiration
The physics of evaporation from stomata are the same as for open water. The only difference is the conductance term.
Conductance is a two step process
  stomata to leaf surface
  leaf surface to atmosphere

## Slide 105: Transpiration

## Slide 106: Stomata respond to
Light
Humidity
Water content (related to soil moisture)
Temperature
Other factors such as wind, CO2, chemicals
from http://www.ck12.org/

## Slide 108: How Does Water Get to the Leaf?
Water is PULLED, not pumped. Water within the whole plant forms a continuous network of liquid columns from the film of water around soil particles to absorbing surfaces of roots to the evaporating surfaces of leaves.
It is hydraulically connected.

## Slide 109
Even a perfect vacuum can only pump water to a maximum of a little over 30 feet. At this point the weight of the water inside a tube exerts a pressure equal to the weight of the atmosphere pushing down
> 100 meters
So why doesn’t the continuous column of water in trees taller than 34 feet collapse under its own weight? And how does water move UP a tall tree against the forces of gravity?

## Slide 110
Water is held “up” by the surface tension of tiny menisci (“menisci” is the plural of meniscus) that form in the microfibrils of cell walls, and the adhesion of the water molecules to the cellulose in the microfibrils
cell wall microfibrils of carrot

## Slide 111
Yw(soil)  -0.1 MPa
Yw (root)
 -0.5 MPa
Yw (stem)
 -0.6 MPa
Yw (small
branch)
 -0.8 MPa
Yw (atmosphere)
 -95 MPa
The SPAC (soil-plant-atmosphere continuum)

## Slide 112
Cohesion-Tension Theory:
(Böhm, 1893; Dixon and Joly, 1894)
The cohesive forces between water molecules keep the water column intact unless a threshold of tension is exceeded (embolism). When a water molecule evaporates from the leaf, it creates tension that “pulls” on the entire column of water, down to the soil.
Notes: To understand WHY the pipeline is vulnerable:
LOOK AT MECHANISM: COHESION – TENSION – THEORY
about 100 yrs ago – proposed independently by Boehm and by Dixon and Joly
Transpiration
Capillary forces – Tension – NEGATIVE PRESURE
Water is pulled up – cohesive forces between water molecules keep the water column together
Conduits are dead
Class: Tug-of-war – the air pulls on one end, the soil particles on the other end
Very simple mechanism and very cheap - driven by the sun
Once the pipeline is in place
plants don’t have to use energy for water transport
What makes the pipeline “vulnerable”?
It’s the MAGNITUDE of the NEGATIVE Xylem Pressure

## Slide 113
ET = Rain * 0.80
ET = Rain * 0.95
1,000 mm * 0.80 = 800 mm
1,000 mm * 0.95 = 950 mm
Assume Q & ΔS = 0
G = 200 mm
G = 50 mm
4x more groundwater recharge from open stands than from highly stocked plantations.
?
G = P - ET
NRCS is currently paying for growing more open stands, mainly for wildlife.

## Slide 115: Trading Environmental Priorities?
Water for Carbon
Water for Energy
Jackson et al. 2005 (Science)

## Slide 116: Canopy and atmospheric conductance
Resistance Analogy
from Shuttleworth 1993
from Dingman (2002)

## Slide 123: Penman-Monteith Model
Open water
Vegetation
Shuttleworth 4.2.27 resistance notation
D = vapor pressure deficit

## Slide 124: Soil moisture functions for actual ET
from Shuttleworth 1993
Common – consistent with “Crop factor” concept
Theoretically preferable based on resistance/conductance concept (Dingman 7-69)

## Slide 129: Water Availability: PET vs. AET
PET (potential ET) is the expected ET if water is not limiting
  Given conditions of: wind, Temperature, Humidity
AET (actual ET) is the amount that is actually abstracted (realizing that water may be limiting)
  AET = a * PET
  Where a is a function of soil moisture, species, climate
  In Florida, ~ a is unity for the summer, 0.75 otherwise
ET:PET is low in arid areas due to water limitation
ET ~ PET in humid areas due to energy limitation

## Slide 130: A Simple Catchment Water Balance
Consider the net effects of the various water balance components (esp. ET)
ET controlled by water availability and atmospheric demand
The “Budyko” Curve
  Dry conditions: when PET:P → ∞, AET:P → 1 and Q:P → 0
  Wet conditions: when PET:P → 0 AET → PET

## Slide 131: Theory vs. Real Data – Budyko curves across the world’s catchments
PET:P
AET:P

## Slide 132: Complimentary (Advection-Aridity) Approach (Dingman p314)
from Dingman (2002)