## Slide 1: Physical Hydrology & Hydroclimatology (Multiscale Hydrology)
A science dealing with the properties, distribution and circulation of water.
R. Balaji
balajir@colorado.edu
CVEN5333 http://civil.colorado.edu/~balajir/CVEN5333
Includes slides from Prof. Mike Gooseff

## Slide 2: Snow & Snomelt
Formation
Characteristics
Measurement
Distribution
Snomelt
  Energy and mass balance
Snomelt Modeling
  Physical Hydrology, Dingman (Chapter 5, Appendix D)
  Hydrology, Bras (Chapter 6)
  Prof. Mark Serreze, CU Geography & Prof. Tarboton, USU
  Comet – MedEd
  http://www.comet.ucar.edu/class/hydromet/09_Oct13_1999/docs/cline/comet_snowhydro/index.htm
  Utah Energy Balance Model
  http://www.neng.usu.edu/cee/faculty/dtarb/snow/snow.html

## Slide 4: The “Snow Cycle”
Formation in the atmosphere
Snowfall
Snowpack development, metamorphosis
Snow ablation (melt, sublimation)
…the rest of the hydrologic cycle...

## Slide 5: Hydrologic Significance of Snow
~ 67% of world’s fresh water found in snow and ice
Only 3% of permanent snow & ice is located outside the polar regions
~ 60 years of earth annual ppt is locked up in snow and ice
~ 50% of ice & snow outside the poles is in the Himalayas; also critical to Europe, Asia, S. Am., Western US
  90% of runoff in N. AZ, NM due to rain-on-snow events
~80-85% of Colorado River Basin Runoff from snowmelt

## Slide 7: Atmospheric Snow Crystal Formation
Ice Nucleation - the condensation of water vapor from supersaturated air onto aerosol particles (0.01 - 1 mm in size) must first occur
Water molecules are able to “escape” from a liquid surface more easily than from an ice surface.
So, for a given freezing temperature, e over water is greater than the e over ice.
SnowCrystals.com
Notes: Ice Nucleation - the condensation of water vapor from supersaturated air onto aerosol particles (0.01 - 1 mm in size) must first occur
Water molecules are able to “escape” from a liquid surface more easily than from an ice surface.
So, for a given freezing temperature, e over water is greater than the e over ice.

## Slide 8: Ice Nucleation 2 types
Homogeneous – spontaneous process that requires no nuclei; it’s the formation of ice crystals from supercooled water droplets that occurs around -40oC
Heterogeneous –
  Deposition Nucleus (Vapor Deposition)
  Contact Nucleation (Riming)
  Aggregation
Notes: Homogeneous – spontaneous process that requires no nuclei; it’s the formation of ice crystals from supercooled water droplets that occurs around -40oC
Heterogeneous –
  Deposition Nucleus (Vapor Deposition)
  Contact Nucleation (Riming)
  Aggregation

## Slide 9: Heterogeneous Ice Nucleation Vapor Deposition
Diffusion of water vapor onto an ice crystal surface
Undersaturated wrt water, oversaturated wrt ice
Ice crystals grow at the expense of water droplets (which haven’t yet frozen)
The Avalanche Handbook, 1993
Notes: Diffusion of water vapor onto an ice crystal surface
Undersaturated wrt water, oversaturated wrt ice
Ice crystals grow at the expense of water droplets (which haven’t yet frozen)

## Slide 10: Heterogeneous Ice Nucleation Riming
Supercooled water droplets (liquid) attach to snow grain by contact
Typical formation process of snowflakes
Can result in graupel, hail or sleet
The Avalanche Handbook, 1993
Droplet
Droplet
Droplet
Notes: Supercooled water droplets (liquid) attach to snow grain by contact
Typical formation process of snowflakes
Can result in graupel, hail or sleet

## Slide 11: Typical Explanation of Crystal Formation
Notes: http://www.thenakedscientists.com/HTML/articles/article/science-of-snowflakes/

## Slide 12: Crystal Growth
The growth of snow crystals depends on a balance between faceting and branching.
Faceting tends to make simple flat surfaces
Branching tends to make more complex structures.
SnowCrystals.com
Notes: The growth of snow crystals depends on a balance between faceting and branching.
Faceting tends to make simple flat surfaces
Branching tends to make more complex structures.

## Slide 13: Crystal Growth function of T & e
SnowCrystals.com

## Slide 14: Snow Crystal Formation
Dendrite
Sectored Plate
Dendritic
Sectored Plate
Prism
(Column)
Needle
A-Axis
Growth
C-Axis
Growth

## Slide 16: Snow Pack Characteristics

## Slide 17: Snow Pack Characteristics
What is a Snow Pack?
  Porous Medium
    ice + air (+ liquid water)
  Generally composed of layers of different types of snow
    more or less homogeneous within one layer
  Ice is in form of crystals and grains that are usually bonded together
    forms a texture with some degree of strength

## Slide 18: Snow Pack Characteristics
Primary physical characteristics of deposited snow
Density
Grain Size
Grain Shape
Liquid Water Content
Impurities
Strength
Hardness
Depth
Water Equivalent
Albedo
Temperature

## Slide 19: Snow Pack Characteristics
Snow Water Equivalent (SWE)
  The height of water if a snow cover is completely melted, on a corresponding horizontal surface area.
    Snow Depth x (Snow Density/Water Density)

## Slide 20: Density of Snow Cover
Snow Type
Density (kg/m3)
Wild Snow
Ordinary new snow immediately
after falling in still air
Settling Snow
Average wind-toughened snow
Hard wind slab
New firn snow
Advanced firn snow
Thawing firn snow
10 to 30
50 to 65
70 to 90
280
350
400 to 550
550 to 650
600 to 700
Snow Depth for
One Inch Water
98” to 33”
20” to 15”
14” to 11”
3.5”
2.8”
2.5” to 1.8”
1.8” to 1.5”
1.6” to 1.4”

## Slide 21: Snow Pack Characteristics
Grain Shape
  The “Smoking Gun”
  One of the most tell-tale characteristics that allows inference of snow pack evolution
  Morphological classification of snow grains
    several have been developed

## Slide 22: Snow Pack Characteristics
General Attributes of Grain Shape
  Appearance:
    solid, hollow, broken, abraded, partly melted, rounded, angular
  Surface:
    rounded facets, stepped or striated, rimed
  Interconnections:
    bonded, unbonded, bond size, clustered, number of bonds per grain, oriented texture, arranged in columns

## Slide 23: Snow Grain Shapes
Rime on Plate Crystal
Early Rounding
Faceted Growth
Early Sintering (Bonding)
Wind-Blown Grains
Melt-Freeze with
No Liquid Water
Melt-Freeze with
Liquid Water
Faceted Layer Growth
Hollow, Faceted Grain
(Depth Hoar)

## Slide 24: Electron Microscopy of Snow Crystals

## Slide 25: Snow Pack Characteristics
Grain Size
  The average size of the characteristic grains within a mass of snow
    its greatest extension in mm
Term
Size (mm)
Fine
Medium
Coarse
Very Coarse
Extreme
Very Fine
< 0.2
0.2 - 0.5
0.5 - 1.0
1.0 - 2.0
2.0 - 5.0
> 5.0

## Slide 26: Snow Pack Characteristics
Liquid Water Content
  Wetness, Percentage by volume
Term
Remarks
Moist
Wet
Very Wet
Slush
Dry
Approximate Range
Usually T < 0oC, but can occur at any temperature up to 0oC. Little tendency for snow grains to stick together.
T = 0oC. The water is not visible even at 10x magnification. Has a distinct tendency to stick together.
T = 0oC. The water can be seen at 10x magnification by its miniscus between grains, but cannot be pressed out by squeezing snow (pendular regime).
T = 0oC. The water can be pressed out by squeezing snow, but there is an appreciable amount of air (funicular regime).
T = 0oC. The snow is flooded with water and contains a relatively small amount of air.
<3%
3-8%
8-15%
>15%
0%

## Slide 27: Snow Characteristics
Temperature
  Two basic situations:
    Variation in temperature between the top of the snow pack and the ground
      Temperature Gradient
      Largely determined by thickness of snow pack and the mean snow surface temperature
        Base of snow pack is usually near 0oC
    No temperature gradient
      Isothermal

## Slide 28: Snow Characteristics
Diurnal Temperature Gradients

## Slide 32: Definitions and Terms
Snow: porous form of solid water of relatively low density. It is an aggregate of delicately skeletal ice crystals formed in the atmosphere through sublimation
  There are many forms of ice crystals; more than 6,000 have been mapped and several classification schemes developed

## Slide 33: Snow Classification
Courtesy CRREL - http://www.crrel.usace.army.mil/alaska-office/snoclass.html

## Slide 34: Snow Measurement

## Slide 37: Snow Measurement
Ground Observations
  Snow Water Equivalent (SWE)
    Snow Pillows
      SNOTEL Sites (Western U.S.)
    Snow Courses
      Transects with snow depth and density
    Snow Tubes/Cutters
      measure volume and mass of snow cores
    Snow Pits
      Measure vertical profiles of SWE, and other snow pack variables.

## Slide 38: Snow Measurement
Grain Size
Hardness
Density
Depth
Temperature
Chemistry
Stratigraphy

## Slide 40: Snow survey
Snow tube field survey
  Depth of snow
  Length of core
  Weight of empty tube
  Weight of tube + core
  Water content
    (tube + core) - tube
  Density
    WC / snow depth
Courtesy http://www.gi.alaska.edu/alison/ALISON_measures.html

## Slide 41: Snow Survey –Manual Approach
http://www.wcc.nrcs.usda.gov/factpub/sect_4a.html
Filling out the sheet:
Examples: WE = (125 – 67) = 58
(122 – 67) = 55
Examples: density = 58/151 = 0.38
55/162 = 0.34

## Slide 42: Snow Survey - SNOTEL
Brooklyn Lake SNOTEL site - http://www.wcc.nrcs.usda.gov

## Slide 43: Where do I Get Data?
http://www.wcc.nrcs.usda.gov/snow/ - online source for SNOTEL data
  Example

## Slide 47: Other ways to measure snow
Ultrasonic Snow Depth Sensor
  Inexpensive
  Remote sensing instrument
Rain/Snow Station Standpipe
  12” standpipe
  Above snow depth
  Glycol in top; tipping bucket in the bottom
http://www.rickly.com/

## Slide 48: Snow Measurement
Airborne Snow Survey Program
  Snow Water Equivalent (SWE) estimated from attenuation of naturally occurring terrestrial gamma radiation.
    Typical flight line is 16 km long, measuring a ground swath 3000 m wide.
      Measures average SWE over area of ~5 km2
    1800 flight lines throughout coterminous U.S.
    Two twin-engine aircraft fly ~900 lines/year.

## Slide 49: Snow Measurement
Airborne Snow Survey Program

## Slide 50: Snow Measurement
Airborne Snow Survey Program

## Slide 51: Snow Measurement
Airborne SWE Measurement Theory
  Airborne SWE measurements are made using the following relationship:
Where:
C and C0 = Uncollided terrestrial gamma count rates over snow and dry, snow-free soil,
M and M0 = Percent soil moisture over snow and dry, snow-free soil,
A = Radiation attenuation coefficient in water, (cm2/g)

## Slide 52: Snow Measurement
Airborne SWE: Accuracy and Bias
Airborne measurements include ice and standing water that ground measurements generally miss.
RMS Agricultural Areas: 0.81 cm
RMS Forested Areas: 2.31 cm

## Slide 53: Airborne Snow Survey Products

## Slide 54: Airborne Snow Survey Products
.B GAMMA 990120 /SAIRF/SWIRF
:TO ------ Service Hydrologist (Please give HARDCOPY to SH)
:FROM ---- Tom Carroll, (612) 361-6610 ext 225, Minneapolis, Minnesota
:Visit our web page at www.nohrsc.nws.gov
:SUBJECT - AIRBORNE SNOW WATER EQUIVALENT DATA 990120222453
:-----------------------------------------------------------------------
: Total No. of flight lines sent = 10
:-----------------------------------------------------------------------
:Line Survey %SC SWE SWE %SM Est Fall %SM Pilot
:No. Date (in) (35%) (M) Typ Date (F) Remarks
:=======================================================================
MI113 DY990120 / 100 / 1.8 : 1.2, 25 SE 0 , 25 OLD CRUSTY SNOW
MI114 DY990120 / 100 / 2.3 : 1.7, 25 SE 0 , 25
MI115 DY990120 / 100 / 0.8 : 0.3, 25 SE 0 , 25 TOWN LINE RVR FRZ
MI116 DY990120 / 100 / 0.7 : 0.2, 25 SE 0 , 25 HOUGHTON LAKE FROZEN
MI117 DY990120 / 100 / 1.8 : 1.3, 25 SE 0 , 25
MI118 DY990120 / 100 / 1.6 : 1.0, 25 SE 0 , 25
MI121 DY990120 / 100 / 1.6 : 1.0, 25 SE 0 , 25 MUSKEGON RVR OPEN 90
MI123 DY990120 / 100 / 1.8 : 1.3, 25 SE 0 , 25
MI124 DY990120 / 100 / 1.9 : 1.4, 25 SE 0 , 25 TWIN RVR PRTLY OPN
MI138 DY990120 / 100 / 3.1 : 2.6, 25 SE 0 , 25
.END
Conditions on the ground observed over the survey area were of complete
snow cover with frozen lakes and many frozen rivers. Partially open
rivers are noted in the survey line comments.
NNNN

## Slide 55: Snow Measurement
Satellite Hydrology Program
AVHRR and GOES Imaging Channels

## Slide 56: Snow Measurement
Remote Sensing of Snow Cover
(NOAA 16)

## Slide 57: Snow Measurement
NOAA-15 1.6 Micron Channel

## Slide 58: Snow Measurement
NOAA-16 1.6 Micron Channel
Visible Channel
1.6 micron Channel
SNOW
Snake River Valley, Idaho

## Slide 59: Satellite Hydrology Products
Satellite Areal Extent of Snow Cover

## Slide 60: Satellite Hydrology Products
Snow Cover by Elevation

## Slide 61: Satellite Hydrology Products
.BR MSP 990121 DM012018 DC01212234 /SAIPZ
:----------------------------------------------------------------------
:National Weather Service - Office of Hydrology
:National Operational Hydrologic Remote Sensing Center
:Chanhassen, Minnesota (612) 361-6610
:----------------------------------------------------------------------
:Satellite Areal Extent of Snow Cover (percent), Elevation Zones (1000ft)
:Composite Analysis 9901181615 - 9901211830
:
:BASIN SA Name
: ezone1 ezone2 ezone3 ezone4 ezone5
AFRA3L 0.0 : AGUA FRIA - ROCK SPRINGS
: 2.0- 5.0 5.0- 7.0
: 0.0 0.0
ALMA3L 0.0 : ALAMO RESERVIOR
: 1.2- 4.0 4.0- 6.6
: 0.0 0.0
LKPA3L 0.0 : AGUA FRIA - LAKE PLEASANT
: 1.6- 4.0 4.0- 7.0
: 0.0 0.0
Snow Cover by Basin

## Slide 62: Satellite Hydrology Products
Snow Water Equivalent (SWE) Analysis

## Slide 63: Satellite Hydrology Products
.BR MSP 990122 DM012018 DC01220349 /SWIPZ
:----------------------------------------------------------------------
:National Weather Service - Office of Hydrology
:National Operational Hydrologic Remote Sensing Center
:Chanhassen, Minnesota (612) 361-6610
:----------------------------------------------------------------------
:Estimated Snow Water Equivalent (inches), Elevation Zones (1000ft)
:Composite Analysis 9901190000 - 9901212400
:
:BASIN SW Name
: ezone1 ezone2 ezone3 ezone4 ezone5
AFMA3 0.0 : AGUA FRIA NR MAYER
: 3.6- 5.5 5.5- 7.6
: 0.0 0.0
AFPU1 7.8 : AMERICAN FORK NR AMERICAN FORK
AFRA3L 0.0 : AGUA FRIA - ROCK SPRINGS
: 2.0- 5.0 5.0- 7.0
: 0.0 0.0
ALEC2 7.1 : EAST R - ALMONT
: 8.0- 9.0 9.0-10.0 10.0-13.1
: 3.8 5.6 8.8
SWE Analysis by Basin

## Slide 64: More terms
Snowpack density (ρs): Weight per unit volume
  Fresh snow 0.1 g/cm3
  Ripe snow 0.4 g/cm3
Snow water equivalent (WE): weight of snow expressed as the depth of water over unit area
  D = depth of snow (cm)
  Ρw = density of water (g/cm3)
Ripe snowpack: snowpack that is ready to yield water. Any addition of energy or liquid water will result in a corresponding amount of snow being released as water.

## Slide 65: More Terms
Cold snow: Snow with temp < 0° C
Temperature Deficit (Ts): snowpack temp. below 0 deg. C
Thermal Deficiency: Heat required to raise the temperature of 1cm WE by 1° C
  Heat capacity of ice = 0.5 cal/g/°C
Latent Heat of Fusion: heat required to change 1g of dry snow at 0° C to a liquid state without changing the temperature
  80 cal/g = 80 cal/cm3

## Slide 66: What Happens When Water Hits the Pack?
After a cold period, the pack temp. is at or below 0°C
As it warms, some snow at surface melts…
  Water percolates into pack, hits the ice, and freezes
    Recrystallization process  films of water which increases ice crystal size in the pack
    Freezing liberates latent heat, which warms the snowpack
  Continues until the pack  0°C

## Slide 67: When the Snow Gets to 0°C
Usually is rounded ice crystals
  2-5 mm in size
  “corn snow”
  Water holding capacity and transmission properties similar to coarse sand
Percolating influx water brings pack to field capacity
  2-8% by volume
This pack is “ripe”
  Adding water or temperature will produce runoff
http://www.avalanche.org/~uac/encyclopedia/cornsnow.htm

## Slide 68: Total retention storage
Defined as the total amount of melt that must be added to a snowpack before liquid water is released
When this occurs, the snowpack is ripe

## Slide 69: Sources of energy
Radiation
  Shortwave
  Longwave
Convection – condensation melt: turbulent exchange of sensible heat and direct condensation on the surface
Rain melt: sensible heat added from rainwater
Conduction melt: heat conducted from the ground

## Slide 70: Wind Effects on Snow
Vegetation manipulation works…
  Thinning not very efficient
  Patch cuts more – up to 35% increase
  Effects last for 5+ years
Worry about watershed management goals
  Flooding
  Water quality
  Multiple use

## Slide 73: Snow Metamorphism
Why snow grains change...

## Slide 74: Snow Metamorphism
Changes in snow morphology that take place as a functions of temperature and pressure
Factors changed by metamorphism
  density -- strength
  porosity -- thermal conductivity
  reflectivity of radiant energy (albedo)

## Slide 75: Snow Metamorphism
Why does snow undergo metamorphism?
  Close to melting temperature
  Thermodynamically unstable
    large surface to volume ratio, therefore large surface free energy
      minimum surface to volume ratio is sphere
  Compaction due to overlying layers

## Slide 76: Snow Metamorphism
Two types of snow metamorphism:
  DRY
    No liquid water present
    Temperature less than 0oC
    Solid state in equilibrium with vapor
  WET
    Liquid water present
    Temperature equal to 0oC (usually)

## Slide 77: Snow Metamorphism
Dry Metamorphism:
  Driven by water vapor movement in pores
  Vapor movement is driven by vapor pressure gradient, controlled by:
    temperature: saturation vapor pressure depends on temperature; warmer areas can hold more vapor than colder areas
    radius of curvature: how curved a particular part of a snow grain is; increased radius of curvature, increased vapor density
    grain size: decreased grain size, increased radius of curvature, therefore increased vapor density

## Slide 78: Snow Metamorphism
Two Types of Dry Metamorphism:
  Equitemperature (ET)
    Destructive - destroys crystal structure
  Temperature Gradient (TG)
    Constructive - builds grains

## Slide 79: Snow Metamorphism
ET Dry Metamorphism:
    reduces surface free energy to its stable state
    Depends mostly on radius of curvature
      Convex: positive; steeper convexity is higher radius, which can hold a higher vapor density over it
      Hollows: negative
      Vapor flows along gradient - from points to hollows
    Reduces surface to volume ratio, therefore density increases (fills pore spaces)
    Structural strength increases (builds bonds)
    Rounds the snow grains

## Slide 80: ET Dry Snow Metamorphism
Reduces surface free energy to its stable state
Depends mostly on radius of curvature
  Convex: positive; steeper convexity is higher radius, which can hold a higher vapor density over it
  Hollows: negative
  Vapor flows along gradient - from points to hollows
Result: rounds the snow grains
Modified from D. Cline
  - Reduces SA:V, therefore r increases (fills pore spaces)
  - Structural strength increases (builds bonds)
The Avalanche Handbook, 1993
Notes: Reduces surface free energy to its stable state
Depends mostly on radius of curvature
  Convex: positive; steeper convexity is higher radius, which can hold a higher vapor density over it
  Hollows: negative
  Vapor flows along gradient - from points to hollows
Result: rounds the snow grains

## Slide 81: Gradients, Gradients…
Temperature gradients drive vapor pressure gradients within the snowpack
Hornberger et al., 1998, Fig 2.1

## Slide 83: Mass Movement
Vapor pressure gradients force vapor to move up toward less saturated locations of the snowpack
The Avalanche Handbook, 1993
Notes: Vapor pressure gradients force vapor to move up toward less saturated locations of the snowpack

## Slide 84: Sintering (bonding)
Water molecules move to concave regions (low vapor pressure) to form necks between grains
The Avalanche Handbook, 1993
Notes: Water molecules move to concave regions (low vapor pressure) to form necks between grains

## Slide 85: TG Dry Snow Metamorphism
TG Dry Metamorphism:
  Kinetic growth - rate of vapor transport very fast
  Builds angular, faceted grains, with poor bonding
  Resulting strength is poor, density decreases
  Must have temperature gradient of 10oC/m or greater
  Must have snow density less than 350 kg/m3
  maintain sufficient vapor flow
Modified from D. Cline
Notes: TG Dry Metamorphism:
    Kinetic growth - rate of vapor transport very fast
    Builds angular, faceted grains, with poor bonding
    Resulting strength is poor, density decreases
    Must have temperature gradient of 10oC/m or greater
    Must have snow density less than 350 kg/m3
      maintain sufficient vapor flow

## Slide 86: Wet Snow Metamorphism
Liquid water in the snow pack
  Acts like supercharged Dry ET metamorphism
  rates are accelerated
  small grains are destroyed preferentially
  large grains become rounded (equilibrium forms)
  Melting and refreezing results in large, bonded grain clusters
Notes: Liquid water in the snow pack
  Acts like supercharged Dry ET metamorphism
    rates are accelerated
    small grains are destroyed preferentially
    large grains become rounded (equilibrium forms)
  Melting and refreezing results in large, bonded grain clusters

## Slide 87: Results: Heterogeneity
Good or bad?
The Avalanche Handbook, 1993

## Slide 89: Snow Cover Distribution

## Slide 90: Snow Cover Distribution
Three Spatial Scales
  Macroscale
    Areas up to 106 km2
    Characteristic Distances of 10-1000 km
    Dynamic meteorologic effects are important
  Mesoscale
    Characteristic Distances of 100 m to 10 km
    Redistribution of snow along relief features due to wind
    Deposition and accumulation of snow may be related to terrain variables and to vegetation cover
  Microscale
    Characteristic Distances of 10 to 100 m
    Differences in accumulation result from variations in air flow patterns and transport

## Slide 91: Snow Cover Distribution
Effect of Topography
  The depth of seasonal snow cover usually increases with elevation if other influencing factors do not vary with elevation
    This trend is generally due to:
      increase in the number of snowfall events
      decrease in evaporation and melt
    The rate of increase with elevation may vary widely from year-to-year
  However, elevation alone is not a causative factor in snow cover distribution
    Many other factors must be considered:
      slope, aspect, vegetation, wind, temperature, and characteristics of the parent weather systems

## Slide 92: Snow Cover Distribution
Effect of Vegetation
  Snow falling into a vegetation canopy is influenced by two phenomena:
    Turbulent air flow above and within the canopy
      may lead to variable snow input rates and microscale variation in snow loading on the ground
    Direct interception of snow by the canopy elements
      may either sublimate or fall to the ground
  Processes are related to vegetation type, vegetation density, and the presence of nearby open areas

## Slide 93: Snow Cover Distribution
Forested Environments
  Differences in snow accumulation between different species of conifers is usually small compared to between coniferous and deciduous stands
    coniferous stands are all relatively efficient snow interceptors
    Once intercepted, cohesion between snow particles helps keep snow in the canopy for extended time periods
      snow is more susceptible to sublimation losses in the canopy than on the forest floor
        High surface area to mass ratio

## Slide 94: Snow Cover Distribution
Forested Environments
  Most studies show greater snow accumulation in clearings than in the forest
  Most of the difference develops during storms, not between storms
    redistribution of intercepted snow by wind to clearings is not typically a significant factor
  Interception and subsequent sublimation are the major factors contributing to the difference
20-45%
Greater Snow
Accumulation

## Slide 95: Snow Cover Distribution
Open Environments
  Over highly exposed terrain, the effects of meso- and micro-scale differences in vegetation and terrain features may produce wide variations in accumulation patterns.

## Slide 96: Snow Cover Distribution
Open Environments
  Relative accumulation on various landscapes in an open grassland environment
    Normalized to snow accumulation on level plains under fallow

## Slide 97: Blowing Snow

## Slide 98: Blowing Snow
Two major hydrological influences of wind transport of snow:
Redistribution of Snow Water Equivalent
Loss of Water by Sublimation

## Slide 99: Blowing Snow
Four Factors
1. Shear Velocity
2. Threshold Wind Speed
3. Types of Transport
4. Transport Rates

## Slide 100: Blowing Snow
Shear Velocity
  Movement of snow particles occurs when the drag force exerted on the snow surface by the wind exceeds the surface shear strength.
  The total atmospheric shear stress, J, is equal to pau*2, where pa is the air density and u* is the friction (shear) velocity.

## Slide 101: Blowing Snow
Shear Velocity - Wind
  The friction velocity u* is usually calculated from wind profiles, but can be estimated from a single 10-m wind speed (u10):
u* =u10 1.18/41.7
u* =u10/26.5
u* =u10 1.30/44.2
Antarctic Ice Sheet
Snow-covered Lake
Snow-covered
Fallow Field
u10 = 5 m/s
u* = 0.19
u* = 0.16
u* = 0.18

## Slide 102: Blowing Snow
Threshold Shear Velocity - Snow
  u*t is the friction velocity at which snow transport begins
    depends on snow characteristics
Older, wind-hardened,
dense or wet-snow:
u*t = 0.25 - 1.0 m/s
Fresh, loose, dry snow,
and during snowfall:
u*t = 0.07 - 0.25 m/s

## Slide 103: Blowing Snow
Three Types of Transport
Creep
TYPE
MOTION
HEIGHT
WINDSPEED
Saltation
Turbulent
Diffusion
Roll
Bounce
Suspended
< 1 cm
1 cm - 10 cm
1 m - 100 m
<< 5 m/s
5 - 10 m/s
> 10 m/s

## Slide 104: Blowing Snow
Transport Rates
  Approximately proportional to u103
    Double the wind speed, ~8 times the transport rate
    4 times the wind speed, ~64 times the transport rate
  Depends on snow surface conditions, availability of erodible snow, wind characteristics.

## Slide 105: Blowing Snow
Sublimation Losses
  Snow particles are more exposed to atmosphere during wind transport
  Sublimation losses can be very high as a result
    depends on transport rate, transport distance, temperature, humidity, wind speed, and solar radiation

## Slide 106: Blowing Snow
Sublimation Losses
30
25
25
22
16
22
50
20
Mean Annual Blowing Snow Sublimation
CANADA, 1970-1976
Loss in mm SWE over 1 km

## Slide 107: Blowing Snow
Effect on Snow Characteristics
  Mechanical fragmentation and sublimation losses result in small, rounded particles
  Windblown snow deposits are inherently more dense
Snow crystal
collected during
snowfall under
calm winds
Windblown snow
particle collected
during transport
2 mm

## Slide 108: Blowing Snow

## Slide 112: Snow Ablation
Definition – the loss of snowpack through snow melt and/or snow sublimation
Surface energy balance dictates energy changes to the snowpack
The snow used to be this deep…
Notes: Definition – the loss of snowpack through snow melt and/or snow sublimation
Surface energy balance dictates energy changes to the snowpack
Image: nicholas.edu

## Slide 113: Snow Ablation
The energy available for
  Snow melt or ablation is a function of the
  Energy balance (inputs – outputs) of the snowpack
Notes: The energy available for snow melt or ablation is a function of the energy balance (inputs – outputs) of the snowpack
Image: www.meted.ucar.edu

## Slide 114: Snow Ablation Modeling
There can be a great difference in the amount of water
Notes: There can be a great difference in the amount of water in a snowpack (as observed with SNOTEL sites, etc.) and the amount of water that melts into streams
Image: http://hydro.vwrrc.vt.edu/about/snowmelt_hb/

## Slide 115: Temperature Index Model
Simplified model relating degree days > 0oC to snowmelt
Degree days = (time > 0oC) * (Temp - 0oC)
Thus, a relationship between air temperature and snowmelt
General form:
M = a DD
M is melt (mm), a is the Degree Day Factor (mm/(d oC)), and DD is the degree-days > 0oC (oC*d)
Rango & Martinec, 1995
Notes: Simplified model relating degree days > 0oC to snowmelt
Degree days = (time > 0oC) * (Temp - 0oC)
Thus, a relationship between air temperature and snowmelt
General form:
M = a DD
M is melt (mm), a is the Degree Day Factor (mm/(d oC)), and DD is the degree-days > 0oC (oC*d)

## Slide 116: Temperature Index Model
We can relate 2 things that are easily measured: snowmelt and air temperature
Dingman, 1998
Danville, VT
March, 1973
Degree-Day Factor is the slope of this line

## Slide 117: DDF depends on…
DDF depends on location: forest vs. open areas
DDF increases in time
DDF depends on snow density
Rango & Martinec, 1995
general
open
forest
Notes: DDF depends on location: forest vs. open areas
DDF increases in time
DDF depends on snow density

## Slide 118: Snowmelt

## Slide 119: Water in snow
Meltwater is generated at the surface of the snowpack,
We would assume that gravity would move meltwater vertically into and through the snow pack
Rain on snow also supplies liquid water to the surface of the snowpack
Hydrologic analogy is groundwater infiltration and movement – precipitation at the ground surface infiltrates and then percolates vertically toward the groundwater table
Notes: Meltwater is generated at the surface of the snowpack,
We would assume that gravity would move meltwater vertically into and through the snow pack
Rain on snow also supplies liquid water to the surface of the snowpack
Hydrologic analogy is groundwater infiltration and movement – precipitation at the ground surface infiltrates and then percolates vertically toward the groundwater table

## Slide 120: Water in snow
Water moves in preferential channels
Once melt occurs at the snow surface, we lose track of it as liquid water infiltrates into the snowpack
Preferential flow common, but we don’t understand from first principles
Notes: Water moves in preferential channels
Once melt occurs at the snow surface, we lose track of it as liquid water infiltrates into the snowpack
Preferential flow common, but we don’t understand from first principles

## Slide 121: Water Flow Through Snow
Wide Range of Flow Velocities
  2-60 cm/min
  Depends on several factors
    internal snow pack structure
    condition of the snow pack prior to introduction of water
    amount of water available at the snow surface
Notes: Wide Range of Flow Velocities
  2-60 cm/min
  Depends on several factors
    internal snow pack structure
    condition of the snow pack prior to introduction of water
    amount of water available at the snow surface

## Slide 122: Water Flow Through Snow
Flow through Homogeneous Snow
  At melting temperature, a thin film of water surrounds each snow grain
    Much of the water can flow through this film
  Once pores are filled, laminar flow can occur
    Very efficient mechanism for draining the snow pack
Notes: Flow through Homogeneous Snow
  At melting temperature, a thin film of water surrounds each snow grain
    Much of the water can flow through this film
  Once pores are filled, laminar flow can occur
    Very efficient mechanism for draining the snow pack

## Slide 123: Water Flow Through Snow – Four Liquid Water Regimes
  Capillary: < 1% free water
    water doesn’t drain due to capillary tension
  Unsaturated: 1-14% free water
    water drains by gravity, but air spaces are continuous
    Pendular Regime
  Saturated: > 14% free water
    water drains by gravity, but air spaces are discontinuous
    Funicular Regime
  Melt/Freeze
    water melts and refreezes, possibly several times, before it drains from the snow pack
Notes:   Capillary: < 1% free water
    water doesn’t drain due to capillary tension
  Unsaturated: 1-14% free water
    water drains by gravity, but air spaces are continuous
    Pendular Regime
  Saturated: > 14% free water
    water drains by gravity, but air spaces are discontinuous
    Funicular Regime
  Melt/Freeze
    water melts and refreezes, possibly several times, before it drains from the snow pack

## Slide 124: Water Flow Through Snow – Liquid Water Transmission
Melt and rain water are lagged and attenuated as they move through the snow cover.
Function of depth, density, ice layers, grain size, and refreezing.
Rain
Notes: Melt and rain water are lagged and attenuated as they move through the snow cover.
Function of depth, density, ice layers, grain size, and refreezing.

## Slide 134: Snow Energy Exchanges
(Qsi-Qr) + (Lin - Lout) + Qh + Qe + Qg + Qp - dU/dt = Qm
Modified from D. Cline
Qsn
Qle
Qsi
Qr
Lout
Lin

## Slide 147
David G. Tarboton
Utah Water Research Laboratory
Utah State University
www: http://www.engineering.usu.edu/dtarb/snow/snow.html
An Energy Balance Snowmelt Model for use in Spatially Distributed Hydrologic Models
(UEB, Utah Energy Balance Model)

## Slide 148: Snow Energy Exchanges
(Qsi-Qr) + (Lin - Lout) + Qh + Qe + Qg + Qp - dU/dt = Qm
Modified from D. Cline
Qsn
Qle
Qsi
Qr
Lout
Lin

## Slide 149: Snow Model Physics and Parameterizations
Inputs
Q
Q
g
m
Water Equivalence W
Wind
Thermally
active
layer
Snow
Soil
D
e
Energy Content U
Q
Q (T ,T )
h a s
Q (T )
le
s
Q (e ,T )
e a s
Fluxes dependent on
surface temperature
State variables

## Slide 150: Model Structure
Predictor + Corrector Numerical Integration
Predictor
{
{
Corrector

## Slide 151: Surface Energy Balance
Depth sensitivity to
diurnal temperature
fluctuation
Energy Balance /Equilibrium at surface
External Forcing
Surface temperature dependent fluxes
If Ts > 0 oC  Conduction cannot accommodate surface energy inputs
 Surface melt is generated. Set Ts = 0 oC
 Additional energy is advected downwards by surface melt inflow

## Slide 152: Surface Energy Balance – With Forest Canopy
Depth sensitivity to
diurnal temperature
fluctuation
Energy Balance /Equilibrium at surface
External Forcing
Surface temperature dependent fluxes
If Ts > 0 oC  Conduction cannot accommodate surface energy inputs
 Surface melt is generated. Set Ts = 0 oC
 Additional energy is advected downwards by surface melt inflow

## Slide 153: Melt Outflow Calculation

## Slide 154: Shortwave Radiation

## Slide 155: Atmospheric Transmissivity
Bristow, K. L. and G. S. Campbell, (1984), "On the Relationship Between Incoming Solar Radiation and the Daily Maximum and Minimum Temperature," Agricultural and Forest Meteorology, 31: 159-166.

## Slide 156: Reflective Properties of Snow
Modified from D. Cline

## Slide 157: Albedo
Dickinson, R. E., A. Henderson-Sellers and P. J. Kennedy, (1993), "Biosphere-Atmosphere Transfer Scheme (BATS) Version 1e as Coupled to the NCAR Community Climate Model," NCAR/TN-387+STR, National Center for Atmospheric Research.

## Slide 158: Shortwave Radiation & Snow
Why does snow albedo decrease over time?
Modified from D. Cline, Handbook of Snow

## Slide 159: Effect of Illumination angle
Dickinson, R. E., A. Henderson-Sellers and P. J. Kennedy, (1993), "Biosphere-Atmosphere Transfer Scheme (BATS) Version 1e as Coupled to the NCAR Community Climate Model," NCAR/TN-387+STR, National Center for Atmospheric Research.

## Slide 160: Calibration
Data: Central Sierra Snow laboratory winter of 85/86.
1. Drive model with net radiation input.
  • Match overall accumulation and ablation of W
  • Match surface temperatures
2. Drive model with observed incident radiation.
  • Adjust albedo parameters so that observed and net radiation matches.
3. Compare Melt Outflow

## Slide 161: Calibration of zo and Ks to match observations with Net Radiation Input

## Slide 162: Surface conductance Ks adjusted to match diurnal surface temperature fluctuations

## Slide 163: Surface conductance Ks adjusted to match diurnal surface temperature fluctuations

## Slide 164: Drive with incident solar radiation, adjust albedo.

## Slide 165: Confirm agreement between modeled and observed Net Radiation

## Slide 166: Calibrate Ksat to match Melt Outflow