## Slide 1: Physical Hydrology & Hydroclimatology (Multiscale Hydrology)
A science dealing with the properties, distribution and circulation of water.
R. Balaji
balajir@colorado.edu
CVEN5333 http://civil.colorado.edu/~balajir/CVEN5333
Includes slides from Prof. Mike Gooseff

## Slide 2: Physical factors in the generation of runoff
Learning objectives
Be able to describe the processes involved in runoff generation
Be able to distinguish between infiltration excess, saturation excess and subsurface stormflow runoff generation mechanisms and identify when and where each is more likely to occur
Be able to describe the physical factors resulting in the occurrence of runoff by the different mechanisms

## Slide 3: Resources
Rainfall Runoff Module Online, http://hydrology.usu.edu/RRP, Chapters 1 - 3
Dingman Chapters 10
Chow Book Chapters 5, 7
Jeff McDonnell Website (http://www.cof.orst.edu/cof/fe/watershd/)
Benchmark papers in streamflow generation processes (many at http://www.cof.orst.edu/cof/fe/watershd/fe537/bpapers.html)

## Slide 4: Physical Processes involved in Runoff Generation
Rainfall Runoff Processes
Notes: Figure 1. Physical Processes involved in Runoff Generation.

## Slide 5
Pathways followed by subsurface runoff on hillslopes
(from Kirkby, 1978)
Notes: Figure 2. Pathways followed by subsurface runoff on hillslopes

## Slide 6
Relationship between runoff ratio and soil moisture content. (Woods et al., 2001.)
Threshold Hillslope Response

## Slide 7
(a) 14 m from stream,
(b) 103 m from stream
Relation between runoff and depth to groundwater
Two different locations in the Svartberget catchment (Seibert et al., 2003)
Notes: Figure 4. Relation between runoff and depth to groundwater for two different locations in the Svartberget catchment (Seibert et al., 2003)

## Slide 8
(a) Photograph of cross section through soil following dye tracing experiment. (b) Moisture content inferred from dye tracing experiment. (Courtesy of Markus Weiler)
Infiltration follows preferential pathways

## Slide 9
Wetting may occur at depth before at the surface
See preferential pathway infiltration animation http://hydrology.neng.usu.edu/RRP/ (ch 2)

## Slide 10: Runoff Generation Mechanisms
See infiltration excess runoff generation animation http://hydrology.neng.usu.edu/RRP/ (ch 2)
(a) Infiltration excess overland flow
(also called Horton overland flow)
P
P
P
qo
f
f
(following Beven, 2001)

## Slide 11
f1
f0
Figure 7. Rainfall, runoff, infiltration and surface storage during a natural rainstorm. The shaded areas under the rainfall graph represent precipitation falling at a rate exceeding the infiltration rate. The dark grey area represents rainfall that enters depression storage, which is filled before runoff occurs. The light grey shading represents rainfall that becomes overland flow. The initial infiltration rate is f0, and f1 is the final constant rate of infiltration approached in large storms. (from Dunne and Leopold, 1978)

## Slide 12
Overland flow moves downslope as an irregular sheet (from Dunne and Leopold, 1978)

## Slide 13
(b) Partial area infiltration excess overland flow
P
P
P
qo
f
Fraction of area contributing to overland flow
(following Beven, 2001)

## Slide 14
(c) Saturation excess overland flow
P
P
P
qr
qs
qo
Variable source area
(following Beven, 2001)
See saturation excess runoff generation animation http://hydrology.neng.usu.edu/RRP/ (ch 2)

## Slide 15
(d) Subsurface stormflow
P
P
P
qs
(following Beven, 2001)
See subsurface runoff generation animation http://hydrology.neng.usu.edu/RRP/ (ch 2)

## Slide 16
(e) Perched subsurface stormflow
Horizon 1
Horizon 2
P
P
P
qs
Impeding layer
(following Beven, 2001)
See perched layer stormflow runoff generation animation http://hydrology.neng.usu.edu/RRP/ (ch 2)

## Slide 17
Map of saturated areas showing expansion during a single rainstorm. The solid black shows the saturated area at the beginning of the rain; the lightly shaded area is saturated by the end of the storm and is the area over which the water table had risen to the ground surface. (from Dunne and Leopold, 1978)

## Slide 18
Seasonal variation in pre-storm saturated area (from Dunne and Leopold, 1978)

## Slide 19
Variable Source Area Concept (from Chow et al, 1988). The small arrows in the hydrographs show how the streamflow increases as the variable source extends into swamps, shallow soils and ephemeral channels. The process reverses as streamflow declines.

## Slide 20
Schematic illustration of macropore network being activated due to rise in groundwater resulting in rapid lateral flow.
Transmissivity Feedback

## Slide 21
Brutsaert, 2005

## Slide 22
Soil
Low permeable bedrock
Rapid lateral flow at soil bedrock interface.

## Slide 23: Features of subsurface stormflow
Unimpeded entry by new water from rainfall into the soil
Rapid downslope flow through preferential paths
Mixing with old water depending on rainfall intensity and soil moisture status
From Brutsaert, 2005, p454

## Slide 24
Direct precipitation
on saturated zone
0 s 0 s
Baseflow
Water
table
0 s 0 s
Water
table
0 s 0 s
Water
table
Baseflow + subsurface stormflow
Baseflow + subsurface stormflow
Return flow
(a)
(b)
(c)
Rain
Rain
Rain
Groundwater ridging subsurface stormflow processes in an area of high infiltration rate.
Notes: Figure 12. Groundwater ridging subsurface stormflow processes in an area of high infiltration rate.

## Slide 25
The particular runoff process that dominates is place and time dependent

## Slide 26
Infiltration capacity
Surface Water Input
Saturation OF
Deeper groundwater aquifer
Infiltration
Soil regolith
Regolith subsurface flow
(interflow)
Saturation
Aquifer subsurface flow
(baseflow)
Percolation
Variable
source area
Return flow
Hortonian OF
Evapotranspiration
Notes: Figure 13. Hydrological Pathways involved in different runoff generation processes. Infiltration excess pathways are shown in red. Saturation excess and subsurface stormflow pathways are shown in blue. Groundwater and baseflow pathways in black and Evapotranspiration is green.

## Slide 27: Summary points
A bewildering range of hydrologic, climatic, topographic and soil conditions which favor different mechanisms
Extreme complexity suggests a single unifying model may not be possible or desirable
Distributed models allow exploration of consequences of simplifying assumptions and can lead to better understanding of the interplay between processes and pathways
Mathematical rigor may instill false confidence and undeserved sense of realism
Catchment scale parameterizations have difficulty representing spatial variability
From Brutsaert, 2005, p457-461

## Slide 28: Rainfall-Runoff Modeling
Catchment-scale responses
  “Engineering” Methods
    Rational Method
    SCS Curve-Number Method
    Unit Hydrograph
  Process Based Method
    TOPMODEL

## Slide 29: Rainfall-Runoff Models Rational Method
Based on a proportionality between effective rainfall intensity (p*) and peak discharge (qpk)
eR is a unit conversion factor
AD is the drainage area
Used mostly for
catchment response
modeling
qpk = eR CR p* AD
Notes: FILL IN EQ
Used mostly for urban and suburban catchment response modeling

## Slide 30: Rainfall-Runoff Models SCS Curve Number Method
Based on soil characteristics within a basin
  First compute P*, which is equivalent to Q*:
  Then, compute Smax (watershed storage):
  The Curve Number is determined by the soil type and antecedent moisture conditions

## Slide 31
Curve Numbers for Antecedent Soil Moisture Condition II |  |  |  | 
 | Hydrologic Soil Group |  |  | 
Land Use Description | A | B | C | D
Commercial, row houses and townhouses | 80 | 85 | 90 | 95
Fallow, poor condition | 77 | 86 | 91 | 94
Cultivated with conventional tillage | 72 | 81 | 88 | 91
Cultivated with conservation tillage | 62 | 71 | 78 | 81
Lawns, poor condition | 58 | 74 | 82 | 86
Lawns, good condition | 39 | 61 | 74 | 80
Pasture or range, poor condition | 68 | 79 | 86 | 89
Pasture or range, good condition | 39 | 61 | 74 | 80
Meadow | 30 | 58 | 71 | 78
Pavement and roofs | 100 | 100 | 100 | 100
Woods or forest thin stand, poor cover | 45 | 66 | 77 | 83
Woods or forest, good cover | 25 | 55 | 70 | 77
Farmsteads | 59 | 74 | 82 | 86
Residential quarter-acre lot, poor condition | 73 | 83 | 88 | 91
Residential quarter-acre lot, good condition | 61 | 75 | 83 | 87
Residential half-acre lot, poor condition | 67 | 80 | 86 | 89
Residential half-acre lot, good condition | 53 | 70 | 80 | 85
Residential 2-acre lot, poor condition | 63 | 77 | 84 | 87
Residential 2-acre lot, good condition | 47 | 66 | 77 | 81
Roads | 74 | 84 | 90 | 92
Source: From NRCS, 1984. |  |  |  | 
Group A – low runoff potential, well drained soils (Ksat > 0.3 in/hr)
Group B – moderate infiltration, fairly deep soils (Ksat ~ 0.15-0.3 in/hr)
Group C – slow infiltration rate soils, fine texture (Ksat ~ 0.05-0.15 in/hr)
Group D – high runoff potential, clay soils (Ksat < 0.05 in/hr)

## Slide 32
Adjustments to Runoff Curve Number (CN) for Dry |  | 
or Wet Antecedent Soil Moisture Conditions |  | 
 | Factors to Convert Curve Number | 
 | for AMC II to AMC I or AMC III | 
Curve Number (AMC II) | AMC I (dry) | AMC III (wet)
10 | 0.40 | 2.22
20 | 0.45 | 1.85
30 | 0.50 | 1.67
40 | 0.55 | 1.50
50 | 0.62 | 1.40
60 | 0.67 | 1.30
70 | 0.73 | 1.21
80 | 0.79 | 1.14
90 | 0.87 | 1.07
100 | 1.00 | 1.00
AMC I – dormant season moisture < 0.5”, growing < 1.4”
AMC II – dormant season moisture >0.5”, <1.1”; growing season >1.4”, <2.1”
AMC III – dormant season moisture >1.1”, growing season >2.1”

## Slide 33: SCS Method
Then, compute the hydrograph and its timing:
Q
time
Tr =
qpk =
Tb =

## Slide 34: Example
George’s house is just downstream of a 4-acre watershed that presently has mature forest on top of a Crosby soil. He is worried that the new townhouse development will increase the amount of water flowing in the creek by his house.
Using a 2 inch storm determine the increase in water volume that will flow by George’s house due to the development.

## Slide 35
Step 1--Calculate S numbers
  -Crosby soil is Type C (tables will provide this)
  -CN (AMC II) mature forest is 70
  -CN (AMC II) townhouses is 90
  -Convert to AMC III-worst case scenario
  -CN 70*1.21=84.7
  -CN 90*1.07=96.3
  -S (forest) = 1.81in =
  -S (townhouses) = 0.38in =
Notes: Step 1--Calculate S numbers
  -Crosby soil is Type C (tables will provide this)
  -CN (AMC II) mature forest is 70
  -CN (AMC II) townhouses is 90
  -Convert to AMC III-worst case scenario
  -CN 70*1.21=84.7
  -CN 90*1.07=96.3
  -S (forest) = 1.81in =
  -S (townhouses) = 0.38in =

## Slide 36
Curve Numbers for Antecedent Soil Moisture Condition II |  |  |  | 
 | Hydrologic Soil Group |  |  | 
Land Use Description | A | B | C | D
Commercial, row houses and townhouses | 80 | 85 | 90 | 95
Fallow, poor condition | 77 | 86 | 91 | 94
Cultivated with conventional tillage | 72 | 81 | 88 | 91
Cultivated with conservation tillage | 62 | 71 | 78 | 81
Lawns, poor condition | 58 | 74 | 82 | 86
Lawns, good condition | 39 | 61 | 74 | 80
Pasture or range, poor condition | 68 | 79 | 86 | 89
Pasture or range, good condition | 39 | 61 | 74 | 80
Meadow | 30 | 58 | 71 | 78
Pavement and roofs | 100 | 100 | 100 | 100
Woods or forest thin stand, poor cover | 45 | 66 | 77 | 83
Woods or forest, good cover | 25 | 55 | 70 | 77
Farmsteads | 59 | 74 | 82 | 86
Residential quarter-acre lot, poor condition | 73 | 83 | 88 | 91
Residential quarter-acre lot, good condition | 61 | 75 | 83 | 87
Residential half-acre lot, poor condition | 67 | 80 | 86 | 89
Residential half-acre lot, good condition | 53 | 70 | 80 | 85
Residential 2-acre lot, poor condition | 63 | 77 | 84 | 87
Residential 2-acre lot, good condition | 47 | 66 | 77 | 81
Roads | 74 | 84 | 90 | 92
Source: From NRCS, 1984. |  |  |  | 
Adjustments to Runoff Curve Number (CN) for Dry |  | 
or Wet Antecedent Soil Moisture Conditions |  | 
 | Factors to Convert Curve Number | 
 | for AMC II to AMC I or AMC III | 
Curve Number (AMC II) | AMC I (dry) | AMC III (wet)
10 | 0.40 | 2.22
20 | 0.45 | 1.85
30 | 0.50 | 1.67
40 | 0.55 | 1.50
50 | 0.62 | 1.40
60 | 0.67 | 1.30
70 | 0.73 | 1.21
80 | 0.79 | 1.14
90 | 0.87 | 1.07
100 | 1.00 | 1.00

## Slide 37
Step 2-Calculate Q (excess runoff)
  P = 2 inches rainfall
  Q(forest) = 0.91 inches
  Q(townhouses) = 1.61 inches
Notes: Step 2-Calculate Q (excess runoff)
  P = 2 inches rainfall
  Q(forest) = 0.91 inches
  Q(townhouses) = 1.61 inches

## Slide 38
Step 3-Calculate volume
  Area= 4 acre
  Excess rainfall = 0.91in (forest) =
  Excess rainfall = 1.61in (townh) =
  Volume (forest) = 4*0.08=0.32 acre ft
  Volume (townh) = 4*0.13=0.52 acre ft
  Volume (forest) = 14,000ft3
  Volume (townh) = 22,600ft3
  Volume of runoff will increase 61%
Notes: Step 3-Calculate volume
  Area= 4 acre
  Excess rainfall = 0.91in (forest) = 0.08ft
  Excess rainfall = 1.61in (townh) = 0.13ft
  Volume (forest) = 4*0.08=0.32 acre ft
  Volume (townh) = 4*0.13=0.52 acre ft
  Volume (forest) = 14,000ft3
  Volume (townh) = 22,600ft3
  Volume of runoff will increase 61%

## Slide 39: Goal is to quantify watershed response without consideration of detailed subscale processes
Runoff (mm/hr)
Flow (m3/s)
Time
Runoff and Flow
Flow = f(Runoff, Watershed hydrologic properties)

## Slide 40: Systems approach to event flow
From Dingman, 2002, Physical Hydrology

## Slide 41
Rainfall – Runoff Analysis
From Mays, 2011, Ground and Surface Water Hydrology

## Slide 42: Linear Systems
From Chow et al., 1988, Applied Hydrology
Assume superposition, i.e. the principle of additivity
Convolution integral

## Slide 43: Rainfall Runoff Models Unit Hydrograph
Assumes a linear watershed response to a unit effective input – generally found from empirical observations: e.g., 1 inch of rain in 2.5 hours, or 1 inch of rain in 1 hour.
Dingman, Figure 9-45

## Slide 44: Rainfall Runoff Models Unit Hydrograph
Consider an increase in AMOUNT of precipitation
For larger storms, with the same duration, scale unit hydrograph by # of “unit inputs”
All points on increased response hydrograph are 2.4*unit hydrograph
We had 2.5 hr unit hydrograph, what is the response to 2.4 in. in 2.5 hr?
Notes: All points on increased response hydrograph are 2.4*unit hydrograph

## Slide 45: Rainfall Runoff Models Unit Hydrograph
Consider an increase in the DURATION of precipitation
For longer storms, same amount, lag smaller unit hydrographs, then add them
We had 2.5 hr unit hydrograph, what is the response to 2 in. in 5 hours?
Add 2 - 2.5 hr unit hydrographs and lag by 2.5 hours
Notes: Add 2 - 2.5 hr unit hydrographs and lag by 2.5 hours

## Slide 46: Linear Response at Discrete Time Steps
Excess Precipitation

## Slide 47: A Du hour unit hydrograph is the characteristic response of a given watershed to a unit volume (e.g. 1 in or cm) of effective water input (usually rain) applied at a constant rate for Du hours
Runoff (mm/hr)
Flow (m3/s)
Time
Runoff and Flow

## Slide 48: Assumptions (Chow P 214)
Excess rainfall has constant intensity within effective duration
Excess rainfall is uniformly distributed over watershed
The base time of the direct runoff hydrograph from an increment of excess rainfall is constant
The ordinates of all direct runoff hydrographs are proportional to the amount of direct runoff
For a given watershed the hydrograph resulting from a given excess rainfall reflects the unchanging characteristics of the watershed

## Slide 49
Calculating a Hydrograph from a Unit Hydrograph
...
...
for n=1 ... N
From Mays, 2011, Ground and Surface Water Hydrology
Chow page 217

## Slide 50: Example
The 1- hr unit hydrograph for a watershed is given below. Determine the runoff from this watershed for the storm pattern given. The abstractions have a constant rate of 0.3 in/ h.
Time ( hr) | 1 | 2 | 3 | 4 | 5 | 6
Precipitation ( in) | 0.5 | 1 | 1.5 | 0.5 |  | 
Unit hydrograph ( cfs) | 10 | 100 | 200 | 150 | 100 | 50

## Slide 51: Example

## Slide 52: Limitations
Linearity is violated when deeper water flows faster.
Rainfall is seldom uniform in space
Effective input is very uncertain and depends on antecedent conditions

## Slide 53: Example
Determine the 1- hr unit hydrograph for a watershed using the precipitation pattern and runoff hydrograph below. The abstractions have a constant rate of 0.3 in/ hr, and the baseflow of the stream is 0 cfs.
Time (h) | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Precipitation (in) | 0.5 | 1 | 1.5 | 0.5 |  |  |  |  |  | 
Runoff (cfs) | 2 | 27 | 122 | 292 | 385 | 300 | 185 | 80 | 10 | 0

## Slide 54
Calculating a Hydrograph from a Unit Hydrograph and visa versa
...
...
for n=1 ... N
From Mays, 2011, Ground and Surface Water Hydrology

## Slide 55: Determining the Unit Hydrograph from Direct Runoff Hydrograph Observations
M =4 precip values
N=9 Direct Runoff Hydrograph Ordinates
L=N=M+1=6 Unit Hydrograph ordinates
9 equations to solve for 6 U values
(Overdetermined system – use least squares with Solver)
Any 6 initial U values
Minimize this by changing these

## Slide 56: Which hydrograph is associated with each watershed
1
2
3
A
B
C

## Slide 57: Time Area Diagram
Distribution function of area by travel time to outlet
Under assumptions of constant velocity
t = d/v
This provides a geomorphological basis for defining the unit response function.

## Slide 58: Channel Network “Width” Function
The number of channels at a distance x from the outlet
x
x

## Slide 59: Synthetic Unit Hydrographs
A unit hydrograph is intended to quantify the unchanging characteristics of the watershed
The synthetic unit hydrograph approach quantifies the unit hydrograph from watershed attributes
1/3
2/3
Snyder’s Synthetic Unit Hydrograph (Chow et al. p225)
L = main channel length (km or mi)
Lc = length to point opposite centroid
qp=Qp /A = C2Cp/tp

## Slide 60: Example Snyder's Synthetic Unit Hydrograph
A watershed has a drainage area of 5.42 mi2; the length of the main stream is 4.45 mi, and the main channel length from the watershed outlet to the point opposite the center of gravity of the watershed is 2.0 mi. Using Ct = 2.0 and Cp = 0.625, determine the standard synthetic unit hydrograph for this basin. What is the standard duration? Use Snyder’s method to determine the 30- min unit hydrograph parameter.
Follow the procedure of table 8.4.1
L = main channel length = 4.45 mi
Lc = length to point opposite centroid = 2.0 mi
A = watershed area = 5.42 mi2
Widths
(2.37,285)
(3.09,427.5)
(4.05,570)
(5.97,427.5)
(7.41,285)
(14.1,0)
W50
W75
1/3
2/3

## Slide 61: SCS Dimensionless Unit Hydrograph
From Mays, 2011, Ground and Surface Water Hydrology

## Slide 62: Unit Hydrographs of Different Durations - S Curves
From Mays, 2011, Ground and Surface Water Hydrology

## Slide 63: Example
The 1- hr unit hydrograph for a watershed is given below. Determine the 2 hr unit hydrograph.
Time ( hr) | 1 | 2 | 3 | 4 | 5 | 6
Unit hydrograph ( cfs) | 10 | 100 | 200 | 150 | 100 | 50

## Slide 64: S Curve to Develop 2 hr unit hydrograph