## Slide 1: Physical Hydrology & Hydroclimatology (Multiscale Hydrology)
A science dealing with the properties, distribution and circulation of water.
R. Balaji
balajir@colorado.edu
CVEN5333 http://civil.colorado.edu/~balajir/CVEN5333

## Slide 2: Lecture Week – 3 Sep 6
Estimating mass balance quantities (especially ET)
  Under uncertainty
Quantifying temporal variability
  Basic statistics
  Coefficient of variability
Persistence
  Autocorrelation
Flow Duration Curve (FDC)

## Slide 3: Estimation of Areal ET
P
ET
Q
Gout
Gin
S

## Slide 4: Estimation of areal ET
Assume Gin and Gout small and at equilibrium Change in storage is zero
  ET = P - Q
Assume storage is negligible
mET = mp – mQ
Errors: model and measurement
Accuracy of precipitation and streamflow
Absolute and relative uncertainty
Independent errors s2x+y = s2x + s2y

## Slide 5: Estimation of areal ET
Assume Gin and Gout small
Assume storage is negligible
mET = mp – mQ
Errors: model and measurement
Accuracy of precipitation and streamflow
Relative uncertainty (uP) is measurement uncertainty or accuracy
Absolute uncertainty (mp uP)
Assuming Normal Distribution of measurement errors
Pr{mp - mp uP <= true precipitation <= mp + mp uP } = 0.95
mp uP = 2*sP Where sP is the estimated standard deviation for precipitation
Similarly for Q and ET

## Slide 6: Example of ET estimate (2-1)
NH Oyster river
Average precip 1066mm/year, uncertain 10% (at 95% level)
Average drainage outflow 551 mm/year, 5% uncertain
mET = 1066 – 551 mm/year = 515 mm/yr
Uncertainty = SQRT {(1066*.1)**2 + (551*.05)**2} = 55.1 mm/yr
Relative uncertainty = 2 (55.1/515) = 0.214
Pr {405 < mET < 625} = .95

## Slide 7: Exercise 2-1

## Slide 8: Exercise 2-1
M(ET) = m(p) – m(q)
s^2(ET) = s^2(p) + s^2(q)
Convert from m^3/s to mm/yr
Q/A=386 m^3/s /20370km^2 = 598 mm/yr
S(p)=0.1*p = 110 mm/yr
S(q) = 0.05*598 mm/yr
S(ET) = sqrt( s(q)^2 +s(p)^2) = 114 mm/yr
Relative error =114 mm/yr/598 mm/y=23%
Similarly: Yukon River 115/398 = 29%
Euphrates: 32/190 = 17%
Mekong: 221/832 = 27%

## Slide 9
Logan River Annual Aggregate Time Series
0
500
1000
1500
2000
2500
1920
1930
1940
1950
1960
1970
1980
1990
2000
cfs
mean cfs
7 day min cfs
max cfs

## Slide 10: Random variables
Probability density
function
Cumulative distribution
function

## Slide 11: Space/time variability
Continuous series – samples
Expectation, Mean, standard deviation, median, extremes (max/min), percentile, coefficient of variation (CV)
Flow duration curves (FDC) flow rate (q) vs. cumulative distribution (Q)
Exceedence probability E PQ(qp) = 1 – FQ(qp) = Pr {Q>qp}

## Slide 12
From Dingman, 2002

## Slide 13
From Dingman, 2002

## Slide 14: Flow Duration Curve

## Slide 15
Relatively flat slopes at Upper end of FDC
  Snowmelt driven floods
  Large basin with storms
  of several days
Steep slopes at Upper end of FDC
  Flashy streams
  Intense storms of short duration
Flat slopes at low end
  significant groundwater storage
  frequent precipitation inputs
FDC can be constructed on
7-day Min Flow
Average daily flow
Average annual flow
etc

## Slide 18
Mean of Monthly Streamflow. Alafia River

## Slide 20
From Dingman, 2002

## Slide 21
From Dingman, 2002

## Slide 22: Alafia river: Autocorrelation
Autocorrelation of standardized flow

## Slide 23: Alafia River: Monthly streamflow distribution

## Slide 24
Median
Box (Red Lines) enclose 50% of the values
Time Series Box Plot

## Slide 25: Box Plot
Outliers: beyond 1.5*IQR
Whiskers: 1.5*IQR or largest value
Box: 25th %tile to 75th %tile
Line: Median (50th %tile) - not the mean
Note: The range shown by the box is called the “Inter-Quartile Range” or IQR.
This is a robust measure of spread. It is insensitive to outliers since it is based purely on the rank of the values.