## Slide 1: Physical Hydrology & Hydroclimatology (Multiscale Hydrology)
A science dealing with the properties, distribution and circulation of water.
R. Balaji
balajir@colorado.edu
CVEN5333 http://civil.colorado.edu/~balajir/CVEN5333
Includes slides from Prof. Mike Gooseff

## Slide 2: Lectures Week 4
Solar Radiation
  Basics
Terrestrial Radiation
  Net Incoming/Outgoing
Global Energy Balance
  Simple (Surface)
  One layer (Surface + Atmos)
  Two layer
Solar Radiation at a point on Earth’s surface
  Physical Climatology, Hartman (Chapter 2)
  Physical Hydrology, Dingman (Chapter 2, Appendix D)
  Terrestrial Hydrometeorology, Shuttleworth, (Chapter 5)
  Hydrology, Bras (Chapter 2)

## Slide 3: Basics of Energy Balance in Watersheds - Internal Energy
Sensible Heat:
Latent Heat:
Internal energy of a body that is proportional to its temperature and it’s a f(cp), specific heat:
deu = cp dT
Amount of internal energy required to change phase; melting is ‘fusion’; liquid  gas is ‘vaporization’; solid  gas is ‘sublimation’
lv = 2.501 x 106 – 2360*T(J/kg)
where T is the body temperature in ºC
Notes: Sensible Heat: internal energy of a body that is proportional to its temperature, and is a function of Cp, specific heat
FILL IN EQ 2.7.5
Latent Heat: the amount of internal energy required to change phase; melting is ‘fusion’, ‘vaporization’ is liquid to gas, and ‘sublimation’ is solid to gas.
FILLIN EQ 2.7.6

## Slide 4: Basics of Energy Balance in Watersheds - Internal Energy

## Slide 5: Laws of Radiant Energy
Radiation is a form of energy carried by (or photons) that travel at the speed of light (c, 3.0x108 m/s):
Where, l is wavelength (m), v is frequency (s-1 or Hz)
can be characterized by either (the length of a single period of the wave) or (the number of periods of the wave passing a given point per unit time).
electromagnetic waves (EM)
lv = c
wavelength
frequency
Notes: Radiation is a form of energy carried by electromagnetic (EM) waves (or photons) that travel at the speed of light (c, 3.0x108 m/s):
lv = c
Where, l is wavelength (m), v is frequency (s-1 or Hz)
can be characterized by either wavelength (the length of a single period of the wave) or frequency (the number of periods of the wave passing a given point per unit time).

## Slide 6: Basics of Radiation – it’s mostly invisible…
We primarily care about ultraviolet (nanometer scale) to microwave (centimeter scale) wavelengths, which contain non-negligible amounts of energy.

## Slide 7: Radiation Basics - Stefan-Boltzman Eqn
Bulk radiative energy flux from a body, can be calculated by integrating the spectral radiant emittance , i.e. for a blackbody:
which, yields the so-called Stefan-Boltzmann equation:
σ ≡ Stefan-Boltzmann constant = 5.67 x10−8 W m−2 K−4
across all wavelengths
Notes: Bulk radiative energy flux from a body, can be calculated by integrating the spectral radiant emittance across all wavelengths, i.e. for a blackbody:
FILL IN EQN
which, yields the so-called Stefan-Boltzmann equation:
FILL IN EQN
σ ≡ Stefan-Boltzmann constant = 5.67 x10−8 W m−2 K−4

## Slide 8: Radiative Properties of Media– Radiative Flux
Emitted radiative flux from a particular body depends on its physical
Land surface type largely dictates the broadband emissivity, ranging
temperature and e (emissivity)
0.9 – 1.0
Notes: Emitted radiative flux from a particular body depends on its physical temperature and its emissivity
Land surface type largely dictates the broadband emissivity, ranging 0.9-1.0

## Slide 9: Example – Remotely Sensed emissivity from Egypt/Israel
Tang et al., 2009 Optical Express
Notes: Bo-Hui Tang, Zhao-Liang Li, Yuyun Bi, "Estimation of land surface directional emissivity in mid-infrared channel around 4.0 μm from MODIS data," Opt. Express 17, 3173-3182 (2009); http://www.opticsinfobase.org/oe/abstract.cfm?uri=oe-17-5-3173

## Slide 10: Radiative Properties of Media– Radiative Flux of the Atmosphere
The broadband emissivity of the atmosphere strongly depends on the concentration of , i.e. conceptually
Gas concentrations can vary in time and space; so,
The most variable radiatively active gas is ; broadband emissivity of the atmosphere depends greatly on concentration
radiatively active gases
e also varies in time and space
water
vapor
Notes: The broadband emissivity of the atmosphere strongly depends on the concentration of radiatively active gases, i.e. conceptually
FILL IN EQN
Gas concentrations can vary in time and space; so, emissivity varies also.
The most variable radiatively active gas is water vapor; broadband emissivity of the atmosphere depends greatly on water vapor concentration

## Slide 11: Radiative Properties of Media – radiative properties
Additional radiative properties of a media:
Transmissivity (t) the fraction of incident radiation that gets through a media
Absorptivity (a) - the fraction of incident radiation that gets by the media
Reflectivity (r) - the fraction of incident radiation that is
Note:
transmitted
a
absorbed
scattered in all directions
tl + al + rl = 1
Notes: Additional radiative properties of a media:
Transmissivity (t) the fraction of incident radiation that gets transmitted through a media
Absorptivity (a) - the fraction of incident radiation that gets absorbed by the media
Reflectivity (r) - the fraction of incident radiation that is scattered in all directions
Note: FILL IN EQN

## Slide 12: Radiative Properties of Media – atmospheric energy balances
In the atmosphere, scattering in the LW spectrum is << in the clear sky atmosphere than transmissivity and absorptivity, such that
The land surface is essentially opaque to both SW and LW radiation (i.e. the transmissivity is small) and similar to the atmosphere, LW reflectivity is small:
longwave
Notes: In the atmosphere, scattering in the LW spectrum is << in the clear sky atmosphere than transmissivity and absorptivity, such that
FILL IN EQN
The land surface is essentially opaque to both SW and LW radiation (i.e. the transmissivity is small) and similar to the atmosphere, LW reflectivity is small:
FILL IN EQN
And a is surface albedo

## Slide 13: The Atmosphere Composition
theozonehole.com

## Slide 14: Composition
The majority of the atmosphere is made up of
N: 78%
O: 21%
Notes: NITROGEN, then OXYGEN…

## Slide 15: Composition
A radiatively active gas is one whose molecular structure is such that it absorbs and emits radiative energy
AKA: “Greenhouse Gases (GHG)”
Examples: CO2, CH4, N2O, O3, H2O
Notes: A radiatively active gas is one whose molecular structure is such that it absorbs (and emits) radiative energy
AKA: greenhouse gases
Examples: CO2, CH4, H2O, O3, N2O

## Slide 16: Can humans alter atmospheric composition and therefore climate?
Hypothesis of anthropogenic climate change stems from 2 facts:
Humans have added a significant amount of carbon dioxide (CO2) to the atmosphere This has largely occurred since the industrial revolution, when we began converting carbon-based fuels to energy with the bi-product of CO2 from the combustion of the fuel. (see next slide)
Notes: Hypothesis of anthropogenic climate change stems from 2 facts:
humans have added a significant amount of carbon dioxide (CO2) to the atmosphere This has largely occurred since the industrial revolution, when we began converting carbon-based fuels to energy with the bi-product of CO2 from the combustion of the fuel. (see next slide)

## Slide 17
https://www.esrl.noaa.gov/gmd/ccgg/trends/full.html

## Slide 18: Can humans alter atmospheric composition?
Secondly, CO2 is a greenhouse gas, it is a strong radiatively active gas. Thus, expectation is:
Notes: Secondly, CO2 is a greenhouse gas, it is a strong radiatively active gas. The expectation is:

## Slide 19: Vertical Profiles of the Atmosphere
Typical temperature profile is used to define different layers of the atmosphere
The lowest layer of the atmosphere is the troposphere and is approximately 10 km in depth. This is where most weather happens and where most of the
The temperature in the troposphere is reasonably linear (decreasing with height), i.e.:
where, T0 is surface temperature, G is lapse rate, and z is altitude
Notes: Typical temperature profile is used to define different layers of the atmosphere
The lowest layer of the atmosphere is the troposphere and is approximately 10 km in depth. This is where most weather happens and where most of the water vapor exists.
The temperature in the troposphere is reasonably linear (decreasing with height), i.e.:
FILL IN EQN

## Slide 20
The lapse rate in the troposphere is ~ 6.5 K/km
Surface temperature is ~290 K
Notes: http://www.theozonehole.com/atmosphere.htm

## Slide 21: Vertical Profiles of the Atmosphere - Pressure
Pressure and density profiles are tightly coupled via the hydrostatic equation
where density (r) depends on pressure, temperature, and vapor pressure via the Ideal Gas Law
How does p change as z increases?
i.e., linear, and approximate near earth surface
Pressure decreases!
Notes: Pressure and density profiles are tightly coupled via the hydrostatic equation
FILL IN EQN
Where density depends on pressure, temperature, and vapor pressure via the Ideal Gas Law
How does p change as z increases?
It decreases, right?

## Slide 22: Global Energy Budget is Driven by Radiation…

## Slide 23: Global Energy Budget is Driven by Radiation…
Does it all balance? Recall, we expect that we should neither create nor destroy energy. Take the incoming solar radiation – 341 W/m2
  What are its fates?
  Do these fates add up to the total incoming radiation?
  Absorbed by atmosphere (78 W/m2)
  Absorbed by surface (161 W/m2)
  Reflected by surface (23 W/m2)
  Reflected by atmosphere (79 W/m2)
Notes: 4 Fates of Incoming Solar Radiation (341 W/m2):
Absorbed by atmosphere (78 W/m2)
Absorbed by Surface (161 W/m2)
Reflected by Surface (23 W/m2)
Reflected by Clouds and Atmosphere (79 W/m2) And… 78 + 161 + 23 + 79 = 341 --> YES!!!!

## Slide 24: Global Energy Budget is Driven by Radiation - Shortwave vs Longwave Radiation
Temperature plays the key role in the intensity and distribution of emitted radiative energy from a given body
Two sources of radiative energy in hydrology:
  Solar Radiation (5800K)
  Terrestrial Radiation (250-300 K) (emitted by earth surface)
Notes: Temperature plays the key role in the intensity and distribution of emitted radiative energy from a given body
Two sources of radiative energy in hydrology:
  solar radiative fluxes (emitted by the sun; 5800K)
  terrestrial radiative fluxes (emitted by the Earth’s surface and atmosphere; 250-300 K).

## Slide 25: Shortwave vs. Longwave Radiation – 2 sources have different characteristics

## Slide 28: Shortwave vs. Longwave Radiation – components of the spectrum
Solar irradiance distribution covers three primary parts of the EM spectrum:
  UV (ultraviolet), ~the left tail of the distribution
  Visible, ~peak region of distribution
  NIR (near infrared), the right tail of the distribution
Terrestrial spectrum covers two different parts of the EM spectrum:
  IR, infrared; thermal and far IR
  microwave (>50 um)
Notes: Solar irradiance distribution covers three primary parts of the EM spectrum:
  Ultraviolet (in the left tail),
  Visible (around the peak), and
  Near-infrared (on the right side of the distribution).
The terrestrial spectrum covers two different parts:
  Infrared (thermal infrared and far infrared)
  Microwave (in the tail of the distribution beyond 50 microns).

## Slide 29: Shortwave vs. Longwave Radiation – longwave characteristics
Peak occurs in the thermal infrared ( 12um )
Thus “night-vision” goggles are tuned to be sensitive to the thermal IR wavelengths
Notes: Peak occurs in the thermal infrared ( ~12 um)
This “night-vision” goggles are tuned to be sensitive to the thermal infrared region.
IMAGES ARE FROM A THERMAL IR CAMERA (FLIR)

## Slide 30: Incoming Radiation hits the Earth differently at different locations…

## Slide 31: Of course this varies as the earth’s tilt drives seasons…

## Slide 32
Holocene Climatic Optimum
The Holocene Climatic Optimum
- period of warmer temperatures
due to greater insolation
(+ ~40 W m-2 = +8%)
magnitude of warming compares
well to projected green-house
gas warming by GCMs
Notes: The earths orbit around the Sun is elliptical and asymmetric in that at one pole (perihelion) we are slightly closer to the Sun than the other (aphelion). Our Earth is tilted at 23.5°, which produces seasonality in our annual cycle. Currently, northern hemisphere summer, when the northern hemisphere is facing the Sun, occurs at aphelion. Precession is a slow (~ 22,000 year) change in the orientation of the 23.5° tilt. So, about 11,000 years ago, Earth was tilted the opposite way, which resulted in northern hemisphere summer at perihelion, and thus, slightly greater insolation during summer than present day and a warmer northern hemisphere.
This time period is sometimes thought of as an analog to a warmer climate, i.e. future climate.
There are caveats, however. The warming during this time was concentrated to northern hemisphere summers only, whereas warming due to anthropogenic causes is global and year-round. The idea, however, is that this period along with only a handful of others in our recent past provides an example to look at the response of the Indian summer monsoon to warming, albeit slightly different warming.

## Slide 33: Latitudinal Energy Transfer is driven by energy and pressure gradients
At the global scale, this lateral transfer sets up several
How? Why?
zones of circulation
Notes: At the global scale, this lateral transfer sets up several zones of circulation

## Slide 34: The difference in radiation from equator to poles  heat transport
The distribution across the earth is
This unevenness drives a heat gradient that causes lateral transport
uneven
Notes: The distribution across the earth is uneven
This unevenness drives heat gradients that cause lateral transport…
What is seen is a relatively symmetric pattern around the equator, with a surplus of energy being input to the system in the tropics (i.e. between latitudes of +/- 30¡) and a deficit of energy from midlatitudes to the poles. In other words, the net radiation is positive near the equator and negative near the poles. This imbalance is a result of most of the solar input occurring near the equator and radiative cooling occurring at the poles.

## Slide 35: The difference in radiation from equator to poles  heat transport
For earth to be in overall equilibrium, there must be net transport of heat pole-ward from the equator
Warm tropical air must be moved poleward & cool polar air must be moved equator-ward
Notes: For earth to be in overall equilibrium, there must be net transport of heat pole-ward from the equator.
Warm tropical air must be moved pole-ward & cool polar air must be moved equator-ward
FIGURE 4.3 Inferred total latitudinal heat transport resulting from global net radiation distribution along with estimated contribution
by the atmosphere and ocean circulation. PW = 1015 W

## Slide 36
Terrestrial Solar Radiation
http://eesc.columbia.edu/courses/ees/climate/lectures/radiation/what_is_e.html

## Slide 37: Useful Resources
http://www.ucar.edu/learn/
http://eesc.columbia.edu/courses/ees/climate/lectures/radiation/what_is_e.html
http://www.mesoscale.iastate.edu/agron206/animations/10_AtmoEbal.html

## Slide 41
W/m2
Year AD
Total Solar Irradiance (W/m2) reconstructed data
Slide from Simon Wang
Source: Delaygue and Bard (2010)

## Slide 47: Solar Radiation Receipt at a point on Earth (Shortwave)
Solar Output
Distance from the Sun
Angle of solar incidence
  Latitude (phi)
  Time of day
  Seasons – declination (delta)
  Length of day time
  Hour angle (tau or omega)
  Solar Position (alpha)
Atmospheric properties

## Slide 50
From Dingman, 1994
Day Angle
ro
r
Eo=(ro/r)2 Eqn. D-4
 Eqn. D-5
(D-3)

## Slide 51
 Eqn. D-5
Zenith angle  Eqn. D-6
Latitude 
Sunrise Thr Eqn E-5a
Sunset Ths Eqn E-5b
Horizontal plane radiation
Instantaneous kET' Eqn D-2
Daily total KET' Eqn D-9

## Slide 52
Equivalent plane at latitude eq
Latitude 
Slope Sunrise Tsr Eqn D-26a
Slope Sunset Tss Eqn D-26b
Equivalent sloping plane radiation
Daily total KET Eqn D-27
Sloping surface
angle 
eq

## Slide 53
Solar Insolation

## Slide 55: Clear sky attenuation of solar radiation passing through atmosphere
K'ET
K'dir =  K'ET
0.5 sK'ET
0.5 sK'ET
and s - appendix D
  optical air mass
  precipitable water
  dust
  backscattering
  Optical air mass – Dingman Fig D-5
0.5 a sK'g

## Slide 56: Shortwave Radiation at a Point
Extraterrestrial radiation So is a function of date (season) time, latitude, slope and aspect.
St at surface is So modified by absorption by atmospheric gases, particularly water vapor, through scattering by air molecules and dust particles, and additionally by clouds when they are present.
Net shortwave takes into account losses after reflection (albedo) Sn = St(1-)
as – fraction of So on overcast days (n=0)
as+bs – fraction of So on clear days
n/N – (1 - cloudiness fraction)
n – bright sunshine hours per day
N – total day length
So– extraterrestrial radiation [MJ m-2 day-1]
[MJ m-2 day-1 or W m-2]
Refer to Shuttleworth 1993

## Slide 58
Albedo

## Slide 61: Longwave Radiation
Atmosphere and ground emit black body radiation
Surface usually warmer than atmosphere -> net loss of energy as thermal radiation from the ground.
 - adjustment for cloud cover
’ – net emmissivity between the atmosphere and the ground
 - Stefan-Boltzmann constant
4.903 x 10-9 [MJ m-2 K-4 day-1]
T – mean air temperature [oC]
ed – vapor pressure [kPa]
ae = 0.34
be = -0.14
Rn = Sn + Ln
Net Radiation
Refer to Shuttleworth 1993 for details

## Slide 63: Two layer atmosphere energy balance
W
Refer to Box 3-2 for definitions of quantities and numerical estimates of parameters