## Slide 1: Physical Hydrology & Hydroclimatology (Multiscale Hydrology)
A science dealing with the properties, distribution and circulation of water.
R. Balaji
balajir@colorado.edu
CVEN5333 http://civil.colorado.edu/~balajir/CVEN5333
Includes slides from Prof. Mike Gooseff

## Slide 2: Lectures Week – 5 - 6
Water Vapor in Atmosphere
  Basics
Vertical Gradients in Atmosphere
  Temperature
  Pressure
Atmospheric Stability
Precipitation
  Formation
  Areal estimation
  Physical Hydrology, Dingman (Chapter 3, Appendix E)
  Terrestrial Hydrometeorology, Shuttleworth, (Chapter 2,3)
  Hydrology, Bras (Chapter 3)

## Slide 12: Thermodynamics of Cloud Formation – Parcel Theory
Several different thermodynamic mechanisms for cooling an air parcel:
  - radiative cooling - cooling via conduction
However the most efficient mechanism for cooling air is so called adiabatic cooling as a result of vertical uplift
Notes: Several different thermodynamic mechanisms for cooling an air parcel:
  radiative cooling,
  cooling via conduction
However the most efficient mechanism for cooling air is so-called adiabatic cooling as a result of vertical uplift.

## Slide 16: Thermodynamics of Cloud Formation – Parcel Theory
Requirement for cloud formation: condensation mechanism whereby water vapor molecules are converted to liquid or ice
We will use “parcel theory” - a conceptual representation - to “follow” parcels of air as they move through the atmosphere
  Specific humidity of an air parcel (q) is conserved (i.e., q is constant) as a parcel moves,
  Given this fact, vapor will be carried around by a parcel right up until the parcel becomes saturated
Notes: Requirement for cloud formation: condensation mechanism whereby water vapor molecules are converted to liquid or ice.
We will use “parcel theory” - a conceptual representation - to “follow” parcels of air as they move through the atmosphere
  Specific humidity of an air parcel (q) is conserved (i.e. q = constant) as a parcel moves, if no condensation.
  Given this fact, vapor will be carried around by a parcel right up until the parcel becomes saturated

## Slide 17
http://www.ux1.eiu.edu/~cfjps/1400/stability.html
Notes: Moist adiabatic lapse rate = 0.6°C per 100 m. Remember -- This is an average lapse rate. The actual one varies!!! If the moisture falls out of the parcel as rain, the process is not reversible.
Reversible only if no moisture has been removed!
If we (somehow) lift the parcel: It will cool at the dry adiabatic lapse rate. The parcel will find itself cooler than the environmental (sounding) temperature. At the same pressure, a cooler parcel will be more dense than the environment. Being denser, the parcel will descend back to where it came from. STABLE!

## Slide 18
http://www.ux1.eiu.edu/~cfjps/1400/stability.html
Notes: If we (somehow) lift the parcel: It will cool at the dry adiabatic lapse rate. The parcel will find itself warmer than the environmental (sounding) temperature. At the same pressure, a warmer parcel will be less dense than the environment. Being less dense, the parcel will ascend and move farther from where it came from. UNSTABLE!

## Slide 19
http://www.ux1.eiu.edu/~cfjps/1400/stability.html
Notes: If we (somehow) lift the parcel: It will cool at the dry adiabatic lapse rate. The parcel will find itself at the same temperature than the environmental (sounding) temperature. Being the same density, the parcel will not be accelerated in any direction and will remain where it is. NEUTRAL STABILITY! -- Dry Neutral, or Conditional Instability

## Slide 20: Hydrostatic Atmosphere
A
F
F+dF
dz
dM = Adz
dF=dM g
dP = dF/A = gdz

## Slide 21: Physical properties of moisture in the air
Dingman, Chapter 3 (Section 3.1 and 3.2)

## Slide 22: How much water can the air hold?
Td
ea
Ta
es(Ta)
Saturation vapor pressure es(t). The maximum vapor pressure that is thermodynamically stable.
Relative humidity. Vapor pressure relative to saturation vapor pressure. (usually expressed as %)
Dew point. Td. The temperature to which a parcel of air has to be cooled at constant (vapor) pressure to reach saturation
:
See Goff-Gratch (1946) for more precise equation or Lowe (1977) for polynomials for efficient evaluation
mb, for T in oC

## Slide 23: Virtual Temperature
This suggests
Also
with
The temperature that dry air should have in order to have the same density as moist air with given q, T, p (Brutsaert, 2005, p25)

## Slide 24: Vertical Profiles of the Atmosphere - Moisture
There is no standard water vapor profile
In general, higher latitudes have less water vapor since they are colder.
The lower humidity is largely controlled by the saturated specific humidity
Notes: There is no standard water vapor profile
In general, higher latitudes have less vapor since they are colder.
The lower humidity is largely controlled by the saturated specific humidity

## Slide 25: Vertical Profiles of the Atmosphere - Moisture
Specific humidity drops off quickly with height
q ~ 0 at the top of the troposphere
Why does q decrease with z?
Notes: Specific humidity quickly drops off with height
q~0 at the top of the troposphere
Why does q decrease with z?

## Slide 29: Vertical Profiles of the Atmosphere – Total Precipitable Water
The bulk amount of vapor in the atmospheric column; amount (mass) of water that would be yielded (per unit area) if all vapor were condensed out of the column of air.
This is calculated as the integral of the water vapor mass with elevation:
Units: kg H2O/m2
Notes: The bulk amount of vapor in the atmospheric column; amount (mass) of water that would be yielded (per unit area) if all vapor were condensed out of that column of air.
This is calculated as the integral of the water vapor mass with elevation:
FILL IN EQN
Units: kg H2O/m2

## Slide 30: Vertical Profiles of the Atmosphere – Total Precipitable Water
However, it’s difficult to measure vapor density.
So, we can substitute in specific humidity and hydrostatic pressure terms to give this integral instead:

## Slide 31: Vertical Profiles of the Atmosphere – Total Precipitable Water
Of course, if clouds exist, must consider ice and liquid as well
We can convert the Wp values to a depth of water by normalizing to the density of water:
Wp/r dimensional analysis:
Typical values are 1-5 cm
Notes: Of course, if clouds exist, must consider ice and liquid as well
We can convert the Wp values to a depth of water by normalizing to the density of water:
Wp/r, dimensional analysis: [kg/m2]
[kg/m3]
Typical values are 1-5 cm

## Slide 32
Source of moisture
Lifting mechanism (orographic or heating)
Phase change from vapor to water - Energy
Small nuclei or dust for droplet formation
Droplets must grow as they fall to earth
Formation of Precipitation
From Bedient

## Slide 33
Lifting Mechanisms
From Bedient

## Slide 35
Ralph, F. M., P. J. Neiman, G. A. Wick, S. I. Gutman, M. D. Dettinger, D. R. Cayan, and A. B. White (2006), Flooding on California's Russian River: Role of atmospheric rivers, Geophys. Res. Lett., 33, L13801, doi:10.1029/2006GL026689.

## Slide 37
ATMOSPHERIC STABILITY
Temp
Altitude
Dry Adiabatic Lapse Rate (10 0C/km)
Moist Adiabatic Lapse Rate (6 0C/km). Lower due to release of latent heat of condensation from moist air
Environmental Lapse Rate
Modified from Bedient

## Slide 38: Atmospheric Stability
Ambient lapse rate < adiabatic lapse rate of lifted parcel
Ambient lapse rate > adiabatic lapse rate of lifted parcel
From Brutsaert, 2005
Stable
Unstable

## Slide 39: Conditional instability of partially saturated atmosphere
From Brutsaert, 2005
Gamma > Gamma(s) – Unstable
Gamma < Gamma(s) – Stable
Gamma = Gama(s) - Neutral

## Slide 44: Meteorology of Precipitation
Precipitation requires
  Cooling to below dew point
  Condensation nuclei
  Drop growth
Primary cooling mechanism is uplift
Precipitation amounts frequently larger than precipitable water
  Requirement for supply of water vapor
  Convergence and uplift
Weather systems
  Extratropical cyclone/frontal system
  Intertropical convergence zone
  Hurricane
  Convection (Thunderstorms) following surface heating.
  Orography

## Slide 45
Major Thunderstorm
From Bedient

## Slide 46
From Dingman,1994

## Slide 47
From http://www.physicalgeography.net/fundamentals/7u.html
Hurricane Floyd, September 15, 1999
Graphical model showing a vertical cross-section of the air circulation, clouds, and precipitation associated with a hurricane.

## Slide 48
Hurricane Katrina in the Gulf - 8/29/2005
Katrina 08-28-2005 at 17:00 UTC
From Bedient

## Slide 49
From Bras, 1990

## Slide 50
From Brutsaert, 2005

## Slide 51
Measuring Rainfall - Tipping
Bucket
Recording gage
Collector and Funnel
Bucket and Recorder
Accurate to .01 ft
Telemetry- computer
From Bedient

## Slide 52: Precipitation Measurement – Observe and Report
So, we need records to evaluate to determine design criteria for civil infrastructure
We can measure precipitation in 2 ways: - Point measurements at a gauge - Across an area using radar
Notes: So, we need records to evaluate to determine design criteria for civil infrastructure
We can measure precipitation in 2 ways:
  Point measurements at a gauge
  Across an area using radar

## Slide 53: Precipitation Measurement – characterization
We characterize precipitation by:
  Amount – the total precipitation for an event (storm) or length of time (day, month, etc.), reported as a depth of water (mm, in)
  Duration – temporal length of an event, reported in units of time (hr, d)
  Intensity – rate of precipitation input (Amount per time), reported as depth / time (mm/d)
Notes:   Amount – the total precipitation for an event (storm) or length of time (day, month, etc.), reported as a depth of water (mm, in)
  Duration – temporal length of an event, reported in units of time (hr, d)
  Intensity – rate of precipitation input (Amount per time), reported as depth / time (mm/d)

## Slide 54: Precipitation Measurement – Precipitation Variability
Precipitation is in general and variable
Fig. 2, Black, 1997
Notes: Precipitation is in general spatially and temporally variable

## Slide 55: Precipitation Measurement – Interpretation of Data
Time distributions
  Records of precipitation displayed as
  Range of timescales of interest
Area distributions
  Using point data to find
  Isohyetal Method
  Thiessen method
Notes: Time distributions
  Records of precipitation displayed as hyetographs
  Range of timescales of interest (hours to seasons to years to decades)
Area distributions
  Using point data to find average rainfall
  Isohyetal Method
  Thiessen method

## Slide 56: Precipitation Measurement – Data as recorded…
Hyetograph –
Hourly hyetograph for a site near Charlottesville, Virginia
Hourly precipitation is
Hornberger et al., 1998, Fig 2.2
Notes: Hyetograph – temporal record of precipitation
Hourly hyetograph for a site near Charlottesville, Virginia
Hourly precipitation is very heterogeneous, and often zero…

## Slide 57: Precipitation Measurement – Precipitation Records
Hyetographs record
Hornberger et al., 1998, Fig 2.3
In general, we want to know:
Averages
Standard Deviations
Extremes
Probabilities
Return Periods
This is
Notes: Hyetographs record something and nothing...
In general, we want to know:
Averages
Standard Deviations
Extremes
Probabilities
Return Periods
This is Frequency Analysis

## Slide 58: The Hyetograph
Graph of Rainfall Rate (in/hr) vs Time (hr) at a single gage location
Usually plotted as a bar chart of gross RF
Net Rainfall is found by subtracting infiltration
Integration of Net Rainfall over time =
  Direct RO Vol (DRO) in inches over a Watershed
From Bedient

## Slide 59
Mass Curves & Rainfall Hyetographs
From Bedient

## Slide 60: Precipitation Measurement – Statistics on Different Time Scales, Distributions
Hornberger et al., 1998, Fig 2.7

## Slide 61: Precipitation Measurement – Storm Types
Figure 2.14
Environmental Hydrology, 2002

## Slide 62: Precipitation Measurement – Spatial & Temporal Precipitation Variability
Fig. 2.5 – Hornberger et al., 1998

## Slide 63: Precipitation Measurement – Calculating Precipitation Inputs
Fig. 2.4 – Hornberger et al., 1998
We want to know how much water entered the basin in a precipitation event
General Integration Method
Isohyetal Method

## Slide 64
Connect gages with lines
Form triangles as shown
Create perpendicular bisectors of the triangles
Each polygon is formed by lines and WS boundary
Thiessen Polygons - Areal Average Rainfall from Gages
P = S (Ai*Pi) / AT
From Bedient

## Slide 65
Thiessen Method for Average Rain
Step 1
Notes: Figure 2.15

## Slide 66
Step 2
Thiessen Method for Average Rain
Notes: Figure 2.15

## Slide 67
Step 3
Thiessen Method for Average Rain
Notes: Figure 2.15

## Slide 68
Step 4
Thiessen Method for Average Rain
Notes: Figure 2.15
After summing areas and rainfall Thiessen predicts 2.08 inches, and the mean is 1.97 inches. This is because the heavier rainfall amounts in center of study area get more carry more area and weight in the calculation.

## Slide 69
Rainfall Averaging Methods
From Bedient

## Slide 70: Precipitation Measurement – gauges
  Storage gauge – collect rain and calibrated to read depth of precipitation
  Weighing-recording gauge – rain collected in a bucket is weighed and the weight is recorded periodically
Source: USA Today, Chad Palmer
Measured at a single location.
Precipitation is measured in 1 of 3 gauge types:
Notes:   Measured at a single location. Precipitation is measured in 1 of 3 gauge types:
  Storage gauge – collect rain and calibrated to read depth of precipitation
  Weighing-recording gauge – rain collected in a bucket is weighed and the weight is recorded periodically

## Slide 71: Precipitation Measurement – gauges
Tipping Bucket Gauge – small calibrated buckets on a “see-saw” when one fills, it tips and spills, then the other fills, tips and spills. The number of tips are recorded
Source: USA Today, Chad Palmer
Source: Rickly Hydrological
Notes: Tipping Bucket gauge – small calibrated buckets on a “see-saw” when one fills, it tips and spills, then the other fills, tips and spills. The number of tips are recorded

## Slide 72: Precipitation Measurement – gauges
Problems with gauges:
  Mis-readings by operator or by datalogger
  Limitations of methods
    Not accurate for small events (< 0.01 in)
    Tipping buckets often under measure large events because they cannot keep up with the intensity
    Weighing gauge becomes less sensitive as it gets full
Notes: Problems with gauges:
  Mis-readings (by operator or data logger)
  Limitations of methods
    Not accurate for small events, less than 0.01 in.
    Tipping buckets often under measure large events because they cannot keep up with the intensity
    Weighing gauge becomes less sensitive as it gets full

## Slide 73: Precipitation Measurement – Gauge Errors

## Slide 74: Precipitation Measurement – gauges
Gauge performance is affected by:
  Nearby obstacles decrease gauge ‘catch’
  Height of gauge opening affects catch
  Evaporation out of gauge
  Wind field near gauge
Notes: Gauge performance is affected by:
  Nearby obstacles decrease gauge “catch”
  Height of gauge opening affects catch
  Evaporation out of gauge
  Wind field near gauge

## Slide 75: Precipitation Measurement – Location of Gages
Gauges measure point precipitation
True precipitation unaffected by surroundings-
Clearance distance 2 times height of object
For large areas multiple gauges are needed for more accurate estimates
Notes: Gauges measure point precipitation
True precipitation unaffected by surroundings- winds, trees, buildings
Clearance distance 2 times height of object
For large areas multiple gauges are needed for more accurate estimates

## Slide 76: RADAR Rainfall Estimates
NEXRAD provides real-time data on a ~16 km2 (6 mi2) grid
Each estimate represents an average rainfall amount over the entire 4 x 4 km2 area
NEXRAD rainfall estimates compare well with point rain gage measurements (r2 ~ 0.9)
From Bedient

## Slide 78: Thermodynamics of Cloud Formation – Parcel Theory
@right, the cloud base (LCL) occurs at 3 km
The location of the cloud base depends on the initial temperature and humidity contained in the near-surface air parcel.
Notes: @right, the cloud base (LCL) occurs at 3 km
The location of the cloud base depends on the initial temperature and humidity contained in the near-surface air parcel.

## Slide 79: Cloud Microphysics
Cooling via adiabatic uplift is necessary for cloud formation, but not sufficient alone
Particulates that are often found in the atmosphere (aerosols, ash, salt, etc.), facilitate formation of hydrometeors as cloud condensation nuclei (CCN)
Notes: Cooling via adiabatic uplift is necessary for cloud formation, but not sufficient alone
Particulates that are often found in the atmosphere (aerosols, ash, salt, etc.), facilitate formation of hydrometeors as cloud condensation nuclei (CCN)

## Slide 80: Cloud Microphysics – nucleation processes
Homogeneous nucleation - process of water vapor molecules spontaneously condensing form a liquid droplet (or ice crystal)
  Possible, but rare because of the small size of water molecules (0.3nm diameter) and high surface tension of water (which increases with decreasing diameter)
Heterogeneous nucleation - CCNs (~0.2 um diameter) provide a site for water vapor molecules to condense onto
Notes: Homogeneous nucleation - process of water vapor molecules spontaneously condensing to form a liquid droplet (or ice crystal)
Possible, but rare because of the small size of water molecules (0.3 nm diameter) and high surface tension of water (which increases with decreasing diameter)
Heterogeneous nucleation - CCNs (~0.2 um diameter) provide a site for water vapor molecules to condense onto

## Slide 81: Cloud Microphysics – cloud seeding
Notes: http://www.blueplanet.nsw.edu.au/mi--water--cloud-seeding/.aspx

## Slide 82: Cloud Microphysics – hydrometeor size dictates its fate
Hydrometeor must be sufficient size (volume, mass) to:
i) achieve terminal velocities that are > updraft velocity in the cloud and
ii) survive evaporation between the cloud base and the surface.
Notes: Hydrometeor must be sufficient size to:
i) achieve terminal velocities that are > updraft velocity in the cloud and
ii) survive evaporation between the cloud base and the surface.

## Slide 83: Cloud Microphysics growing hydrometeors
In warm clouds (T>0oC, and made up of liquid water and vapor only) there are two primary growth mechanisms:
Diffusional condensation - individual water vapor molecules diffuse through the air (as a result of vapor concentration gradients) and attach to a CCN or existing droplet
  Slow process: one vapor molecule at a time
Notes: In warm clouds (T>0oC, and made up of liquid water and vapor only) there are two primary growth mechanisms:
Diffusional condensation - individual water vapor molecules diffuse through the air (as a result of vapor concentration gradients) and attach to a CCN or existing droplet.
  Slow process: one vapor molecule added at a time

## Slide 84: Cloud Microphysics growing hydrometeors
Coalescence Growth – droplets of sufficient size exist in the cloud start to fall relative to the updraft
  Bigger droplets fall faster than smaller ones, overtaking them
  Much faster process responsible for generating droplets that fall out of the cloud
Notes: Coalescence Growth – droplets of sufficient size exist in the cloud start to fall relative to the updraft.
  Bigger droplets fall faster than smaller ones, overtaking them
  Much faster process responsible for generating droplets that fall out of the cloud

## Slide 85: Cloud Microphysics – Summary of drop formation
Uplift occurs in the cloud
Saturated conditions yield condensation
Droplets form in a process of being uplifted and falling within the cloud
When drops are big enough, they fall out of the cloud
Notes: Uplift occurs in cloud
Saturated conditions yield condensation
Droplets form in a process of being uplifted and falling within the cloud
When drops are big enough, they fall out of the cloud

## Slide 86: Meteorology of Precipitation – Uplift
Uplift is required to form precipitation
4 main mechanisms that cause vertical uplift:
Large-scale Horizontal convergence
large-scale air masses of similar thermal characteristics coming together at the surface, being forced upward as a result of mass conservation
Notes: Uplift is required to form precipitation
4 main mechanisms that cause vertical uplift:
Large-scale Horizontal convergence
large-scale air masses of similar thermal characteristics coming together at the surface, being forced upward as a result of mass conservation

## Slide 87: Meteorology of Precipitation – Uplift
Large-scale Horizontal convergence – examples
the ITCZ which is the coming together of the surface branches of the Hadley cells
Notes: the InterTropical Convergence Zone which is the coming together of the surface branches of the Hadley cells
http://tnhsprgteam.blogspot.com/2011/07/what-is-intertropical-convergence-zone.html

## Slide 88: Meteorology of Precipitation – Large-scale Horizontal convergence – examples
A tropical depression is an area of relatively low atmospheric pressure
At latitudes of +/- 5-20o latitude the Coriolis force is strong enough that cyclonic flow patterns can form around low pressure centers with surface winds converging toward the low pressure center
Notes: A tropical depression is an area of relatively low atmospheric pressure.
At latitudes of +/- 5-20o latitude the Coriolis force is strong enough that cyclonic flow patterns can form around low pressure centers with surface winds converging toward the low pressure center.

## Slide 89: Meteorology of Precipitation – Uplift
2. Frontal convergence
Occurs mostly in mid-latitudes
convergence of air masses with different thermal characteristics (temperatures)
Cold air masses from high latitudes
Notes: Uplift is required to form precipitation
4 main mechanisms that cause vertical uplift:
Large-scale Horizontal convergence
large-scale air masses of similar thermal characteristics coming together at the surface, being forced upward as a result of mass conservation

## Slide 90: Meteorology of Precipitation – 2. Frontal convergence
A “front” is an interface (a strong temperature gradient) between the two converging air masses
While both air masses are generally moving, one usually overtakes the other; has a higher velocity
Fronts are labeled by the overtaking air mass
Uplift is driven by buoyancy: rwarm < rcold
Notes: A “front” is an interface (a strong temperature gradient) between the two converging air masses
While both air masses are generally moving, one usually overtakes the other; has a higher velocity
Fronts are labeled by the overtaking air mass
Uplift is driven by buoyancy: rwarm < rcold
WARM front over COLD front…

## Slide 94: An aside – Extra-Tropical Cyclones
Low pressure area that forms near the boundary between warm and cool air masses.
Warm air rises up over the cold air mass, and some of the cold air sinks and flows under the warm air mass, the cyclone "deepens" (the air pressure becomes lower) and the winds around the system increase.
Notes: Low pressure area that forms near the boundary between warm and cool air masses.
Warm air rises up over the cold air mass, and some of the cold air sinks and flows under the warm air mass, the cyclone "deepens" (the air pressure becomes lower) and the winds around the system increase.
http://www.weatherquestions.com/What_is_a_cyclone.htm

## Slide 95: Tropical Cyclones
NOT associated with fronts
Fueled by warm oceans (>27oC)
Born in easterlies, so initial movement is westward, but they end up moving poleward

## Slide 96: Tropical Cyclone in cross-section
Notes: http://apollo.lsc.vsc.edu/classes/met130/notes/chapter15/vertical_circ.html

## Slide 97: Tropical Cyclone in cross-section
Notes: http://apollo.lsc.vsc.edu/classes/met130/notes/chapter15/vertical_circ.html

## Slide 98: Meteorology of Precipitation – Uplift
3. Thermal Convection
Heated air from the surface rises in the atmosphere
Example: convective thunderstorms
Notes: 4. Thermal Convection
Heated air from the surface rises in the atmosphere
Example: convective thunderstorms
https://en.wikipedia.org/wiki/Atmospheric_convection#/media/File:Thunderstorm_formation.jpg

## Slide 99: Meteorology of Precipitation – Uplift
4. Orographic uplift
vertical uplift is the result of air masses flowing over significant relief
uplift  adiabatic cooling  condensation
AND: descent  adiabatic warming
Notes: 3. Orographic uplift
vertical uplift is the result of air masses flowing over topography of significant relief
uplift  adiabatic cooling  condensation
AND: descent  adiabatic warming
leeward side surface air will have less specific humidity (due to condensate left behind) and will be warmer

## Slide 100
Notes: https://upload.wikimedia.org/wikipedia/commons/d/d3/Average_precipitation_in_the_lower_48_states_of_the_USA.png

## Slide 101: Meteorology of Precipitation – Orographic Precipitation
West to east profile with Pacific Ocean at the west (left).
Clearly precipitation drops off after the first 4 mountain ranges.

## Slide 102: When does it snow/rain/sleet?
Notes: http://www.differencebetween.info/difference-between-snow-sleet-and-freezing-rain