## Slide 1: Physical Hydrology & Hydroclimatology (Multiscale Hydrology)
A science dealing with the properties, distribution and circulation of water.
R. Balaji
balajir@colorado.edu
CVEN5333 http://civil.colorado.edu/~balajir/CVEN5333
Includes slides from Prof. Mike Gooseff

## Slide 2: Water in Soil
Learning objectives
Be able to quantify the properties of water held in and flowing through soil (porosity, moisture content, pressure, suction, hydraulic conductivity)
References
Rainfall-Runoff Processes workbook chapter 4
Dingman Chapters 7 and 8
Chow Chapter 4

## Slide 3: Conceptual model of subsurface water
Many hydrologic processes occur here in the skin of the landscape
Precip that reaches the ground can infiltrate or move overland…

## Slide 4: Unsaturated Zone Location
The subsurface is generally composed of roots, soil, air and water
Water content of soils generally increases with depth
Notes: The subsurface is generally composed of roots, soil, air, and water
Water content of soils generally increases with depth

## Slide 5
Notes: Figure 21. Cross section through an unsaturated porous medium (from Chow et al. 1988)

## Slide 6
Figure 22. Illustrative grain-size distribution curves. The boundaries between size classes designated as clay, silt, sand and gravel are shown as vertical lines.
Uniformly graded sand
Well graded silt, sand, gravel mixture

## Slide 7
Soil texture triangle, showing the textural terms applied to soils with various fractions of sand, silt and clay. (from Dingman, 2002)
A
B

## Slide 8
Macroscopic and microscopic concepts of porous medium flow. (from Freeze and Cherry, 1979)

## Slide 9: Porous Media Characteristics – Soil Matrix Recipe
Env. Hydrol., Figure 3.3
mm
mv
mw
mt
Vm
Vw
Vv
Va
Vt

## Slide 10: Porous Media Characteristics – Porosity (h or f)
Definition: the proportion of pore space in a volume of soil
What is the range of values for porosity?
0 to 1.0
Measurement: the ratio of the bulk density to the density of soil:
Notes: WHAT IS THE RANGE OF VALUES FOR POROSITY? 0-1

## Slide 11: Porous Media Characteristics – Porosity (h or f)
T/F? Porosity is affected by the amount of water in the soil.
Porosity is affected by the arrangement of soil particles:
FALSE
Notes: Left image: porosity of top = 0.91, porosity of bottom = 0.35

## Slide 12: Groundwater Fluid Dynamics
Water moves down gradient, from high head (or potential) to low head.
Unlike common fluid dynamics examples, porous media induce a tortuous flow path
- Extremely complex flowpath geometry which cannot be specified completely
Notes: The position, size, and shape of each particle or grain in the porous media cannot be specified.
Frictionless flow is meaningless in this situation, we expect head losses to play the predominant role in mediating flow

## Slide 13: Groundwater Fluid Dynamics: simplifying the problem…
First, simplify by “straightening” the tortuous flowpath and idealizing the flowpath as a pipe of variable diameter

## Slide 14: Groundwater Fluid Dynamics: simplifying the problem…
Second, replace variable radius tubes with an equivalent set of constant radius tubes.
Our conceptual model of flow through a porous media is now flow through a bundle of small tubes of different diameters
Conceptual model is drastically oversimplified, but allows forward progress for quantifying the problem

## Slide 15: Groundwater Fluid Dynamics: simplifying the problem…
Consider a single tube of diameter D…
Narrow tube and small velocities, assume laminar conditions
We can describe the velocity and flow through the tube with Poiseulle’s Law
U – velocity
p – pressure
D – diameter
A – area
m – dynamic viscosity
Notes: Narrow tube and small velocities, assume laminar flow conditions
We can describe the velocity and flow through the tube with Poiseulle’s Law

## Slide 16: Groundwater Fluid Dynamics: from tubes to pores…
Discharge varies as the 4th power of the tube diameter
If our “tube” is analogous to pores in a complex media, then groundwater flow should be dependent of the texture and grain size of the porous media…
Recall….
Notes: Discharge varies as the 4th power of the tube diameter
If our “tube” is analogous to pores in a complex media, then GW flow should be dependent of the texture and grain size of the porous media…

## Slide 17: Groundwater Fluid Dynamics: hydraulic head
GW flow does not need to be horizontal, vertical flow components demand for some accounting of gravity
- Hydraulic head (h) [L] is the mechanical energy per unit weight at location Note: both pressure and elevation components considered
Notes: GW flow does not need to be horizontal, vertical flow components demand for some accounting of gravity
- Hydraulic head (h) [L] is the mechanical energy per unit weight at location l: both pressure and elevation components considered

## Slide 18: Groundwater Fluid Dynamics: recall fluid mechanics 101…
Bernoulli equation specifies the total fluid energy per unit weight E [L]
Kinetic
Energy
Potential
Energy
Pressure
Energy
For steady, frictionless, and incompressible flow fluid energy is conserved! Thus, E = constant along a flow path
Notes: KINETIC POTENTIAL PRESSURE
For steady, frictionless, and incompressible flow fluid energy is conserved! i.e. E = constant along a flow path

## Slide 19: Groundwater Fluid Dynamics: negligible kinetic energy in groundwaters…
Kinetic
HEAD
Potential
HEAD
Pressure
HEAD
Hydraulic head is the total mechanical energy per unit weight of water!

## Slide 20: Groundwater Fluid Dynamics: scale of observation….
Q
A
This only pertains to a single flowpath, and we have yet to explain velocities or discharge for the entire system

## Slide 21: Groundwater Fluid Dynamics: Darcy’s Experiments….
What parameters influence flow through a porous media?

## Slide 22: Groundwater Fluid Dynamics: Darcy’s Experiments….
Total discharge
Specific discharge
Rearrange…
Notes: Hydraulic conductivity K is a constant of proportionality explaining the relationship between hydraulic gradient and discahrge
dh/dl is the hydraulic gradient. The negative sign indicates that positive specific discharge (indicating direction of flow) corresponds with a negative hydraulic gradient.

## Slide 23: Groundwater Fluid Dynamics: hydraulic conductivity….
Specific discharge
BLACK High K sand
A
BLUE Low K sand
Which of these relationships is the higher K material, and which is the lower K material?
B
A is the high K material
B is the low K material
Notes: A is high K sand
B is low K sand

## Slide 24: Groundwater Fluid Dynamics: hydraulic conductivity….
K depends on the nature of both
Grainsize
(analogous to D)
K
K
Fluid viscosity
the fluid and porous material
Notes: K depends on the nature of both the fluid and porous material

## Slide 25: Groundwater Fluid Dynamics: hydraulic conductivity….
N = shape factor, d = mean grain diameter
k = intrinsic permeabiltiy
Is hydraulic conductivity temperature dependent?

## Slide 26: Groundwater Fluid Dynamics: hydraulic conductivity….

## Slide 27: Groundwater Fluid Dynamics: average linear velocity….
- This (q) is NOT the linear velocity, despite the units [L/T]
- Recall we got this by dividing the total volumetric flow rate Q by the total column area A
Q
A
… but water only flows through a fraction of the total area A

## Slide 28: Groundwater Fluid Dynamics: average linear velocity….
Q
A
Recall, porosity is the fraction of fraction of a porous material which is void space
Average linear velocity is the specific discharge normalized by the porosity

## Slide 29
Experimental apparatus for the illustration of Darcy's equation. (From Freeze and Cherry)
1
2
1
2

## Slide 30
Parallel conduit conceptual model for porous media flow.
vi
Ai
A

## Slide 31
Group learning challenge 1
Figure out how much the flow rate through a porous media will change for a 5 C change in temperature.
Does flow rate increase or decrease as temperature increases

## Slide 32: Water Viscosity at different temperatures
From http://www.engineeringtoolbox.com/water-dynamic-kinematic-viscosity-d_596.html

## Slide 33: The Unsaturated Zone
Unsaturated Zone – the region between the soil surface and water table, where pores are partially filled with water and partially filled with air.
Water in the unsaturated zone is referred to as soil moisture
Understanding hydrologic fluxes in this zone requires resolving a three phase problem

## Slide 34: The Unsaturated Zone
Soil water zone – zone directly below the soil surface where water may be discharged into the atmosphere by evaporation and transpiration.
Field capacity – the moisture condition prevailing when downward gravitational forces are in equilibrium with surface tension forces.

## Slide 35: The Unsaturated Zone
Capillary fringe – zone where the pressure is less than atmospheric but soils are saturated, overlying the water table.
** water is being held against the force of gravity
Intermediate zone – simply the zone between the soil water zone and the capillary fringe. Because something gotta be there…

## Slide 36: Forces in the unsaturated zone
Capillary forces – allow liquid to flow in narrow spaces (pores) without the assistance of, and in the opposite direction of gravity
Capillary pressure head – the negative (gage) pressure produced by capillary forces (when divided by ρg)
Gage pressure = 0

## Slide 37
Soil-water status as a function of pressure (tension). Natural soils do not have tensions exceeding about -31000 cm; in this range water is absorbed from the air. [from Dingman, 1994]

## Slide 38: The Unsaturated Zone

## Slide 39
(from Freeze and Cherry, 1979)
Negative Pressure Head. Suction vs Moisture content

## Slide 40
Pressure Head Measurement

## Slide 41
Illustration of capillary rise due to surface tension and relationship between pore size distribution and soil water retention curve.
Moisture Content 
Suction head -||

## Slide 42: Surface Tension
From http://www.engineeringtoolbox.com/water-surface-tension-d_597.html

## Slide 43: Forces in the unsaturated zone: negative gage pressure can “pull” water

## Slide 44: Forces in the unsaturated zone: hydraulic head in the vadose zone
Hydraulic head in the vadose zone is the sum of negative capillary-pressure head, ψ, and the elevation head, z.
Capillary-pressure head is a function of the volumetric moisture content θ
The specific relationship between negative capillary-pressure head (suction) and the volumetric moisture content is known as the soil’s moisture characteristic (curve)

## Slide 45: The moisture characteristic ψ=f(θ): measuring the negative head of a soil
A pressure plate measures the negative pressure head of a soil at a given moisture content

## Slide 46: The moisture characteristic ψ=f(θ): the moisture characteristic curve
saturation
Exceed critical suction and rapidly drain pore spaces

## Slide 47: Unsat’d hydraulic cond. K = f(θ) conductivity is a function of θ
Hydraulic conductivity decreases rapidly as the porous media becomes unsaturated.
  As suction is applied to soil, large pore spaces become filled with air first.
  Flow is restricted to larger pore spaces
  Recall..

## Slide 48: Unsat’d hydraulic cond. K = f(θ) conductivity is a function of θ
K varies by orders of magnitude as volumetric moisture content decreases from saturation

## Slide 49
Residual moisture content r =5%
Characteristic curve relating moisture content to pressure head (from Freeze and Cherry, 1979).

## Slide 50: Basis for Hysteresis
See http://hydrology.usu.edu/rrp/ hysteresis animation

## Slide 51
Characteristic curve relating Hydraulic Conductivity to pressure head (from Freeze and Cherry, 1979).

## Slide 52
Variation of soil suction head, ||, and hydraulic conductivity, K, with moisture content. (from Dingman, Chap 7)

## Slide 53: Equations to representing soil water characteristic functions
Brooks and Corey (1966)
van Genuchten (1980)
Clapp and Hornberger (1978)

## Slide 54
Clapp and Hornberger (1978) parameters for Soil Moisture Characteristic functions based on analysis of 1845 soils. Values in parentheses are standard deviations.
Also see Rosetta model (Update to URL in Module)
http://ars.usda.gov/Services/docs.htm?docid=8953

## Slide 55
Soil suction head, ||, for different soil textures using the Clapp and Hornberger (1978) parameterization.

## Slide 56
Hydraulic conductivity K() for different soil textures using the Clapp and Hornberger (1978) parameterization.

## Slide 57
Residual moisture content r =5%
Characteristic curve relating moisture content to pressure head (from Freeze and Cherry, 1979).

## Slide 58
Ranges of porosities, field capacities, and permanent wilting points for soils of various textures. (from Dunne and Leopold, 1978)

## Slide 59: Unsat’d Darcy’s Law: steady flow example
Water table
3m
3.5m
θ=0.15
θ=0.25
Ground surface
A
B
Determine the steady state vertical moisture flux between A and B….

## Slide 60: Unsat’d Darcy’s Law: steady flow example
Water table
3m
3.5m
θ=0.15
θ=0.25
Ground surface
Determine the steady state vertical moisture flux between A and B….
Ψ(θ=0.25) = -0.42m
Ψ(θ=0.15) = -0.45m
A
B

## Slide 61: Unsat’d Darcy’s Law: steady flow example
Water table
3m
3.5m
θ=0.15
θ=0.25
Ground surface
A
B
K(θ=0.15)
K(θ=0.25)
K(θav)
A
B
Determine the steady state vertical moisture flux between A and B….

## Slide 62: Unsat’d Darcy’s Law: steady flow example
Water table
3m
3.5m
θ=0.15
θ=0.25
Ground surface
A
B
Determine the steady state vertical moisture flux between A and B….
qz = 1.88 x 10-5 m/s from A to B

## Slide 63: Equilibrium moisture profiles
Let’s determine what the equilibrium soil moisture profile looks like in a homogeneous material above the water table, within the intermediate zone.
Note: assuming zero vertical flux conditions

## Slide 64: Equilibrium moisture profiles: how does ψ vary with z?
Assuming K > 0, we can divide through and re-arrange
If there is no flux, and K >0, then the hydraulic gradient must be zero. Under these conditions the capillary-pressure head balances the elevation head throughout the moisture profile

## Slide 65: Equilibrium moisture profiles: leveraging the moisture characteristic
Recall VWC is function of ψ…

## Slide 66: Capillary-head profiles indicate flow: measuring capillary-head
Recall the key to knowing answering this question was knowing the capillary-pressure head values at two (or more) locations. We need this to establish the magnitude and direction of the gradient
Tensiometer is an instrument used to measure the capillary-pressure head at a point (more or less).

## Slide 67: Capillary-head profiles indicate flow: measuring capillary-head
Water is moved from a tube into the surrounding soil through a porous cup. Changes in the amount of water in the tube, correspond to a change in internal pressure equal to the suction force being applied by the surrounding soil.
The pressure gage measures the capillary-pressure head relative to zero, (zero being atmospheric pressure)

## Slide 68: Capillary-head profiles indicate flow: measuring capillary-head @ 2 locs
Water table
zB
Ground surface
zA

## Slide 69: Capillary-head profiles indicate flow: measuring capillary-head @ 1 loc
Water table
Ground surface
zA
If we measure capillary-pressure head at a single location, can we infer flow directions and magnitudes?

## Slide 70: Capillary-head profiles indicate flow: measuring capillary-head @ 1 loc
Recall that under no-flow conditions the capillary-pressure head was perfectly balanced by the elevation head. No gradient – no flux
Region A – capillary-pressure head is more negative than the elevation head is positive. Pressure > gravity, so flow is upwards
Region B – capillary-pressure head is less negative than the elevation head is positive. Pressure < gravity, so flow is downwards

## Slide 71: Problem 17 example

## Slide 72
Group learning challenge 1
Figure out how much the flow rate through a porous media will change for a 5 C change in temperature.
Does flow rate increase or decrease as temperature increases